## Slide 1
GRAINS Enabling High-Performance and Low-Cost
Graph-Based Genome Analysis
via Storage-Aware Algorithm-Architecture Co-Design
Mohammad Sadrosadati Jisung Park Onur Mutlu
Nika Mansouri Ghiasi Harun Mustafa Talu Güloglu Rakesh Nadig
Konstantina Koliogeorgi Susana Rebolledo Ruiz Marc Rautmann Furkan Eris

## Slide 2: Applications of Genome Analysis
Precision Medicine
Outbreak Prevention and Management
Agriculture
Scientific Discovery
& Many More…
Notes: Genome analysis plays key roles in many applications
Related to health
Life sciences
And beyond

## Slide 3: DNA Under Electron Microscope
human chromosome #12
from HeLa cell
Notes: To get the organisms' genomic information encoded in their nucleotide sequences, such as DNA, into a digital format for analysis…

## Slide 4: High-Throughput Sequencers
… and more! All produce data with different properties.
Illumina MiSeq
Pacific Biosciences RS II
Illumina NovaSeq 6000
Oxford
Nanopore GridION
Pacific
Biosciences
Sequel II
Oxford
Nanopore
PromethION
Oxford Nanopore MinION
Notes: We rely on high-throughput sequencers

## Slide 5: High-Throughput Sequencers
… and more! All produce data with different properties.
Illumina MiSeq
Oxford Nanopore MinION
Pacific Biosciences RS II
Illumina NovaSeq 6000
Oxford
Nanopore SmidgION
Pacific
Biosciences
Sequel II
Oxford
Nanopore
PromethION
Sequencing technologies
extract smaller fragments of the original DNA sequence, known as reads
AAGCTTCCATGG
AAATGGGCTTTC
GCCCAAATGGTT
GCTTCCAGAATG
Notes: Sequencing technologies
extract smaller fragments of the original DNA sequence, known as reads

## Slide 6: Genome Analysis
Read Set
AAGCTTCCATGG
AAATGGGCTTTC
GCCCAAATGGTT
GCTTCCAGAATG
Reference Genome
Large-Scale Databases (e.g., containing reference genomes
from many species
or previously sequenced samples)
Determine species or genomic features present in the sample
Find differences from genomes in the reference genome or database
Notes: A set of reads sequenced from an organism, called a read set
Then goes through genome analysis
Which involves looking up the reads
In a reference genome or
In Large-Scale Databases (e.g., containing reference genomes from many species or previously sequenced samples) TO
Determine species or genomic features present in the sample
Find differences from genomes in the reference genome or database

## Slide 7: Large-Scale Genome Graphs
Powerful and efficient representation of genomic data
✓
Great expressive power
Compact representation
✓
Input Sequences
GTGG
TGGA
TATG
GTGGATTATGACGAGGCTA
ATGA
TGAC
GACG
ACGA
CGAG
…
…
GTGG
TGGA
GTGGATTATGCCGAGGCTA
TATG
…
…
ATGC
TGCC
GCCG
CCGA
CGAG
GTGG
TGGA
TATG
GTGGATTATGTCGAGGCTA
ATGT
TGTC
GTCG
TCGA
CGAG
…
…
Graph Representation
GTGGATTATG
ATGACGA
ATGCCGA
ATGTCGA
CGAGGCTA
GTGG
TGGA
TATG
GTGGATTATGACGAGGCTA
ATGA
TGAC
GACG
ACGA
CGAG
…
…
GTGG
TGGA
GTGGATTATGCCGAGGCTA
TATG
…
…
ATGC
TGCC
GCCG
CCGA
CGAG
GTGG
TGGA
TATG
GTGGATTATGTCGAGGCTA
ATGT
TGTC
GTCG
TCGA
CGAG
…
…
Notes: Unlike traditional models, which represent genomic databases as a collection of disjoint, linear sequences, sequences in a graph are represented by graph walks
And that leads to a powerful and efficient representation of genomic data due to great expressive power of graph topology and
its compact representation

## Slide 8: Large-Scale Genome Graphs
Critical for enabling massive, population-scale analyses
https://sangerinstitute.blog/2023/05/10/a-representative-reference-genome/
Notes: Which are Critical for enabling massive, population-scale analyses

## Slide 9: Data Movement Overheads
Data movement overhead
Data Movement
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Storage
System
Notes: Due to large sizes of genome graph databases,
Graph-based genome analysis incurs large data movement overheads from the storage system

## Slide 10: Storage-Centric Computing
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Storage
System
Notes: While storage-centric computing,
Which refers to processing data inside the storage system
Where it originally resides
Can be a fundamental approach to address this data movement overhead

## Slide 11: Challenges
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Storage
System
Graph-based sequence analysis tools cannot run in storage due to SSD limitations
Dependent and random accesses to the sequence graph
Different properties from conventional, non-genome graphs
Notes: None of the Graph-based sequence analysis tools can run in storage due to SSD limits
And this challenge are exacerbated due to Dependent and random accesses to the sequence graph
The fact that genome graphs show Different properties from conventional, non-genome graphs

## Slide 12: GRAINS
The first system for analysis with large-scale genome graphs in storage
Enabled via storage-aware algorithm-architecture co-design, based on the properties of large-scale genome graphs to
  Make the execution pipeline more storage-friendly
  Further improve performance, energy-efficiency, and cost-effectiveness via storage-centric computing
…
Flash
Cntrl.
Flash Cntrl.
Baseline
Metadata
SSD Controller
Internal DRAM
Channel#1
…
NAND Die#M
GRAINS-Enabled SSD
Host System
…
NAND Die#2
NAND Die#M
NAND Die#2
NAND Die#1
NAND Die#1
Channel#N
FTL
Cores
Notes: By addressing these challenges, we introduce GRAINS…

## Slide 13: GRAINS
The first system for analysis with large-scale genome graphs in storage
Enabled via storage-aware algorithm-architecture co-design, based on the properties of large-scale genome graphs to
  Make the execution pipeline more storage-friendly
  Further improve performance, energy-efficiency, and cost-effectiveness via storage-centric computing
…
Flash
Cntrl.
Flash Cntrl.
Baseline
Metadata
SSD Controller
Internal DRAM
Channel#1
…
NAND Die#M
GRAINS-Enabled SSD
Host System
…
NAND Die#2
NAND Die#M
NAND Die#2
NAND Die#1
NAND Die#1
Channel#N
FTL
Cores
Higher performance (by 1.5×–47.8×)
Higher cost effectiveness
Higher energy efficiency (by 3.1×–31.6x)
Notes: We show that compared to the state-of-the-art software and hardware baselines,
GRAINS significantly improves performance, energy-efficiency, and cost-effectiveness of
Graph-based genome analysis
2:45

## Slide 14: Outline
Background
Motivation and Goal
GRAINS
Evaluation
Conclusion
Notes: That was a brief overview of my talk. Let me tell you a little more about background on genome graphs

## Slide 15: Genome Graphs
Input Sequences
GTGG
TGGA
TATG
GTGGATTATGACGAGGCTA
ATGA
TGAC
GACG
ACGA
CGAG
…
…
GTGG
TGGA
GTGGATTATGCCGAGGCTA
TATG
…
…
ATGC
TGCC
GCCG
CCGA
CGAG
GTGG
TGGA
TATG
GTGGATTATGTCGAGGCTA
ATGT
TGTC
GTCG
TCGA
CGAG
…
…
GTGG
TGGA
TATG
GTGGATTATGACGAGGCTA
ATGA
TGAC
GACG
ACGA
CGAG
…
…
GTGG
TGGA
GTGGATTATGCCGAGGCTA
TATG
…
…
ATGC
TGCC
GCCG
CCGA
CGAG
GTGG
TGGA
TATG
GTGGATTATGTCGAGGCTA
ATGT
TGTC
GTCG
TCGA
CGAG
…
…
De Bruijn Graph
Compacted De Bruijn Graph
K-mer: subsequence of length k
u
v
Unitig
Notes: As mentioned before, Unlike traditional models, which represent genomic databases as a collection of disjoint, linear sequences, sequences in a graph are represented by graph walks
To efficiently represent large-scale genome graphs, de Bruijn graphs have been widely adopted due to their great scalability as graph database entries grow
Here, I am showing an example of a de Bruijn graph, where each node is a unique k-mer (i.e., a subsequence of length k) that is observed in the input, and there is a directed edge from node u to node v if the suffix of length (k − 1) of u is equal to the prefix of length (k −1) of v.
This powerful representation enables storing the graph by only storing nodes or only storing edges, and representing the other one implicitly.
Also note that Each node’s color represents its metadata (which refers to the database entry it corresponds to).
A common strategy to reduce a de Bruijn graph’s size is to instead store its corresponding compacted de Bruijn graph, where all k-mers from a maximal non-branching path (called a unitig) are merged into a single node.

## Slide 16: Graph-Based Genome Analysis
Read Set
AAGCTTCCATGG
AAATGGGCTTTC
GCCCAAATGGTT
GCTTCCAGAATG
Input Query Preparation
AAGCTTCCATGG
AAGC
AGCT
GCTT
…
…
Graph Query
Graph-Based Database
K-Mer Lookup
Read Mapping
Notes: Graph-based genome analysis involves querying reads against the graph
To this end, graph-based genome analysis tools first prepare input queries by extracting k-mers out of the reads
And query the graphs, which involves k-mer lookups and/or
Read mapping, to find exact similarities and differences between reads against sub-sequences of the graph

## Slide 17: Outline
Motivation and Goal
Background
GRAINS
Evaluation
Conclusion
Notes: Since graph-based genome analysis requires accessing large genome graph databases…

## Slide 18: Motivation
Chart: 
| SRArep (161 GB) | MetaSUB (659 GB)
No-I/O | 1 | 1
PCIe Gen5 SSD | 0.37602 | 0.10872
PCIe Gen4 SSD | 0.23154 | 0.057486
Case study of the performance of graph-based genome analysis tools
With various state-of-the-art SSD configurations
Normalized Throughput
I/O data movement causes significant performance overhead
Chart: 
| SRArep (231 GB) | MetaSUB (822 GB)
SSD-G4 | 1 | 1
SSD-G5 | 0.23398 | 0.074639
No-I/O | 0.13249 | 0.042331
Graph Database
Graph Database
Node-Centric Tool
Edge-Centric Tool
2.7x
4.3x
Overhead increases as databases grow
8.2x
17.4x
4.3x
7.5x
13.4x
23.6x
Notes: We perform a case study on the throughput of node-centric and edge-centric graph-based genome analysis tools
with various state-of-the-art SSD configurations
We observe that compared to a hypothetical configuration with zero performance overhead due to storage I/O,
I/O data movement causes significant performance overhead
And this overhead increases as databases grow

## Slide 19: I/O Overhead is Hard to Avoid
I/O overhead due to accessing large, low-reuse data is hard to avoid
Sampling techniques to shrink database sizes
Keeping all data required by graph-based genome analysis
completely and always resident in main memory
Reduce accuracy to levels unacceptable for many use cases
Energy inefficient, costly, unscalable, and unsustainable
Database sizes increase rapidly
Different analyses need different databases
[Wood+, Genome Biology’19], [Ounit+, BMC Genomics’15], [Kim+, Genome Research’16], …
Notes: I/O overhead from moving large, low-reuse data is hard to avoid
One might think it is possible to avoid this overhead by
using sampling techniques to shrink database sizes
However, this approach inevitably reduces accuracy to levels unacceptable for many use cases
Or another potential solution might seem to be
Keeping all data required by graph-based genome analysis
completely and always resident in main memory
However, this is energy inefficient, costly, unscalable, and unsustainable due to two reasons
First, the sizes of genome graph databases (which are already large) have been increasing rapidly.
Second, regardless of the sizes of individual databases, different analyses need different databases,
with information from different sets of genomes or with varying parameters.
Therefore, it is inefficient and unsustainable to maintain all data required by all possible analyses in main memory at all times

## Slide 20: Our Goal
Improve graph-based genome analysis performance
by reducing large data movement overhead
from the storage system
in a cost-effective manner and with high accuracy
Notes: Motivated by these points, Our Goal is to Improve graph-based genome analysis performance
by reducing the large data movement overhead from the storage system in a cost-effective manner

## Slide 21: Challenges of In-Storage Processing
No graph-based genome analysis tools can run in-storage due to SSD limitations
  Long access latency of NAND flash chips
  Limited DRAM capacity inside the SSD
  Limited DRAM bandwidth inside the SSD
SSD DRAM
⋯
SSD
Controller
Cores
FTL
⋯
SSD
Cntrl
Cntrl
Channel#N
Channel#1
Notes: While storage-centric computing (SCC) can be a promising direction to achieve our goal by processing data directly inside the storage device,
none of the existing approaches can be effectively implemented
as an SCC system due to limited hardware resources in the SSD such as
  Long latency of NAND flash chips
  Limited DRAM capacity inside the SSD
  And its limited bandwidth

## Slide 22: Challenges of In-Storage Processing
No graph-based genome analysis tools can run in-storage due to SSD limits
  Long latency of NAND flash chips
  Limited DRAM capacity inside the SSD
  Limited DRAM bandwidth inside the SSD
SSD DRAM
⋯
SSD
Controller
Cores
FTL
⋯
SSD
Cntrl
Cntrl
Channel#N
Channel#1
Dependent and random accesses to the sequence graph
Different properties from conventional, non-genome graphs
Notes: All these limitations are pronounced due to
Dependent and random accesses to the sequence graph
Different properties that these graphs have from conventional, non-genome graphs

## Slide 23: Outline
GRAINS
Background
Motivation and Goal
Evaluation
Conclusion
Notes: By addressing these challenges…

## Slide 24: GRAINS
The first system for analysis with large-scale genome graphs in storage
Enabled via storage-aware algorithm-architecture co-design, based on the properties of large-scale genome graphs to
  Make the execution pipeline more storage-friendly
  Further improve performance, energy-efficiency, and cost-effectiveness via storage-centric computing
…
Flash
Cntrl.
Flash Cntrl.
Baseline
Metadata
SSD Controller
Internal DRAM
Channel#1
…
NAND Die#M
GRAINS-Enabled SSD
Host System
…
NAND Die#2
NAND Die#M
NAND Die#2
NAND Die#1
NAND Die#1
Channel#N
FTL
Cores

## Slide 25: GRAINS’s Algorithm-Architecture Co-Design
…
Flash
Cntrl.
Flash Cntrl.
SSD Controller
Internal DRAM
Channel#1
…
NAND Die#M
GRAINS-Enabled SSD
Host System
…
NAND Die#2
NAND Die#M
NAND Die#2
NAND Die#1
NAND Die#1
Channel#N
Cores
New batching technique and execution flow
based on the unique features of genome graphs that reduces #random accesses
Input Query Processing
Notes: GRAINS's algorthim-architecture co-design consists of four key aspects...

## Slide 26: GRAINS’s Algorithm-Architecture Co-Design
…
Flash
Cntrl.
Flash Cntrl.
SSD Controller
Internal DRAM
Channel#1
…
NAND Die#M
GRAINS-Enabled SSD
Host System
…
NAND Die#2
NAND Die#M
NAND Die#2
NAND Die#1
NAND Die#1
Channel#N
Cores
New batching technique and execution flow
based on the unique features of genome graphs that reduces #random accesses
Input Query Processing
In-storage and In-flash processing to avoid transferring low-reused pages and bandwidth waste
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE

## Slide 27: GRAINS’s Algorithm-Architecture Co-Design
…
Flash
Cntrl.
Flash Cntrl.
GRAINS
Metadata
SSD Controller
Internal DRAM
Channel#1
…
NAND Die#M
GRAINS-Enabled SSD
Host System
…
NAND Die#2
NAND Die#M
NAND Die#2
NAND Die#1
NAND Die#1
Channel#N
GRAINS FTL
Cores
New batching technique and execution flow
based on the unique features of genome graphs that reduces #random accesses
Input Query Processing
In-storage and In-flash processing to avoid transferring low-reused pages and bandwidth waste
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
FTL and data placement based on genome graph properties, to leverage SSD’s full internal bandwidth

## Slide 28: GRAINS’s Algorithm-Architecture Co-Design
…
Flash
Cntrl.
Flash Cntrl.
GRAINS
Metadata
SSD Controller
Internal DRAM
Channel#1
…
NAND Die#M
GRAINS-Enabled SSD
Host System
…
NAND Die#2
NAND Die#M
NAND Die#2
NAND Die#1
NAND Die#1
Channel#N
GRAINS FTL
Cores
New batching technique and execution flow
based on the unique features of genome graphs that reduces #random accesses
Input Query Processing
In-storage and In-flash processing to avoid transferring low-reused pages and bandwidth waste
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
FTL and data placement based on genome graph properties, to leverage SSD’s full internal bandwidth
Lightweight scheduling technique enabled by repurposing the existing SSD structures to leverage the full parallelism of all flash dies
Lightweight Scheduler
Scheduler Tables

## Slide 29: GRAINS
Read Set
AAGCTTCCATGG
AAATGGGCTTTC
GCCCAAATGGTT
GCTTCCAGAATG
Input Query Preparation
AAGCTTCCATGG
AAGC
AGCT
GCTT
…
…
Graph Query
Graph-Based Database
K-Mer Lookup
Read Mapping
❶
❷
Notes: Now, let me give a walkthrough of GRAINS’s steps, which involves
Input query preparation an
Graph query

## Slide 30: Data Structures
Read Set
AAGCTTCCATGG
AAATGGGCTTTC
GCCCAAATGGTT
GCTTCCAGAATG
Input Query Preparation
AAGCTTCCATGG
AAGC
AGCT
GCTT
…
…
Graph Query
K-Mer Lookup
Read Mapping
❶
❷
Graph-Based Database
Notes: First, let’s take a look at data structures

## Slide 31: Data Structures
ACGTAGCTGACTATCCTGAAGTTCGATCGATGCTAGCTTCTT.GATAGCTGCGTAGTAGCTAGTCGATTTTCGAAGCTAGTCGTTGC.TAGTCGAGCCATCAGTCGACTGCCGAT.CGTAGCGACATCCTGAAAATTGACTAGTCTAGTTCGTTTAGGCCAATGCTAGCTAGTC.GATCGTAGGACTGCTA…
Strings
[SSHash, Bioinformatics’22]
Unitig
Notes: GRAINS adopts a node-centric De Bruijn Graph representation based on an fast and space-efficient associative dictionary
to compactly represent graph sequences and their associated colors
We store De Bruijn Graph’s unitigs as contiguous strings in a predetermined order,
so that a k-mer occurring in any unitig can be quickly located using a minimal perfect hash function built for the set of k-mers.
The unitigs in Strings are indexed via Sizes and Offsets.
Consider a query k-mer g. First, its minimizer (i.e., the first m-mer with the smallest hash value) is extracted
Second, with the minimizer’s minimal perfect hash value, Sizes is indexed
Third, with the Sizes values, here 7, Offsets is indexed.
Fourth, with the Offsets values, Strings is indexed and a window of a specific length in Strings is checked to
find the minimizer and check if the rest of the k-mer matches

## Slide 32: Data Structures
Query k-mer g = ACATCCTGAAAATTGA
ACGTAGCTGACTATCCTGAAGTTCGATCGATGCTAGCTTCTT.GATAGCTGCGTAGTAGCTAGTCGATTTTCGAAGCTAGTCGTTGC.TAGTCGAGCCATCAGTCGACTGCCGAT.CGTAGCGACATCCTGAAAATTGACTAGTCTAGTTCGTTTAGGCCAATGCTAGCTAGTC.GATCGTAGGACTGCTA…
29 | 172 | 20 | 50 | 329 | 0 | 246 | 118 | 9 | 364 | 105 | 30 | 319 | …
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | …
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | …
Hash
0 | 1 | 2 | 3 | 5 | 7 | 8 | 10 | 11 | 12 | 13 | 15 | 16 | …
Sizes
Offsets
Strings
[SSHash, Bioinformatics’22]
Notes: GRAINS adopts a node-centric De Bruijn Graph representation based on an fast and space-efficient associative dictionary
to compactly represent graph sequences and their associated colors
We store De Bruijn Graph’s unitigs as contiguous strings in a predetermined order,
so that a k-mer occurring in any unitig can be quickly located using a minimal perfect hash function built for the set of k-mers.
The unitigs in Strings are indexed via Sizes and Offsets.
Consider a query k-mer g. First, its minimizer (i.e., the first m-mer with the smallest hash value) is extracted
Second, with the minimizer’s minimal perfect hash value, Sizes is indexed
Third, with the Sizes values, here 7, Offsets is indexed.
Fourth, with the Offsets values, Strings is indexed and a window of a specific length in Strings is checked to
find the minimizer and check if the rest of the k-mer matches

## Slide 33: Data Structures
Query k-mer g = ACATCCTGAAAATTGA
ACGTAGCTGACTATCCTGAAGTTCGATCGATGCTAGCTTCTT.GATAGCTGCGTAGTAGCTAGTCGATTTTCGAAGCTAGTCGTTGC.TAGTCGAGCCATCAGTCGACTGCCGAT.CGTAGCGACATCCTGAAAATTGACTAGTCTAGTTCGTTTAGGCCAATGCTAGCTAGTC.GATCGTAGGACTGCTA…
29 | 172 | 20 | 50 | 329 | 0 | 246 | 118 | 9 | 364 | 105 | 30 | 319 | …
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | …
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | …
Hash
0 | 1 | 2 | 3 | 5 | 7 | 8 | 10 | 11 | 12 | 13 | 15 | 16 | …
Sizes
Offsets
Strings
[SSHash, Bioinformatics’22]
0
0
1
0
1
…
Color Bitmap
Graph Metadata for Unitigs with Color C1
Graph Metadata for Unitigs with Color C2
…
C1
C2
C3
[Fulgor, WABI’23]
Notes: For storing colors, we use an approach where we sort the unitigs in Strings based on their colors
We use a simple Color Bitmap to mark the start of each new color.
Colors are then the IDs pointing to the metadata for graph unitigs with those colors
This encoding efficiently stores repeated colors at low storage overhead

## Slide 34: Input Query Processing
Read Set
AAGCTTCCATGG
AAATGGGCTTTC
GCCCAAATGGTT
GCTTCCAGAATG
Input Query Preparation
AAGCTTCCATGG
AAGC
AGCT
GCTT
…
…
Graph Query
K-Mer Lookup
Read Mapping
❶
❷
Graph-Based Database
Notes: Now let’s go through the first step: Input Query Preparation

## Slide 35: Input Query Processing
❸ Batching
GRAINS prepares reads for efficient queries in the next step
  Performed in the host system due to large #writes
Cross-read k-mer batching
to reduce #random accesses
Genome-graph-aware query reordering to improve access patterns
ACTAGTCGT…
Read:
❶ K-mer Extraction
ACTAG
…
K-mers:
CTAGT
Hash
❷ Sizes Lookup
Sizes
Significantly smaller than other sub-structures
Batch#0
Batch#1
Batch#0
Batch#1
❹ Sorting
and Compaction
Enables efficient batching and compaction
+
Notes: In this step, GRAINS prepares reads for efficient queries in the next step
This step is performed in the host system due to large #writes
In this step, GRAINS performs:
Cross-read k-mer batching to reduce #random accesses AND
Genome-graph-aware query reordering to improve access patterns
First, GRAIN extracts k-mers from query reads
Second, GRAINS performs Sizes lookup. We perform this step in the host system because
Sizes is significantly smaller than other sub-structures AND
Looking up Sizes in the host system enables opportunities for efficient batching and compaction of queries
Third, GRAINS batches the k-mers based on their sizes values
Fourth, GRAINS sorts the k-mers based on their sizes values. during sorting, we further compact k-mers by exploiting the fact that consecutive k-mers sorted by Sizes share the same minimizer So, we store the minimizer once
and keep only the differences, thereby significantly reducing the transferred data size

## Slide 36: Graph Query
Read Set
AAGCTTCCATGG
AAATGGGCTTTC
GCCCAAATGGTT
GCTTCCAGAATG
Input Query Preparation
AAGCTTCCATGG
AAGC
AGCT
GCTT
…
…
Graph Query
K-Mer Lookup
Read Mapping
❶
❷
Graph-Based Database
Notes: Now, let’s go through the second step, Graph Query

## Slide 37: Graph Query: Overview
GRAINS looks up the query k-mers in the graph and retrieves their associated IDs
  By accessing Offsets

## Slide 38: Graph Query: Overview
GRAINS looks up the query k-mers in the graph and retrieves their associated IDs
  By accessing Offsets, Strings

## Slide 39: Graph Query: Overview
GRAINS looks up the query k-mers in the graph and retrieves their associated IDs
  By accessing Offsets, Strings, and Colors

## Slide 40: Graph Query: Overview
GRAINS looks up the query k-mers in the graph and retrieves their associated IDs
  By accessing Offsets, Strings, and Colors
To efficiently execute this step, GRAINS needs to
  Leverage the large internal bandwidth
  Not require expensive hardware resources in the SSD (e.g., costly logic units or large DRAM capacity/bandwidth)
GRAINS executes this step inside the SSD since it
  Involves accessing large graph structures with low reuse
  Requires only lightweight computation

## Slide 41: Graph Query: Offsets
Host System
Chunk#i+1
SSD Controller
Internal DRAM
Channel#1
GRAINS-Enabled SSD
Chunk#i
Die#1
…
…
Die#M
Channel#N
Die#1
…
Die#M
Sequential accesses to fully exploit internal bandwidth
Only a small part of each page moves outside the dies
Plane#1
Page Buffer
Plane#L
Page Buffer
Die I/O
…
Select
ECCLITE
Efficient pipeline between host and SSD
Notes: Now let me show you an overview of GRAINS’s Offsets lookups.
GRAINS receives Offsets indices and compacted k-mers from the host in chunks.
While a chunk is being analyzed inside the SSD
The next chunk is incoming from the host
Forming an efficient pipeline between the host and the in-SSD executions
Since the Sizes values are sorted by the host and Offsets are uniformly placed across flash dies, the Offsets lookups lead to sequential accesses that fully exploit the SSD’s internal bandwidth
Now let’s look deeper inside a flash die After loading a page into a die’s page buffer, GRAINS applies an adopted light ECC to correct errors The in-flash processing units then select and extract only the targeted Offsets entry and send it to the controller,
avoiding the transfer of full pages. GRAINS caches the extracted values in internal DRAM for Strings queries, as we will see next.

## Slide 42: Graph Query: Strings
We aim for Strings accesses to fully exploit internal bandwidth as well
  However, unlike Offsets, the indices into Strings arrive unsorted
Internal DRAM
GRAINS-Enabled SSD
…
…
…
SSD Cntrl.
Lightweight
Scheduler
GRAINS Scheduler Table1,1
GST1,M
One row per Strings page, each row storing
1) bit address in the page, 2) compacted k-mer info, 3) an overflow flag and pointer
Efficient address mapping frees most of the DRAM
Compact k-mer representation keeps GST entries small
GSTN,M
GSTN,M
Die#1
Die#M
Die#1
Die#M
Channel#1
Channel#N
Notes: We aim for Strings accesses to fully exploit internal bandwidth as well
However, unlike Offsets, the indices into Strings arrive unsorted
To address this challenge, we introduce a lightweight scheduler on the SSD controller
Which maintains a small per-die GRAINS Scheduler Table (GST) in the internal DRAM,
with one row per Strings page. Each row stores 1) bit address in the page, 2) compacted k-mer info, and 3) an overflow flag and pointer
GRAINS can store GSTs in the internal DRAM because of its efficient address mapping, which frees most of the DRAM, AND
its compact k-mer representation, which keeps GST entries small

## Slide 43: Graph Query: Strings
We aim for Strings accesses to fully exploit internal bandwidth as well
  However, unlike Offsets, the indices into Strings arrive unsorted
Internal DRAM
GRAINS-Enabled SSD
…
…
…
SSD Cntrl.
Lightweight Scheduler
GRAINS Scheduler Table1,1
GST1,M
Avoids redundant page accesses
Maximizes die-level parallelism, without relying on sorting accelerators
GSTN,M
GSTN,M
Die#1
Die#M
Die#1
Die#M
ECCLITE
Die I/O
…
==
Shift Reg
Plane#1
Page Buffer
Plane#L
Page Buffer
Channel#1
Channel#N
Notes: When accessing Strings, GRAINS light scheduler schedules requests by simply reading one row per each GST sequentially
and issuing requests across all dies and planes in a round-robin manner.
This naturally coalesces requests to the same page and avoids redundant page accesses AND
Maximizes die-level parallelism, without relying on sorting accelerators
Next, again looking deeper into the flash die
GRAINS reads the corresponding Strings page, and after ECCLITE,
the in-flash processing unit finds the matching unitig IDs and sends to the internal DRAM

## Slide 44: Graph Query: Colors
For each k-mer matching a unitig in Strings, GRAINS retrieves the color of that unitig
GRAINS returns the colors to the host, with colors identifying database entries (e.g., species or samples) containing the matched sequence
Design details are in the paper
Notes: For each k-mer matching a unitig in Strings, GRAINS retrieves the color of that unitig
Retrieved colors are returned to the host, where each color identifies the database entries (e.g., species or samples) containing the matched sequence
I invite you to check the paper for more design details for this step

## Slide 45: Graph Query
Read Set
AAGCTTCCATGG
AAATGGGCTTTC
GCCCAAATGGTT
GCTTCCAGAATG
Input Query Preparation
AAGCTTCCATGG
AAGC
AGCT
GCTT
…
…
Graph Query
K-Mer Lookup
Read Mapping
❶
❷
Graph-Based Database
FTL Design details are in the paper
Notes: Similary, more FTL design details are in the paper.

## Slide 46: More in the Paper
https://arxiv.org/abs/2606.26468

## Slide 47: Outline
Evaluation
Background
Motivation and Gaol
GRAINS
Conclusion
Notes: Now, let’s go through evaluations

## Slide 48: Evaluation Methodology Overview (I)
Performance, Energy, and Power Analysis
Baseline Comparison Points
Fulgor [WABI’23]: A state-of-the-art node-centric tool
MetaGraph [Nature’25]: A state-of-the-art edge-centric tool
AccIdealMem: An idealized accelerator for graph queries with no main memory overheads, but still suffers from the I/O overhead of moving a large amount of low-reuse data
SSD Configurations
SSD-G4: With PCIe Gen4 interface (7 GB/s sequential read bandwidth)
SSD-G5: With PCIe Gen5 interface (14.8 GB/s sequential read bandwidth)
Hardware Components
Synthesized Verilog model for the in-storage accelerators
MQSim [Tavakkol+, FAST’18] for SSD’s internal operations
Ramulator [Kim+, CAL’15] for SSD’s internal DRAM
Software Components
Measure on a real system:
AMD® EPYC® host CPU with 128 physical cores
1.5 TB host DRAM
Notes: We model performance, energy, and power of the systems based on each hardware-based and software-based component
We valuate the following baselines:
...
We evaluate these tools on systems with different state-of-the-art SSD configurations

## Slide 49: Evaluation Methodology Overview (II)
Graph-Based Genome Analysis Task
K-mer set lookup
Alignment-based read mapping
Alignment-free read mapping
Query Samples
With varying sizes
  Small
  Medium
  Large
Notes: We evaluate two graph-based genome analysis tasks
on querying samples of varying sizes

## Slide 50: Benefits over Software
Chart: 
| QL | QM | QS | GMean
Fulgor | 1 | 1 | 1 | 1
MetaGraph | 0.62278 | 0.73413 | 0.77147 | 0.70655
GRAINS | 4.061 | 8.5634 | 17.2404 | 8.4322
Chart: 
| QL | QM | QS | GMean
FG | 1 | 1 | 1 | 1
MG | 0.55421 | 0.68284 | 0.74414 | 0.65546
GRN | 2.7391 | 5.196 | 11.9805 | 5.5452
22.3
Speedup
16.1
SSD-G4
GRAINS provides significant speedup over Fulgor and Metagraph baselines, with both SSD-G4 and SSD-G5
GRAINS improves average energy-efficiency by 11.3x and 21.5x over Fulgor and Metagraph, respectively
SSD-G5
5.5x
8.5x
8.4
11.9
When performing k-mer set lookups
Notes: We observe that on systems with both types of SSDs
GRAINS provides significant speedups compared to both software baselines
While also significantly improving energy efficiency

## Slide 51: Benefits over Hardware
Chart: 
| QL | QM | QS | GMean
IdealAccMem | 1 | 1 | 1 | 1
GRAINS | 2.8967 | 8.0711 | 17.0161 | 7.3547
Chart: 
| QL | QM | QS | GMean
PIM | 1 | 1 | 1 | 1
GRN | 1.5184 | 4.6311 | 11.6728 | 4.3459
SSD-G4
17.0
11.6
Speedup
SSD-G5
GRAINS provides significant speedups over AccIdealMem baseline
4.3x
7.4x
GRAINS improves average energy-efficiency by 3.1—20.7x over AccIdealMem
When performing k-mer set lookups
Notes: Similarly, we observe large performance and energy benefits compared to the hardware baseline

## Slide 52: System Cost-Efficiency
Chart: 
| FG($) | MG($) | FG($$$) | MG($$$) | GRN($)
 | 1 | 0.49121 | 2.819 | 1.8477 | 13.2269
Cost-optimized system ($): With SSD-G4 and 64-GB Host DRAM
Performance-optimized system ($$$): With SSD-G5 and 1-TB Host DRAM
GRAINS outperforms the baselines
even when running on a much less costly system
Speedup
13.2x
26.9x
4.7x
7.2x
($)
($)
($$$)
($$$)
($)
Notes: Next, I am going to show you the impact of GRAINS on system cost efficiency Consider a cost-optimized system with PCIe Gen4 SSD and 64-GB DRAM
a performance-optimized system with PCIe Gen5 SSD and 1-TB DRAM We compare baselines on both systems with GRAINS on the cost-optimized system
And observe that GRAINS provides large benefits when compared to baselines on the cost-optimized system
And we also observe that GRAINS outperforms the baselines
even when running on a much less costly system

## Slide 53: System Cost-Efficiency
Chart: 
| FG($) | MG($) | FG($$$) | MG($$$) | GRN($)
 | 1 | 0.49121 | 2.819 | 1.8477 | 13.2269
Cost-optimized system ($): With SSD-G4 and 64-GB Host DRAM
Performance-optimized system ($$$): With SSD-G5 and 1-TB Host DRAM
GRAINS outperforms the baselines
even when running on a much less costly system
Speedup
13.2x
26.9x
4.7x
7.2x
($)
($)
($$$)
($$$)
($)
GRAINS improves system cost-efficiency
and makes graph-based genome analysis more accessible for wider adoption
Notes: Next, I am going to show you the impact of GRAINS on system cost efficiency Consider a cost-optimized system with PCIe Gen4 SSD and 64-GB DRAM
a performance-optimized system with PCIe Gen5 SSD and 1-TB DRAM We compare baselines on both systems with GRAINS on the cost-optimized system
And observe that GRAINS provides large benefits when compared to baselines on the cost-optimized system
And we also observe that GRAINS outperforms the baselines
even when running on a much less costly system

## Slide 54: Area and Power
Based on Synthesis of GRAINS’s hardware units using the Synopsys Design Compiler @ 22nm technology node
ECCLITE area based on the original paper [AiF, ISCA’25]
On-controller logic units are 0.7% of the four cores on an SSD controller
Logic unit | Area [mm²] | Power [mW]
On SSD Controller | 0.0025 | 0.21
On Die (ECC_LITE) | 0.036 | 18.04
On Die (Others) | 0.000093 | 0.01
On-die logic units take only 0.2% of the flash die’s area and fit well within its power budget
Notes: Based on Synthesis of GRAINS’s hardware units
We observe that On-controller logic units are only a small fraction of the four cores on an SSD controller
And On-die logic units take only also a very small fraction of the flash die’s area and fit well within its power budget

## Slide 55: More in the Paper
GRAINS’s speedups as an accelerator outside the SSD
Impact of different GRAINS optimizations in isolation
  Batching
  Batching + Scheduling
  Batching + Scheduling + SCC
GRAINS’s speedups with varying #SSDs
Execution time breakdown of different steps
GRAINS’s integration with state-of-the-art graph alignment accelerator
GRAINS’s speedup when performing Alignment-Free Read Mapping
Notes: There are may more results in the paper, that I invite you to check, such as

## Slide 56: More in the Paper
https://arxiv.org/abs/2606.26468

## Slide 57: Outline
Conclusion
Background
Motivation and Goal
GRAINS
Evaluation

## Slide 58: Conclusion
Graph-based genome analysis analysis suffers from
significant storage I/O data movement overhead
The first system for large-scale genome graphs analysis in storage Enabled via storage-aware algorithm-architecture co-design, exploiting the properties of large-scale genome graphs
GRAINS
Improves performance
2.7×–47.8× over software baselines
1.5×–17.0× over hardware software
Improves system cost-effectiveness
Reduces energy consumption
4.4×–31.6× over software baseline
3.1×–20.7× over hardware baseline
Makes graph-based genome analysis more accessible for wider adoption

## Slide 59
GRAINS: Enabling High-Performance and Low-Cost
Graph-Based Genome Analysis
via Storage-Aware Algorithm-Architecture Co-Design
Mohammad Sadrosadati Jisung Park Onur Mutlu
Nika Mansouri Ghiasi Harun Mustafa Talu Güloglu Rakesh Nadig
Konstantina Koliogeorgi Susana Rebolledo Ruiz Marc Rautmann Furkan Eris

## Slide 60: Backup Slides

## Slide 61: Unique Characteristics of Genome Graphs
Different Node and Edge Encodings
  Traditional graphs must explicitly store O(N) to O(N²) edges
  DBGs store only nodes or edges and the other is derived implicitly
  Enabled by the inherent overlap structure of encoded sequences
Different Structural Characteristics
  In/out-degrees capped at 4 (A, C, G, T), regardless of graph size
  Power-law hub optimizations from conventional graphs are inapplicable
  Necessitates fundamentally different optimization approaches
Different Access Pattern Optimizations
  Compressed data structures enforce node orderings  no reordering possible
  Structural coupling between queries and graph enables unique locality optimizations
  Query reads sharing k-mer substrings map to nearby index regions

## Slide 62: Benefits Outside the SSD (I)
Key benefits of storage-centric designs outside storage
  Alleviating the burden of moving and analyzing low-reuse data
  More storage-friendly execution pipelines: Efficient access patterns, and fewer random accesses
    Efficient use of the available I/O bandwidth
    Less reliance on large DRAM capacity
However, there are more benefits from analysis inside the storage
  Higher IFP/ISP bandwidth
  Avoid moving low-reuse data
  Does not rely on wider external interfaces

## Slide 63: Benefits Outside the SSD (II)

## Slide 64: Motivation
Case study of the performance of genome graph analysis tools
With various state-of-the-art SSD configurations and data sizes
Chart: 
| 100K | 1M | 10M
SSD-G4 | 0.013012 | 0.057486 | 0.28671
SSD-G5 | 0.025689 | 0.10872 | 0.44565
No-I/O | 1 | 1 | 1
Chart: 
| 100K | 1M | 10M
SSD-G4 | 0.040448 | 0.13429 | 0.43735
SSD-G5 | 0.077752 | 0.23679 | 0.60855
No-I/O | 1 | 1 | 1
#Query Reads
#Query Reads
Normalized Throughput
(i)
(ii)
Chart: 
| MetaSUB (659 GB)
SSD-G4 | 0.23154 | 0.057486
SSD-G5 | 0.37602 | 0.10872
No-I/O | 1 | 1
Chart: 
| SRArep (231 GB) | MetaSUB (822 GB)
SSD-G4 | 0.13249 | 0.057486
SSD-G5 | 0.23398 | 0.10872
Ideal | 1 | 1
SRArep (161 GB) MetaSUB (659 GB)
SRArep (161 GB) MetaSUB (659 GB)
Graph Database
Graph Database
Normalized Throughput
(i)
(ii)
I/O data movement causes significant performance overhead

## Slide 65: Effect of Different GRAINS Optimizations
Chart: 
| QL | QM | QS | GMean
FG | 1 | 1 | 1 | 1
MG | 0.62278 | 0.73413 | 0.77147 | 0.70655
GRN-B | 1.0194 | 1.6376 | 2.0935 | 1.5176
GRN-B-S | 1.3523 | 3.0465 | 9.9586 | 3.449
GRN-B-S-SCC | 4.061 | 8.5634 | 17.2404 | 8.4322
Chart: 
| QL | QM | QS | GMean
FG | 1 | 1 | 1 | 1
MG | 0.55421 | 0.68284 | 0.74414 | 0.65546
GRN-B | 0.9639 | 1.5585 | 2.0523 | 1.4554
GRN-B-S | 1.4712 | 2.9918 | 8.8301 | 3.3873
GRN-B-S-SCC | 2.7391 | 5.196 | 11.9805 | 5.5452
10.0
17.2
Speedup
8.8
12.0
SSD-G4
SSD-G5

## Slide 66: Speedup for Alignment-Free Read Mapping
Chart: 
| QL | QM | QS | GMean
FG | 1 | 1 | 1 | 1
MG | 0.62278 | 0.73413 | 0.77147 | 0.70655
GRN-Ext | 1.2697 | 2.9707 | 10.6185 | 3.4214
GRN | 3.2593 | 7.8812 | 19.0642 | 7.8822
Chart: 
| QL | QM | QS | GMean
FG | 1 | 1 | 1 | 1
MG | 0.55421 | 0.68284 | 0.74414 | 0.65546
GRN-Ext | 1.3254 | 2.8564 | 9.9079 | 3.3474
GRN | 2.1775 | 4.7265 | 13.7906 | 5.2163
10.6
19.1
Speedup
9.9
13.8
SSD-G4
SSD-G5

## Slide 67: Alignment-Based Read Mapping
Chart: 
| QL | QM | QS | GMean
FG+SeGraM | 1 | 1 | 1 | 1
MG+SeGraM | 0.64145 | 0.73588 | 0.77164 | 0.71416
GRN+SeGraM | 3.2849 | 8.0216 | 16.9804 | 7.6485
Chart: 
| QL | QM | QS | GMean
Fulgor+SeGraM | 1 | 1 | 1 | 1
MetaGraph+SeGraM | 0.58417 | 0.68648 | 0.74449 | 0.66836
GRAINS+SeGraM | 2.2824 | 4.8547 | 11.7408 | 5.067
Integrating GRAINS with a state-of-the-art graph alignment accelerator, SeGraM [ISCA’22]
Speedup
When integrated with SeGraM, GRAINS provides significant speedup over Fulgor and Metagraph baselines, with both SSD-G4 and SSD-G5
Notes: Next, we evaluate GRAINS when integrated with a state-of-the-art graph alignment accelerator, SeGraM
And show that GRAINS integrated with SeGraM significantly outperforms other baselines integrated with SeGraM

## Slide 68: Speedup with Different Numbers of SSDs
Chart: 
| QL | QM | QS | GM | QL | QM | QS | GM | 1×SSD | 2×SSDs
FG | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
MG | 0.62278 | 0.73413 | 0.77147 | 0.70655 | 0.55421 | 0.68284 | 0.74414 | 0.65546
GRN | 4.061 | 8.5634 | 17.2404 | 8.4322 | 3.6448 | 7.7493 | 14.2385 | 7.3813
Chart: 
| QL | QM | QS | GM | QL | QM | QS | GM | 1×SSD | 2×SSDs
FG | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
MG | 0.55421 | 0.68284 | 0.74414 | 0.65546 | 0.49555 | 0.61012 | 0.69662 | 0.59497
GRN | 2.7391 | 5.196 | 11.9805 | 5.5452 | 2.7222 | 4.8271 | 9.3742 | 4.9756
SSD-G4
Speedup
SSD-G5