## Slide 1: Storage-Centric System Designs for Enabling Fast, Efficient, and Low-Cost Genomic and Metagenomic Analyses
Nika Mansouri Ghiasi Onur Mutlu
Arch4Health @ ICS 2026
June 2026
Notes: Hi everyone, I am going to give you an overview of my thesis, titled “...”

## Slide 2: Brief Self-Introduction
Nika Mansouri Ghiasi
  Researcher and Lecturer in the SAFARI Research Group @ ETH Zurich
    Defended my PhD thesis, advised by Onur Mutlu, on 31 March 2026
  Visiting researcher at Robust Systems Group @ Stanford
Research interests:
  Computer architecture
  Computational biology
  Storage systems
  Emerging technologies, esp. dense 3D integration
  …
  Designing high-performance, energy-efficient, and low-cost systems
  for widespread adoption of data-intensive applications in healthcare and life sciences
  and enabling new solutions that were out of reach before
Contact Info
  https://nikamgh.github.io
  n.mansorighiasi@gmail.com

## Slide 3: Applications of (Meta)Genome Analysis
Precision Medicine
Outbreak Prevention and Management
Agriculture
Scientific Discovery
& Many More…

## Slide 4: DNA Under Electron Microscope
human chromosome #12
from HeLa cell
Notes: To get the organisms' genomic information encoded in their nucleotide sequences, such as DNA, into a digital format for analysis…

## Slide 5: High-Throughput Sequencers
… and more! All produce data with different properties.
Illumina MiSeq
Pacific Biosciences RS II
Illumina NovaSeq 6000
Oxford
Nanopore GridION
Pacific
Biosciences
Sequel II
Oxford
Nanopore
PromethION
Oxford Nanopore MinION

## Slide 6: High-Throughput Sequencers
… and more! All produce data with different properties.
Illumina MiSeq
Oxford Nanopore MinION
Pacific Biosciences RS II
Illumina NovaSeq 6000
Oxford
Nanopore SmidgION
Pacific
Biosciences
Sequel II
Oxford
Nanopore
PromethION
Current sequencing technologies
cannot sequence very long DNA molecules end-to-end
Instead, they extract smaller fragments of the original DNA sequence, known as reads
AAGCTTCCATGG
AAATGGGCTTTC
GCCCAAATGGTT
GCTTCCAGAATG

## Slide 7: Genome Sequence Analysis
Read mapping: first key step in genome sequence analysis
…GCCCATATGGTTAAGCTTCCATGGAAATGGGCTTTCGCTTCCACAATG…
  Aligns reads to potential matching locations in the reference genome
Reference Genome
Differences
Differences
  For each matching location, the alignment step finds the degree of similarity (alignment score)
AAGCTTCCATGG
GCCCAAATGGTT
GCTTCCAGAATG
AAATGGGCTTTC
Calculating the alignment score requires computationally-expensive approximate string matching (ASM) to account for differences between reads and the reference genome
Notes: Read mapping is the first key step in genome sequence analysis [CLICK]
That Aligns reads to potential matching locations within the reference genome [CLICK]
For each matching location, the alignment step finds the degree of similarity between read and reference by calculating the alignment score
Calculating the alignment score requires computationally-expensive approximate string matching (ASM) to account for differences between reads and the reference genome. [CLICK]

## Slide 8: What is Metagenomics?
Metagenomics: Study of genome sequences of diverse organisms
within a shared environment (e.g., blood, ocean, soil)
A large database containing information
on many species
(e.g., > 100 TBs in emerging databases)
Notes: Since sometimes a sample contains organisms with different species, genomic analysis is complemented by metagenomic analysis
Which enables the Study of genome sequences of diverse organisms within a shared environment (e.g., blood, ocean, soil)

## Slide 9: Sequence Data is Growing at a Fast Pace
Important Role in Many Fields
Large Reduction in Sequencing Cost
Fast growth in sequence data size
Publicly-Hosted Genomic Sequence Reads Data Size in Sequence Read Archive (SRA) Over Years
Chart: Total Size (TB)
~1000000x

## Slide 10: Overheads of (Meta)Genomic Analyses
Computation overhead
Data movement overhead
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Data Movement
Storage
System

## Slide 11: Accelerating (Meta)Genome Sequence Analysis
Heuristics
Accelerators
Filters
Computation overhead
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
✓
Storage
System
Notes: Motivated by all these factors, there has been significant efforts into improving performance [CLICK]
Through… Although there have been significant efforts to improve the analysis of large-scale sequence data,

## Slide 12: Problems
Accessing stored sequence data and feeding it to the analysis units
Overhead of moving large amounts of low-reuse data from the storage system
& unnecessary computational burden on the rest of the system
Notes: In this thesis, we identify major outstanding problems in
accessing stored sequence data
and feeding it to the analysis units.

## Slide 13: Accelerating (Meta)Genome Sequence Analysis
Heuristics
Accelerators
Filters
Computation overhead
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Storage
System
Data movement overhead
✓
Notes: There has been significant effort into improving read mapping performance [CLICK]
Through efficient heuristics [CLICK]
hardware accelerators [CLICK]
and various filters that prune reads that do not require expensive computation [CLICK].
While these approaches address the computation overhead in read mapping [CLICK]
[While Reads Move] None of them alleviate the data movement overhead from storage, whose impact becomes even larger when the computation overhead gets alleviated [CLICK]

## Slide 14: Problems
Accessing stored sequence data and feeding it to the analysis units
Overhead of moving large amounts of low-reuse data from the storage system
& unnecessary computational burden on the rest of the system
Data preparation bottleneck, where compressed genomic sequence data needs to be first decompressed and formatted before it can be analyzed

## Slide 15: Effect of the Data Preparation Bottleneck
Prep
Analysis
Analysis
Analysis
Base.
Acc. Analysis
w/ Ideal Prep.
Prep
Prep
Lost Benefit due to Data Prep. Bottleneck
Execution Timeline (Not drawn to scale)
Acc. Analysis
Potential Benefit of Genome Analysis Acceleration
Baseline Analysis (446 KRead/s)
Accelerated Analysis (69200 KRead/s)
Baseline Prep. (2563 KRead/s)
Ideal Prep. (> 69200 KRead/s)
Notes: 2:10

## Slide 16: Thesis Statement
By designing customized storage-centric systems that efficiently
analyze genomic and metagenomic data inside the storage system
enable highly-compressed storage and high-performance access of large-scale sequence data
we can alleviate the overheads of
computation
data movement
data preparation
thereby, significantly improving
performance
energy efficiency
cost effectiveness
⓵
⓶

## Slide 17: Our Approach
Designing customized storage-centric systems that efficiently
we can alleviate the overheads of
computation
data movement
data preparation
thereby, significantly improving
performance
energy efficiency
cost effectiveness
analyze genomic and metagenomic data inside the storage system
⓵
enable highly-compressed storage and high-performance access of large-scale sequence data
⓶

## Slide 18: Our Approach
Designing customized storage-centric systems that efficiently
MegIS [ISCA’24] Cooperative in-storage processing for metagenomic analysis
GRAINS [ISCA’26] Storage-aware algorithm-architecture co-design for graph-based (meta)genomic analyses
GenStore [ASPLOS’22] In-storage filtering for genomic analysis
SAGe [HPCA’26] Algorithm-architecture co-design for storing and accessing sequence data
analyze genomic and metagenomic data inside the storage system
⓵
enable highly-compressed storage and high-performance access of large-scale sequence data
⓶

## Slide 19: Our Approach
Designing customized storage-centric systems that efficiently
MegIS [ISCA’24] Cooperative in-storage processing for metagenomic analysis
GRAINS [ISCA’26] Storage-aware algorithm-architecture co-design for graph-based (meta)genomic analyses
GenStore [ASPLOS’22] In-storage filtering for genomic analysis
SAGe [HPCA’26] Algorithm-architecture co-design for storing and accessing sequence data
analyze genomic and metagenomic data inside the storage system
⓵
enable highly-compressed storage and high-performance access of large-scale sequence data
⓶

## Slide 20: Key Idea
Storage
System
Non-matching reads
Do not have potential matching locations and can skip alignment
Filter reads that do not require alignment
inside the storage system
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Filtered Reads
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Exactly-matching reads
Do not need expensive approximate string matching during alignment
GenStore
MegIS
GRAINS
SAGe
Notes: Our key idea is to filter reads that do not require the expensive alignment computation in the storage system [CLICK] …
[While Reads Move] To fundamentally reduce the data movement overhead of read mapping
Examples of the reads that not require the costlt alignment step
Exactly-matching reads to the reference genome that do not need approximate string matching performed during alignment
Non-matching reads that have no potential matching locations in the reference genome hence skip the alignemt step

## Slide 21: Read Mapping Process
GCC | 7 |  | 
CCC | 8 |  | 
CAA | 1 |  | 
AAA | 31 | 101 | 
CCA | 25 | 230 | 400
… | … | … | …
…CAATTTGCCCATATGGTTAAGCTTCCATGGAAATGGGCTTTCGCTTTG…
Reference
> 3 billion characters for the human genome
Index
K-mer
Locations
GCCCAAATGGTT
Read
GCC
CCC
…
K-mers
Determine potential matching locations (seed hits) in the reference genome
Prune some seed hits in the reference genome
Determine the exact differences between the read and the reference genome
Seeding
Seed Filtering
(e.g., Chaining)
Alignment
Seed Hits
…
GenStore
MegIS
GRAINS
SAGe
Notes: Mapping reads to reference genome requires expensive computation on large datasets.
[CLICK] The search space in the Reference genome can be very large (for example the human reference genome contains more than three billion characters).
[CLICK] Therefore, read mappers typically use an index of the reference genome to reduce the search space. This index contains unique 𝑘-length subsequences ([CLICK] called 𝑘-mers) extracted from the reference genome, [CLICK] and locations of these 𝑘-mers in the reference genome.
Read mapping is a three step process. State-of-the-art read mappers involve several heuristics to reduce the cost of expensive alignment computation.
[CLICK] In the first step (seeding), the mapper determines the potential matching locations (seeds) in the large reference genome where the read could map.
[CLICK] To do so, the read mapper extracts k-mers from the read [CLICK] and looks up the k-mer fetched from a read in the reference index. [CLICK] For all the k-mers that hit in the index, the read mapper marks the locations of them in the reference genome as the read’s potential matching locations (or seeds).
To further reduce the cost of the computationally-expensive alignment, the read mapper performs a second step [CLICK] , called chaining or seed filtering, in which the mapper [CLICK] prunes the seeds in the reference to which the read would not align using a simple approximation of the alignment score.
At the end of this step, the reads that have all their locations filtered, skip the third step.
[CLICK] For the remaining reads, the thitd step, which is the costly alignment, determines the exact differences between a read and the reference genome [CLICK] via approximate string matching.

## Slide 22: GenStore
GenStore for Exactly-Matching Reads
GenStore for Non-Matching Reads
GenStore
MegIS
GRAINS
SAGe
Notes: by thorough analysis of mapping processes of reads with different properties and different degrees of genetic variation, we design two low-cost in-storage filters
[CLICK] 1) GenStore-EM for filtering exactly-matching reads
[CLICK] and 2) GenStore-NM for filtering most of the non-matching reads

## Slide 23: GenStore
GenStore for Exactly-Matching Reads
GenStore for Non-Matching Reads
GenStore
MegIS
GRAINS
SAGe
Notes: by thorough analysis of mapping processes of reads with different properties and different degrees of genetic variation, we design two low-cost in-storage filters
[CLICK] 1) GenStore-EM for filtering exactly-matching reads
[CLICK] and 2) GenStore-NM for filtering most of the non-matching reads

## Slide 24: GenStore for Exactly-Matching Reads
Efficient in-storage filter for reads with at least one exact match in the reference genome
Uses simple operations, without requiring alignment
Challenge: Large number of random accesses per read to the reference genome and its index
Expensive random accesses to flash chips
Limited DRAM capacity inside the SSD
GenStore
MegIS
GRAINS
SAGe
Notes: [CLICK] GenStore-EM accelerates read mapping by using an efficient in-storage filter to filter reads that have at least one exactly matching location in the reference genome
[CLICK] via simple operations, without requiring alignment.
The key challenge in designing GenStore-EM is the large number of random accesses to large data structures inside the SSD.
This is challenging because. [CLICK]
NAND flash memory exhibits poor performance for random access reads. [CLICK]
there is limited DRAM capacity available in SSD which is relatively small compared to the size of the data structures that need to be accessed.

## Slide 25: Data Structures
GCCCAAATGGTT
Read
GCC
CCC
…
K-mers
K-mer
Read-sized k-mers: to reduce the number of accesses per each read
Only one index lookup per read
Sorted read-sized k-mers: to avoid random accesses to the index
Sequential scan of the read set and the index
✓
✓
GenStore
MegIS
GRAINS
SAGe
Notes: To reduce the **number** of accesses per each read, we introduce read-sized k-mers.
Therefore, instead of extracting several k-mers per read and performing index lookup for each of them, [CLICK] we can use the whole read as one k-mer
[CLICK] And have only one index lookup per read
[CLICK] To avoid **random** accesses to the index, we introduce the **sorted** index of read-sized k-mers.
[CLICK] This sorted index allows finding exact matches via sequential scanning of the read sets and the index

## Slide 26: Index Optimization
Read-sized k-mer index takes up a large amount of space (126 GB for human index) due to the larger number of unique k-mers
K-mer | Loc.
AAAAAAAAAA | 1, 8, …
AAAAAAAAAC | 51
AAAAAAAAAT | 23, 37
… | …
Sorted K-mer Index
Strong Hash Value
1
4
7
…
Using strong hash values instead of read-sized k-mers
reduces the size of the index by 3.9x
GenStore
MegIS
GRAINS
SAGe
Notes: Despite the key benefits of the sorted read-sized k-mer index, this index takes up a large space (126 GB for human index) due to the large number of unique read-sized k-mers.
We further reduce the overheads of GenStore-EM, by replacing read-sized k-mers with a strong hash of each read that act as
Sorting criterion
Fingerprint of each entry
Using strong hash values instead of read-sized k-mers reduces the size of the index by 3.9x
While this index is still larger than the baseline k-mer index used in the conventional read mappers, our proposal is feasible for in-storage processing due to the large capacity and high internal bandwidth of modern NAND flash-based SSDs.

## Slide 27: Evaluation Methodology
Read Mappers
Base: state-of-the-art software or hardware read mappers
  Minimap2 [Bioinformatics’18]: software mapper for short and long reads
  GenCache [MICRO’19]: hardware mapper for short reads
  Darwin [ASPLOS’18]: hardware mapper for long reads
GS: Base integrated with GenStore
SSD Configurations
SSD-L: With SATA3 interface (0.5 GB/s sequential read bandwidth)
SSD-M: With PCIe Gen3 interface (3.5 GB/s sequential read bandwidth)
SSD-H: With PCIe Gen4 interface (7 GB/s sequential read bandwidth)
GenStore
MegIS
GRAINS
SAGe
Notes: We valuate the following systems:
[CLICK] Base: state-of-the-art software or hardware read mappers for both short and long reads
[CLICK] GS: Base integrated with the GenStore inside the SSD
We evaluate these mappers on systems with various SSD configurations, a low-end, medium-end, and high-end SSD
For other details about our methodology, please refer to the paper.

## Slide 28: GenStore for Exactly-Matching Reads
For a read set with 80% exactly-matching reads
Chart: 
| Base | GS | Base | GS | Base | GS | SSD-L | SSD-M | SSD-H
Other | 170.17 | 69.24 | 154.65 | 74.71 | 159.07 | 73.31
Alignment | 0 | 0 | 0 | 0 | 0 | 0
Exec. time [sec]
Chart: 
| Base | GS | Base | GS | Base | GS | SSD-L | SSD-M | SSD-H
 | 44 | 8.8 | 6.2857 | 2.8229 | 4.2832 | 2.8229
 | 0 | 0 | 0 | 0 | 0 | 0
With the Software Mapper
With the Hardware Mapper
2.1× - 2.5× speedup compared to the software Base
1.5× – 3.3× speedup compared to the hardware Base
On average 3.92× energy reduction
29
2.5x
2.1x
2.1x
3.3x
1.5x
2.5x
GenStore
MegIS
GRAINS
SAGe
Notes: We analyze the benefits of GenStore-EM for a 22-GB short read set where 80% of reads exactly match some subsequence in the reference genome and can be filtered.
We show the benefit of GS on software and hardware read mappers.
GS provides 2.1× - 2.5× speedup compared to the software Base
GS provides 1.5× – 3.3× speedup compared to the hardware Base
GS provides on average 3.92× energy reduction

## Slide 29: GenStore for Non-Matching Reads
For a read set with 99.7% non-matching reads
Chart: 
| Base | GS | Base | GS | Base | GS | SSD-L | SSD-M | SSD-H
 | 30.028 | 1.564 | 5.362 | 0.78198 | 5.36 | 0.78198
Exec. time [sec]
Log scale
With the Software Mapper
With the Hardware Mapper
22.4× – 27.9× speedup compared to the software Base
6.8× – 19.2× speedup compared to the hardware Base
On average 27.2× energy reduction
Chart: 
| Base | GS | Base | GS | Base | GS | SSD-L | SSD-M | SSD-H
Time | 34.84 | 1.5537 | 22.55 | 0.77687 | 21.72 | 0.77687
22.4
29x
27.9x
19.2x
6.8x
6.8x
GenStore
MegIS
GRAINS
SAGe
Notes: Similarly, when evaluating GenStore’s filter for non-matching reads, …

## Slide 30: Area and Power
Based on Synthesis of GenStore accelerators using the Synopsys Design Compiler @ 65nm technology node
Logic unit | # of instances | Area [mm2] | Power [mW]
Comparator | 1 per SSD | 0.0007 | 0.14
K -mer Window | 2 per channel | 0.0018 | 0.27
Hash Accelerator | 2 per SSD | 0.008 | 1.8
Location Buffer | 1 per channel | 0.00725 | 0.37375
Chaining Buffer | 1 per channel | 0.008 | 0.95
Chaining PE | 1 per channel | 0.004 | 0.98
Control | 1 per SSD | 0.0002 | 0.11
Total for an 8-channel SSD | - | 0.2 | 26.6
Only 0.006% of a 14nm Intel Processor, less than 9.5% of the three ARM processors in a SATA SSD controller
GenStore
MegIS
GRAINS
SAGe
Notes: We find area and power values of GenStore by synthesizing GenStore-EM and NM using 65nm technology node,
And find that for an 8-channel SSD, the area of GS is 0.2 mm square and the power is 26.6 watts
BY scaling the area to lower technology nodes, we observe that the area overhead of GS is 0.006% of an Intel processor and less than 9.5% of the of the three ARM processors in a SATA SSD controller.

## Slide 31: Our Approach
Designing customized storage-centric systems that efficiently
MegIS [ISCA’24] Cooperative in-storage processing for metagenomic analysis
GRAINS [ISCA’26] Storage-aware algorithm-architecture co-design for graph-based (meta)genomic analyses
GenStore [ASPLOS’22] In-storage filtering for genomic analysis
SAGe [HPCA’26] Algorithm-architecture co-design for storing and accessing sequence data
analyze genomic and metagenomic data inside the storage system
⓵
enable highly-compressed storage and high-performance access of large-scale sequence data
⓶

## Slide 32: Our Approach
Designing customized storage-centric systems that efficiently
MegIS [ISCA’24] Cooperative in-storage processing for metagenomic analysis
GRAINS [ISCA’26] Storage-aware algorithm-architecture co-design for graph-based (meta)genomic analyses
GenStore [ASPLOS’22] In-storage filtering for genomic analysis
SAGe [HPCA’26] Algorithm-architecture co-design for storing and accessing sequence data
analyze genomic and metagenomic data inside the storage system
⓵
enable highly-compressed storage and high-performance access of large-scale sequence data
⓶

## Slide 33: Challenges of Storage-Centric Computing
Metagenomic analysis tools cannot run in-storage due to SSD limits
  Long latency of NAND flash chips
  Limited DRAM capacity inside the SSD
  Limited DRAM bandwidth inside the SSD
SSD DRAM
⋯
SSD
Controller
Cores
FTL
⋯
SSD
Cntrl
Cntrl
Channel#N
Channel#1
GenStore
MegIS
GRAINS
SAGe
Notes: While ...,
none of the existing approaches can be effectively implemented
inside the SSD due to limited hardware resources in the SSD ...

## Slide 34: MegIS: Metagenomics In-Storage
First in-storage system for end-to-end metagenomic analysis
Idea: Cooperative in-storage processing for metagenomic analysis
  Algorithm-Architecture co-design between the storage system and host system
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
GenStore
MegIS
GRAINS
SAGe
Notes: Which is the first in-storage processing system for end-to-end metagenomic analysis
The key idea of megis is Cooperative ISP for metagenomics
Which is enabled by a synergistic hardware/software co-design between the storage system and the host system

## Slide 35: MegIS Algorithm-Architecture Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
GenStore
MegIS
GRAINS
SAGe
Notes: To (i) leverage and (ii) orchestrate the capabilities of both systems, megis includes hw/sw co-design in 5 directions

## Slide 36: MegIS Algorithm-Architecture Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Task partitioning and mapping
Each step executes
in its most suitable system
GenStore
MegIS
GRAINS
SAGe

## Slide 37: MegIS Algorithm-Architecture Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Task partitioning and mapping
Each step executes
in its most suitable system
GenStore
MegIS
GRAINS
SAGe

## Slide 38: MegIS Algorithm-Architecture Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Storage-aware algorithms
Enable efficient
access patterns to the SSD
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Task partitioning and mapping
Each step executes
in its most suitable system
GenStore
MegIS
GRAINS
SAGe

## Slide 39: MegIS Algorithm-Architecture Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
ACC
ACC
Cntrl
Cntrl
Channel#N
Channel#1
Lightweight in-storage accelerators
Minimize SRAM/DRAM buffer spaces needed inside the SSD
Storage-aware algorithms
Enable efficient
access patterns to the SSD
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Task partitioning and mapping
Each step executes
in its most suitable system
GenStore
MegIS
GRAINS
SAGe

## Slide 40: MegIS Algorithm-Architecture Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
⋯
MegIS-Enabled SSD
MegIS
FTL
MegIS
Metadata
Cntrl
Cntrl
Channel#N
Channel#1
Data mapping scheme and Flash Translation Layer (FTL)
Specialize to the characteristics of metagenomic analysis
Leverage the SSD’s full internal bandwidth
Storage-aware algorithms
Enable efficient
access patterns to the SSD
Lightweight in-storage accelerators
Minimize SRAM/DRAM buffer spaces needed inside the SSD
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Task partitioning and mapping
Each step executes
in its most suitable system
ACC
ACC
GenStore
MegIS
GRAINS
SAGe
Notes: 6 mins until here

## Slide 41: Evaluation Methodology Overview (I)
Performance, Energy, and Power Analysis
Baseline Comparison Points
Performance-optimized software, Kraken2 [Genome Biology’19]
Accuracy-optimized software, Metalign [Genome Biology’20]
PIM hardware-accelerated tool (using processing-in-memory), Sieve [ISCA’21]
SSD Configurations
SSD-C: With SATA3 interface (0.5 GB/s sequential read bandwidth)
SSD-P: With PCIe Gen4 interface (7 GB/s sequential read bandwidth)
Hardware Components
Synthesized Verilog model for the in-storage accelerators
MQSim [Tavakkol+, FAST’18] for SSD’s internal operations
Ramulator [Kim+, CAL’15] for SSD’s internal DRAM
Software Components
Measure on a real system:
AMD® EPYC® host CPU with 128 physical cores
1 TB host DRAM
GenStore
MegIS
GRAINS
SAGe
Notes: We model performance, energy, and power of the systems based on the latency and throughput of each hardware-based and software-based component
We valuate the following baselines:
...
We evaluate these tools on systems with cost-optimized and performance-optimized SSD configurations

## Slide 42: Speedup over Software (with Cost-Optimized SSD)
MegIS provides significant speedup over both
Performance-Optimized and Accuracy-Optimized baselines
Speedup
Performance-Optimized
MegIS
Accuracy-Optimized
Sample Genetic Diversity
Chart: 
| Low | Med | High | GMean
P-Opt | 1 | 1 | 1 | 1
A-Opt | 0.43101 | 0.38921 | 0.35039 | 0.38881
MS | 5.3489 | 5.6406 | 6.3871 | 5.7761
SSD-C
5.8x
14.9x
Chart: 
| Low | Med | High | GMean
P-Opt | 1 | 1 | 1 | 1
A-Opt | 0.43101 | 0.38921 | 0.35039 | 0.38881
MS | 5.3489 | 5.6406 | 6.3871 | 5.7761
SSD-C
5.8x
Sample Genetic Diversity
14.9x
GenStore
MegIS
GRAINS
SAGe
Notes: We analyze the benefits of MegIS for samples with low, medium, and high genetic diversity,
And here I am showing for a cost optimized-SSD
We observe that compared to both P-Opt and A-Opt
MegIS provides significant speedups

## Slide 43: Speedup over Software (with Performance-Optimized SSD)
MegIS provides significant speedup over both
Performance-Optimized and Accuracy-Optimized baselines
Speedup
Performance-Optimized
MegIS
Accuracy-Optimized
Sample Genetic Diversity
Chart: 
| Low | Med | High | GMean
P-Opt | 1 | 1 | 1 | 1
A-Opt | 0.3836 | 0.29101 | 0.31974 | 0.32925
MS | 2.6617 | 3.6664 | 6.5218 | 3.9926
SSD-P
4.0x
12.1x
MegIS improves performance on both
cost-optimized and performance-optimized SSDs
GenStore
MegIS
GRAINS
SAGe

## Slide 44: Speedup over the PIM Hardware Baseline
4.9x
Chart: 
| Low | Med | High | GMean
 | 1 | 1 | 1 | 1
 | 4.8422 | 4.8446 | 5.0596 | 4.9144
Chart: 
| Low | Med | High | GMean
 | 1 | 1 | 1 | 1
 | 1.462 | 1.7798 | 2.7359 | 1.9237
Speedup
SSD-C
PIM
MegIS
1.9x
SSD-P
Sample Genetic Diversity
Sample Genetic Diversity
PIM
MegIS
MegIS provides significant speedup over the PIM baseline
GenStore
MegIS
GRAINS
SAGe
Notes: Similarly, we evaluate megis compared to the pim baseline
and show that on systems with cost-optimized
and performance-optimized ssds,
MegiS significantly outperforms the PIM baseline

## Slide 45: Reduction in Energy Consumption
On average across different input sets and SSDs
Chart: 
| Perf-Opt | Acc-Opt | PIM | MegIS
 | 1 | 0.35526 | 2.8421 | 5.4
GeoMean Energy Reduction
(Higher is Better)
MegIS provides significant energy reduction over
the Performance-Optimized, Accuracy-Optimized, and PIM baselines
5.4x
15.2x
1.9x
Same
accuracy
GenStore
MegIS
GRAINS
SAGe
Notes: Next, we show megis's energy reduction on average accross different input sets and SSDs and observe that megis provides...

## Slide 46: Accuracy, Area, and Power
Accuracy
Same accuracy as the accuracy-optimized baseline
Significantly higher accuracy than the performance-optimized and PIM baselines
  4.6 – 5.2× higher F1 score
  3 – 24% lower L1 norm error
Area and Power
Total for an 8-channel SSD:
Area: 0.04 mm2
Power: 7.658 mW
(Only 1.7% of the area and 4.6% of the power consumption
of three ARM Cortex R4 cores in an SSD controller)
GenStore
MegIS
GRAINS
SAGe
Notes: MegIS provides all these benefits while achieving high accuracy

## Slide 47: System Cost-Efficiency
GMean Speedup
Chart: 
| Perf-Opt ($) | Acc-Opt ($) | Perf-Opt($$$) | Acc-Opt ($$$) | MegIS ($)
 | 1 | 0.81324 | 6.8304 | 2.2454 | 16.1756
Cost-optimized system ($): With SSD-C and 64-GB DRAM
Performance-optimized system ($$$): With SSD-P and 1-TB DRAM
MegIS outperforms the baselines
even when running on a much less costly system
($)
($)
($$$)
($$$)
($)
7.2x
2.4x
16.2x
19.9x
GenStore
MegIS
GRAINS
SAGe
Notes: Self-note (copy from arxiv version): For the performance-optimized system, we calculate the cost of 1TB
DRAM to be roughly 7080 USD (8 x 128GB modules [230]) and the cost of
SSD-P to be roughly 875 USD. For the performance-optimized system, we calculate
the cost of 64GB DRAM to be roughly 312 USD (8 x 8GB modules [231],
assuming the same number of memory channels as the performance-optimized
system) and the cost of SSD-C to be roughly 346 USD. Note that the cost of
the total storage system depends not only on the price of each SSD but also on
the available interconnection slots in the systems, as systems typically have
fewer PCIe slots (needed for SSD-P) than SATA slots (needed for SSD-C).

## Slide 48: Our Approach
Designing customized storage-centric systems that efficiently
MegIS [ISCA’24] Cooperative in-storage processing for metagenomic analysis
GRAINS [ISCA’26] Storage-aware algorithm-architecture co-design for graph-based (meta)genomic analyses
GenStore [ASPLOS’22] In-storage filtering for genomic analysis
SAGe [HPCA’26] Algorithm-architecture co-design for storing and accessing sequence data
analyze genomic and metagenomic data inside the storage system
⓵
enable highly-compressed storage and high-performance access of large-scale sequence data
⓶

## Slide 49: Our Approach
Designing customized storage-centric systems that efficiently
MegIS [ISCA’24] Cooperative in-storage processing for metagenomic analysis
GRAINS [ISCA’26] Storage-aware algorithm-architecture co-design for graph-based (meta)genomic analyses
GenStore [ASPLOS’22] In-storage filtering for genomic analysis
SAGe [HPCA’26] Algorithm-architecture co-design for storing and accessing sequence data
analyze genomic and metagenomic data inside the storage system
⓵
enable highly-compressed storage and high-performance access of large-scale sequence data
⓶

## Slide 50: Large-Scale Genome Graphs
Powerful and efficient representations of genomic data
✓
Great expressive power
Compact representations
✓
GenStore
MegIS
GRAINS
SAGe
Input Sequences
Critical for enabling massive, population-scale analyses
GTGG
TGGA
TATG
GTGGATTATGACGAGGCTA
ATGA
TGAC
GACG
ACGA
CGAG
…
…
GTGG
TGGA
GTGGATTATGCCGAGGCTA
TATG
…
…
ATGC
TGCC
GCCG
CCGA
CGAG
GTGG
TGGA
TATG
GTGGATTATGTCGAGGCTA
ATGT
TGTC
GTCG
TCGA
CGAG
…
…
Graph Representation
GTGGATTATG
ATGACGA
ATGCCGA
ATGTCGA
CGAGGCTA
GTGG
TGGA
TATG
GTGGATTATGACGAGGCTA
ATGA
TGAC
GACG
ACGA
CGAG
…
…
GTGG
TGGA
GTGGATTATGCCGAGGCTA
TATG
…
…
ATGC
TGCC
GCCG
CCGA
CGAG
GTGG
TGGA
TATG
GTGGATTATGTCGAGGCTA
ATGT
TGTC
GTCG
TCGA
CGAG
…
…
Notes: Unlike traditional models, which represent genomic databases as a collection of disjoint, linear sequences, sequences in a graph are represented by graph walks

## Slide 51: Challenges of Storage-Centric Computing
Graph-based sequence analysis tools cannot run in storage due to SSD limits
GenStore
MegIS
GRAINS
SAGe
Dependent and random accesses to the sequence graph
Different properties from conventional, non-genome graphs
New challenges due to:
SSD DRAM
⋯
SSD
Controller
Cores
FTL
⋯
SSD
Cntrl
Cntrl
Channel#N
Channel#1
Notes: Again, while analyzing large-scale genome graphs inside storage can provide large benefits,
No graph-based analysis tool can directly run inside storage due to limitations of modern SSDs, as discussed before
And these challenges are exacerbated due to…

## Slide 52: GRAINS
The first system for analysis with large-scale genome graphs in storage
Enabled via storage-aware algorithm-architecture co-design, based on the properties of large-scale genome graphs to
  Make the execution pipeline more storage-friendly
  Further improve performance, energy-efficiency, and cost-effectiveness via storage-centric computing
…
Flash
Cntrl.
Flash Cntrl.
Baseline
Metadata
SSD Controller
Internal DRAM
Channel#1
…
NAND Die#M
GRAINS-Enabled SSD
Host System
…
NAND Die#2
NAND Die#M
NAND Die#2
NAND Die#1
NAND Die#1
Channel#N
FTL
Cores
GenStore
MegIS
GRAINS
SAGe

## Slide 53: GRAINS’s Algorithm-Architecture Co-Design
…
Flash
Cntrl.
Flash Cntrl.
SSD Controller
Internal DRAM
Channel#1
…
NAND Die#M
GRAINS-Enabled SSD
Host System
…
NAND Die#2
NAND Die#M
NAND Die#2
NAND Die#1
NAND Die#1
Channel#N
Cores
New batching technique and execution flow
based on the unique features of genome graphs that reduces #random accesses
Input Query Processing
GenStore
MegIS
GRAINS
SAGe

## Slide 54: GRAINS’s Algorithm-Architecture Co-Design
…
Flash
Cntrl.
Flash Cntrl.
SSD Controller
Internal DRAM
Channel#1
…
NAND Die#M
GRAINS-Enabled SSD
Host System
…
NAND Die#2
NAND Die#M
NAND Die#2
NAND Die#1
NAND Die#1
Channel#N
Cores
New batching technique and execution flow
based on the unique features of genome graphs that reduces #random accesses
Input Query Processing
In-storage and In-flash processing to avoid transferring low-reused pages and bandwidth waste
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
GenStore
MegIS
GRAINS
SAGe

## Slide 55: GRAINS’s Algorithm-Architecture Co-Design
…
Flash
Cntrl.
Flash Cntrl.
GRAINS
Metadata
SSD Controller
Internal DRAM
Channel#1
…
NAND Die#M
GRAINS-Enabled SSD
Host System
…
NAND Die#2
NAND Die#M
NAND Die#2
NAND Die#1
NAND Die#1
Channel#N
GRAINS FTL
Cores
New batching technique and execution flow
based on the unique features of genome graphs that reduces #random accesses
Input Query Processing
In-storage and In-flash processing to avoid transferring low-reused pages and bandwidth waste
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
FTL and data placement based on genome graph properties, to leverage SSD’s full internal bandwidth
GenStore
MegIS
GRAINS
SAGe

## Slide 56: GRAINS’s Algorithm-Architecture Co-Design
…
Flash
Cntrl.
Flash Cntrl.
GRAINS
Metadata
SSD Controller
Internal DRAM
Channel#1
…
NAND Die#M
GRAINS-Enabled SSD
Host System
…
NAND Die#2
NAND Die#M
NAND Die#2
NAND Die#1
NAND Die#1
Channel#N
GRAINS FTL
Cores
New batching technique and execution flow
based on the unique features of genome graphs that reduces #random accesses
Input Query Processing
In-storage and In-flash processing to avoid transferring low-reused pages and bandwidth waste
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
FTL and data placement based on genome graph properties, to leverage SSD’s full internal bandwidth
Lightweight scheduling technique enabled by repurposing the existing SSD structures to leverage the full parallelism of all flash dies
Light Scheduler
Scheduler Tables
GenStore
MegIS
GRAINS
SAGe

## Slide 57: Evaluation Methodology Overview (I)
Performance, Energy, and Power Analysis
Baseline Comparison Points
Fulgor [WABI’23]: A state-of-the-art node-centric tool
MetaGraph [Nature’25]: A state-of-the-art edge-centric tool
AccIdealMem: An idealized accelerator for graph queries with no main memory overheads, but still suffers from the I/O overhead of moving a large amount of low-reuse data
SSD Configurations
SSD-G4: With PCIe Gen4 interface (7 GB/s sequential read bandwidth)
SSD-G5: With PCIe Gen5 interface (14.8 GB/s sequential read bandwidth)
Hardware Components
Synthesized Verilog model for the in-storage accelerators
MQSim [Tavakkol+, FAST’18] for SSD’s internal operations
Ramulator [Kim+, CAL’15] for SSD’s internal DRAM
Software Components
Measure on a real system:
AMD® EPYC® host CPU with 128 physical cores
1.5 TB host DRAM
GenStore
MegIS
GRAINS
SAGe
Notes: We model performance, energy, and power of the systems based on the latency and throughput of each hardware-based and software-based component
We valuate the following baselines:
...
We evaluate these tools on systems with cost-optimized and performance-optimized SSD configurations

## Slide 58: Benefits over Software
Chart: 
| QL | QM | QS | GMean
Fulgor | 1 | 1 | 1 | 1
MetaGraph | 0.62278 | 0.73413 | 0.77147 | 0.70655
GRAINS | 4.061 | 8.5634 | 17.2404 | 8.4322
Chart: 
| QL | QM | QS | GMean
FG | 1 | 1 | 1 | 1
MG | 0.55421 | 0.68284 | 0.74414 | 0.65546
GRN | 2.7391 | 5.196 | 11.9805 | 5.5452
22.3
Speedup
16.1
SSD-G4
GRAINS provides significant speedup over Fulgor and Metagraph baselines, with both SSD-G4 and SSD-G5
GRAINS improves average energy-efficiency by 11.3x and 21.5x over Fulgor and Metagraph, respectively
SSD-G5
5.5x
8.5x
8.4
11.9
GenStore
MegIS
GRAINS
SAGe

## Slide 59: Benefits over Hardware
Chart: 
| QL | QM | QS | GMean
IdealAccMem | 1 | 1 | 1 | 1
GRAINS | 2.8967 | 8.0711 | 17.0161 | 7.3547
Chart: 
| QL | QM | QS | GMean
PIM | 1 | 1 | 1 | 1
GRN | 1.5184 | 4.6311 | 11.6728 | 4.3459
SSD-G4
17.0
11.6
Speedup
SSD-G5
GRAINS provides significant speedups over AccIdealMem baseline
4.3x
7.4x
GRAINS improves average energy-efficiency by 3.1—20.7x over AccIdealMem
GenStore
MegIS
GRAINS
SAGe

## Slide 60: Area and Power
Based on Synthesis of GRAINS’s hardware units using the Synopsys Design Compiler @ 22nm technology node
ECCLITE area based on the original paper [AiF, ISCA’25]
On-controller logic units are 0.7% of the four cores on an SSD controller
Logic unit | Area [mm²] | Power [mW]
On SSD Controller | 0.0025 | 0.21
On Die (ECC_LITE) | 0.036 | 18.04
On Die (Others) | 0.000093 | 0.01
On-die logic units take only 0.2% of the flash die’s area and fit well within its power budget
GenStore
MegIS
GRAINS
SAGe

## Slide 61: More Details
ISCA 2026 Presentation: Monday, June 29
Session 4C, 16:55 EDT
Paper:
https://arxiv.org/abs/2606.26468

## Slide 62: Our Approach
Designing customized storage-centric systems that efficiently
MegIS [ISCA’24] Cooperative in-storage processing for metagenomic analysis
GRAINS [ISCA’26] Storage-aware algorithm-architecture co-design for graph-based (meta)genomic analyses
GenStore [ASPLOS’22] In-storage filtering for genomic analysis
SAGe [HPCA’26] Algorithm-architecture co-design for storing and accessing sequence data
analyze genomic and metagenomic data inside the storage system
⓵
enable highly-compressed storage and high-performance access of large-scale sequence data
⓶

## Slide 63: Our Approach
Designing customized storage-centric systems that efficiently
MegIS [ISCA’24] Cooperative in-storage processing for metagenomic analysis
GRAINS [ISCA’26] Storage-aware algorithm-architecture co-design for graph-based (meta)genomic analyses
GenStore [ASPLOS’22] In-storage filtering for genomic analysis
SAGe [HPCA’26] Algorithm-architecture co-design for storing and accessing sequence data
analyze genomic and metagenomic data inside the storage system
⓵
enable highly-compressed storage and high-performance access of large-scale sequence data
⓶

## Slide 64
Prep
Analysis
Analysis
Analysis
Base.
Acc. Analysis
w/ Ideal Prep.
Prep
Prep
Lost Benefit due to Data Prep. Bottleneck
Execution Timeline (Not drawn to scale)
Acc. Analysis
Potential Benefit of Genome Analysis Acceleration
Baseline Analysis (446 KRead/s)
Accelerated Analysis (69200 KRead/s)
Baseline Prep. (2563 KRead/s)
Ideal Prep. (> 69200 KRead/s)
Recall: Effect of Data Preparation Bottleneck
GenStore
MegIS
GRAINS
SAGe
Notes: 2:10

## Slide 65: Mitigating Data Preparation Bottleneck
We need to effectively mitigate the data preparation bottleneck while meeting four key requirements:
Meeting all these requirements is challenging
High performance
High compression ratio
Low overhead
High energy efficiency
Even more challenging in genome analysis systems used
in hardware resource-constrained environments
GenStore
MegIS
GRAINS
SAGe
Notes: 2:50

## Slide 66: .
Genome Analysis
System
Request Data with SAGe’s Interface Commands
Send Prepared Data
in Desired Format
Receive Compressed Data
SAGe-Compressed Genomic Data
Operate w/ SAGe
Data Layout
Decompress & Reformat
SAGe HW
An algorithm-architecture co-design for highly-compressed storage and high-performance access of large-scale genomic sequence data
Key insight: Information encoded in genomic data follows specific properties We leverage these properties in our algorithm-architecture co-design
GenStore
MegIS
GRAINS
SAGe

## Slide 67: Case Studies of SAGe’s Hardware Integration
Due to its lightweight design, SAGe can seamlessly integrate with genome analysis systems
Genome Analysis ACC
SAGe HW
SSD
Genome Analysis ACC
SSD
Host System
SAGe HW
Host System
SSD
Host System
Genome Analysis ACC
SAGe HW
GenStore
MegIS
GRAINS
SAGe
Notes: 14

## Slide 68: Evaluation Methodology Overview (I)
Performance, Energy, and Power Analysis
Datasets: Read sets (RS)
From a variety of species (i.e., H. sapiens, T. cacao, M. acuminata malaccensis)
Sequenced with different sequencing technologies (i.e., Illumina and Oxford Nanopore Technologies)
End-to-end performance of a genome analysis application, which includes both data preparation and genome analysis
Hardware Components
Synthesized Verilog model for the hardware units
MQSim [Tavakkol+, FAST’18] for SSD’s internal operations
Ramulator [Kim+, CAL’15] for SSD’s internal DRAM
Software Components
Measure on a real system:
AMD® EPYC® host CPU with 128 physical cores
1.5 TB host DRAM
GenStore
MegIS
GRAINS
SAGe
Notes: We model performance, energy, and power of the systems based on the latency and throughput of each hardware-based and software-based component

## Slide 69: Recall: Case Studies of SAGe’s Hardware Integration
Due to its lightweight design, SAGe can seamlessly integrate with genome analysis systems
Genome Analysis ACC
SAGe HW
SSD
Genome Analysis ACC
SSD
Host System
SAGe HW
Host System
SSD
Host System
Genome Analysis ACC
SAGe HW
GenStore
MegIS
GRAINS
SAGe
Notes: 14

## Slide 70: Evaluation Methodology Overview (II)
Genome Analysis
A state-of-the-art hardware accelerator (GEM [Chen+, TPDS’23]), for read mapping
Near-data processing (NDP) baseline: GenStore [Mansouri Ghiasi+, ASPLOS’22]
  Alleviates the burden of moving and analyzing a large amount of low-reuse data
  Implemented in the resource-constrained environment of the SSD
SSD Controller
SSD’s
Internal
DRAM
⋯
Flash Cntrl.
Channel#N-1
Genome Analysis ACC
SSD
Flash Cntrl.
Channel#0
Genome Analysis ACC
GenStore
MegIS
GRAINS
SAGe

## Slide 71: Evaluation Methodology Overview (II)
Data Preparation
pigz: Commonly-used general-purpose software ([Adler, JPL’15])
(N)Spr: Genomics-specific software for short (Spring [Chandak, Bioinformatics’18]) and long reads (NanoSpring [Meng+, Scientific Reports’23])
(N)SprAcc: (N)Spring hardware-accelerated
0TimeDec: An idealized decompressor (with zero decompression time), but inefficient for integration in resource-constrained environments
SAGe: SAGe implemented as a standalone accelerator for data preparation
SAGeSSD: SAGe inside the SSD, for integration with the NDP analysis system
SSD Controller
SSD’s
Internal
DRAM
SAGe FTL
Metadata
⋯
Flash Cntrl.
Channel#N-1
Genome Analysis ACC
SAGe HW
Double-Reg.
SSD
Flash Cntrl.
Channel#0
Genome Analysis ACC
SAGe HW
Double-Reg.
GenStore
MegIS
GRAINS
SAGe
Notes: 14:30

## Slide 72: Speedup
Chart: 
| RS1 | RS2 | RS3 | RS4 | RS5 | GMean
pigz | 0.3207 | 0.22018 | 0.52661 | 0.42172 | 0.22321 | 0.32271
(N)Spr | 1 | 1 | 1 | 1 | 1 | 1
(N)SprAcc | 1.5353 | 1.2884 | 1.7302 | 1.086 | 1.0869 | 1.3221
SAGe | 4.8537 | 2.2779 | 28.5302 | 2.0725 | 1.5084 | 3.9699
0TimeDec | 4.8537 | 2.2779 | 28.5302 | 2.0725 | 1.5084 | 3.9699
SAGeSSD+NDP | 7.1782 | 10.3865 | 51.9319 | 2.0725 | 14.9719 | 10.3738
28.5
51.9
28.5
Speedup
15.0
3.9x
3.0x
12.3x
2.6x
SAGe provides significant speedup over both
general-purpose and genomics-specific baselines
SAGe achieves the same speedup as 0TimeDec
By efficiently integrating SAGeSSD with NDP SAGeSSD+NDP leads to large speedups
SAGeSSD+NDP
GenStore
MegIS
GRAINS
SAGe

## Slide 73: Reduction in Energy Consumption
  Normalized to (N)SprAcc (higher is better)
Chart: 
| RS1 | RS2 | RS3 | RS4 | RS5 | GMean
pigz | 0.25285 | 0.23041 | 0.38335 | 0.80657 | 0.45126 | 0.38195
(N)Spr | 0.67476 | 0.8028 | 0.57937 | 0.92535 | 0.92733 | 0.76922
SG | 9.3415 | 6.2919 | 45.2882 | 13.8158 | 10.0488 | 12.9878
Energy Reductuion
SAGe provides significant energy reduction over both
general-purpose and genomics-specific baselines
16.9x
34.0x
GenStore
MegIS
GRAINS
SAGe
SAGe

## Slide 74: Compression Ratio
2.9× better average compression ratio than general-purpose baseline
Comparable compression ratio to genomics-specific baseline (with a modest 4.6% average reduction)
GenStore
MegIS
GRAINS
SAGe

## Slide 75: Area and Power
Based on Synthesis of SAGe’s hardware units using the Synopsys Design Compiler @ 22nm technology node
Logic unit | # of instances | Area [mm2] | Power [mW]
Comparator | 1 per channel | 0.000045 | 0.014
Read Construction Unit | 1 per channel | 0.000017 | 0.023
Double Registers | 1 per channel | 0.00020 | 0.035
Control Unit | 1 per channel | 0.000029 | 0.025
Total for an 8-channel SSD | - | 0.002 | 0.77
SAGe’s hardware units consume small area and power
GenStore
MegIS
GRAINS
SAGe

## Slide 76: Our Approach
Designing customized storage-centric systems that efficiently
MegIS [ISCA’24] Cooperative in-storage processing for metagenomic analysis
GRAINS [ISCA’26] Storage-aware algorithm-architecture co-design for graph-based (meta)genomic analyses
GenStore [ASPLOS’22] In-storage filtering for genomic analysis
SAGe [HPCA’26] Algorithm-architecture co-design for storing and accessing sequence data
analyze genomic and metagenomic data inside the storage system
⓵
enable highly-compressed storage and high-performance access of large-scale sequence data
⓶

## Slide 77: Conclusion
analyze genomic and metagenomic data inside the storage system
⓵
By designing customized storage-centric systems that efficiently
enable highly-compressed storage and high-performance access of large-scale sequence data
we can alleviate the overheads of
computation
data movement
data preparation
SAGe
MegIS
GRAINS
GenStore
⓵
⓶
Notes: To conclude, in this thesis, we show that

## Slide 78: Putting It All Together
Performance
Energy Efficiency
Cost Effectiveness
Make accurate (meta)genomic analysis more accessible for wider adoption
Storage-Centric Systems for (Meta)Genomics

## Slide 79: More About My Research
https://nikamgh.github.io
Thesis Publications
Other Storage-Centric Computing Works
Memory-Centric Computing & Dense-3D Integration
Bioinformatics Algorithms
Algorithm-Architecture Co-design
Improving Storage & Memory System
Architecture for Health (Arch4Health) Initiative

## Slide 80: Storage-Centric System Designs for Enabling Fast, Efficient, and Low-Cost Genomic and Metagenomic Analyses
Nika Mansouri Ghiasi Onur Mutlu
Arch4Health @ ICS 2026
June 2026
Notes: Hi everyone, I am going to give you an overview of my thesis, titled “...”