## Slide 1: MegIS High-Performance, Energy-Efficient, and Low-Cost Metagenomic Analysis with In-Storage Processing
Nika Mansouri Ghiasi
Mohammed Alser Jisung Park Onur Mutlu
Mohammad Sadrosadati Harun Mustafa Arvid Gollwitzer Can Firtina
Julien Eudine Haiyu Mao Joël Lindegger Meryem Banu Cavlak
Notes: Hi everyone, I am Nika, and today, I will talk about
MegIS: High-Performance, Energy-Efficient, and Low-Cost Metagenomic Analysis with In-Storage Processing

## Slide 2: Outline
Conclusion
Background
Motivation and Goal
MegIS
Evaluation

## Slide 3: What is Metagenomics?
Metagenomics: Study of genome sequences of diverse organisms
within a shared environment (e.g., blood, ocean, soil)
Overcomes the limitations of traditional genomics
  Bypasses the need for culturing individual species in isolation
Notes: Metagenomics: Study of genome sequences of diverse organisms within a shared environment (e.g., blood, ocean, soil)
Metagenomics overcomes the limitations of traditional genomics
Because it bypasses the need for culturing individual species in isolation,
which is not feasible in many important clinical and environmental use cases

## Slide 4: What is Metagenomics?
Has led to groundbreaking advances
Precision medicine
Understanding microbial diversity of an environment
Discovering early warnings of communicable diseases
Metagenomics: Study of genome sequences of diverse organisms
within a shared environment (e.g., blood, ocean, soil)
Notes: Therefore, metagenomics has led to ground-breaking advances
In many fields such as
Precision medicine
Understanding microbial diversity of an environment
Discovering early warnings of communicable diseases

## Slide 5: Metagenomic Analysis
A large database
containing information
on many species
Metagenomic sample
with species that
are not known in advance
Preparation
of Input Queries
Query
K-mers
…
GCTCA
CTCAT
TCATG
Presence/Absence Identification
Abundance
Estimation
V. cholerae
E. coli
SARS-CoV-2
Chart: 
| Species#1 | Species#2 | Species#3
 | 0.6 | 0.25 | 0.15
(e.g., > 100 TBs in emerging databases)
Notes: Since the species that are present in a metagenomic sample are not known in advance,
Metagenomic analysis performs tasks to enable an understanding of the sample’s composition.
Here, I am going to start with showing the genomic sequences of the organisms in the metagenomic sample,
To perform metagenomic analysis
First, many tools extract k-mers (i.e., subsequences of length k) from the input queries in a sample
Second, they find species present/absent in the sample by searching the query k-mers against a large metagenomic database containing information on many species’ genomes.
Many databases used for various use cases can be very large, for example, to several TBs or more than a hundred TBs in emerging databases
This step outputs the IDs of the species that are identified to be present in the sample
Finally, some applications perform a third optional step of abundance estimatimation,
which calculates the relative frequencies of the occurrence of different species in the sample

## Slide 6: Outline
Conclusion
Background
Motivation and Goal
MegIS
Evaluation

## Slide 7: Motivation
Case study of the performance of metagenomic analysis tools
With various state-of-the-art SSD configurations
Normalized Throughput
Database Size (Terabyte)
I/O data movement causes significant performance overhead
Chart: 
| 0.7 | 1.4
No I/O | 1 | 1
Performance-Optimized | 0.31054 | 0.24299
Cost-Optimized | 0.03627 | 0.025496
3.2x
4.1x
27.6x
39.2x
Notes: We perform a case study on the throughput of metagenomic analysis tools
with various state-of-the-art cost-optimized or performance-optimized SSD configurations
And normalized throughput compared to a hypothetical configuration with zero performance overhead due to storage I/O
We observe that I/O data movement causes significant performance overhead

## Slide 8: Motivation
Case study on the throughput of metagenomic analysis tools
With Various state-of-the-art SSD configurations
Normalized Throughput
Database Size (Terabyte)
Chart: 
| 0.7 | 1.4
SSD-C | 0.03627 | 0.025496
SSD-P | 0.31054 | 0.24299
No-I/O | 1 | 1
I/O data movement causes significant performance overhead
Cost-Optimized
Performance-Optimized
No I/O
I/O becomes an even larger overhead (by 2.7x)
in systems where other bottlenecks are alleviated

## Slide 9: I/O Overhead is Hard to Avoid
I/O overhead due to accessing large, low-reuse data is hard to avoid
Sampling techniques to shrink database sizes
Keeping all data required by metagenomic analysis
completely and always resident in main memory
Reduce accuracy to levels unacceptable for many use cases
Energy inefficient, costly, unscalable, and unsustainable
Database sizes increase rapidly (doubling every few months)
Different analyses need different databases
Notes: I/O overhead from moving large, low-reuse data is hard to avoid
One might think it is possible to avoid this overhead by
using sampling techniques to shrink database sizes
However, this approach inevitably reduces accuracy to levels unacceptable for many use cases
Or another potential solution might seem to be
Keeping all data required by metagenomic analysis
completely and always resident in main memory
However, this is energy inefficient, costly, unscalable, and unsustainable due to two reasons
First, the sizes of metagenomic databases (which are already large, i.e., in some recent examples, exceeding a hundred terabytes) have been increasing rapidly.
For example, recent trends show the doubling of different important databases in only several months
Second, regardless of the sizes of individual databases, different analyses need different databases,
with information from different sets of genomes or with varying parameters.
Therefore, it is inefficient and unsustainable to maintain all data required by all possible analyses in main memory at all times

## Slide 10: Our Goal
Improve metagenomic analysis performance
by reducing large data movement overhead
from the storage system
in a cost-effective manner
Notes: Motivated by these points, Our Goal is to Improve metagenomic analysis performance
by reducing the large data movement overhead from the storage system in a cost-effective manner

## Slide 11: Challenges of In-Storage Processing
Existing metagenomic analysis approaches cannot be implemented as an in-storage processing system due to SSD hardware limitations
  Long latency of NAND flash chips
  Limited DRAM capacity inside the SSD
  Limited DRAM bandwidth inside the SSD
SSD DRAM
⋯
SSD
Controller
Cores
FTL
⋯
SSD
Cntrl
Cntrl
Channel#N
Channel#1
Notes: While In-Storage Processing (ISP) can be a promising direction to achieve our goal by processing data directly inside the storage device,
none of the existing approaches can be effectively implemented
as an ISP system due to limited hardware resources in the SSD such as
  Long latency of NAND flash chips
  Limited DRAM capacity inside the SSD
  And its limited bandwidth

## Slide 12: Outline
Conclusion
Background
Motivation and Goal
MegIS
Evaluation

## Slide 13: MegIS: Metagenomics In-Storage
First in-storage system for end-to-end metagenomic analysis
Idea: Cooperative in-storage processing for metagenomic analysis
  Hardware/software co-design between the storage system and host system
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Notes: Which is the first in-storage processing system for end-to-end metagenomic analysis
The key idea of megis is Cooperative ISP for metagenomics
Which is enabled by a synergistic hardware/software co-design between the storage system and the host system

## Slide 14: MegIS’s Steps
A large database
containing information
on many species
Metagenomic sample
with species that
are not known in advance
Preparation
of Input Queries
Query
K-mers
…
GCTCA
CTCAT
TCATG
Presence/Absence Identification
V. cholerae
E. coli
SARS-CoV-2
Abundance
Estimation
Chart: 
| Species#1 | Species#2 | Species#3
 | 0.6 | 0.25 | 0.15
Step 1
Step 2
Step 3

## Slide 15: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Notes: To (i) leverage and (ii) orchestrate the capabilities of both systems, megis includes hw/sw co-design in 5 directions

## Slide 16: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Step 1
Task partitioning and mapping
Each step executes
in its most suitable system
Step 2
Step 3

## Slide 17: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Step 1
Step 2
Step 3
Task partitioning and mapping
Each step executes
in its most suitable system

## Slide 18: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Storage-aware algorithms
Enable efficient
access patterns to the SSD
Step 1
Step 2
Step 3
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Task partitioning and mapping
Each step executes
in its most suitable system

## Slide 19: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
ACC
ACC
Cntrl
Cntrl
Channel#N
Channel#1
Lightweight in-storage accelerators
Minimize SRAM/DRAM buffer spaces needed inside the SSD
Step 1
Step 2
Step 3
Storage-aware algorithms
Enable efficient
access patterns to the SSD
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Task partitioning and mapping
Each step executes
in its most suitable system

## Slide 20: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
MegIS
FTL
MegIS
Metadata
Cntrl
Cntrl
Channel#N
Channel#1
Data mapping scheme and Flash Translation Layer (FTL)
Specialize to the characteristics of metagenomic analysis
Leverage the SSD’s full internal bandwidth
Step 1
Step 2
Step 3
Storage-aware algorithms
Enable efficient
access patterns to the SSD
Lightweight in-storage accelerators
Minimize SRAM/DRAM buffer spaces needed inside the SSD
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Task partitioning and mapping
Each step executes
in its most suitable system
ACC
ACC
Notes: 6 mins until here

## Slide 21: Step 1 Overview
A large database
containing information
on many species
Metagenomic sample
with species that
are not known in advance
Presence/Absence Identification
V. cholerae
E. coli
SARS-CoV-2
Abundance
Estimation
Chart: 
| Species#1 | Species#2 | Species#3
 | 0.6 | 0.25 | 0.15
Preparation
of Input Queries
Query
K-mers
…
GCTCA
CTCAT
TCATG
Step 1
Step 2
Step 3

## Slide 22: Step 1 Overview
MegIS works with sorted data structures
to avoid expensive random accesses to the SSD
  Extract k-mers from the sample
  Sort the k-mers (database is sorted offline)
Preparation
of Input Queries
Query
K-mers
…
GCTCA
CTCAT
TCATG
MegIS executes Step 1 in the host system
  Benefits from larger DRAM and more powerful computation
  Incurs fewer writes to NAND flash chips (than processing this step in the SSD)
  Enables overlapping Step 1 with Step 2
To execute Step 1 efficiently in the host system, MegIS needs to:
  Avoid significant overhead due to data transfer time between the steps
  Minimize performance and lifetime overheads even when host DRAM cannot hold all query k-mers
Notes: MegIS works with lexicographically-sorted data structures to avoid expensive random accesses to the SSD
Therefore, to prepare the input queries, MegIS 1) extracts k-mers from the sample,
2) sorts the k-mers
We execute this step in the host system for three reasons.
First, this step benefits from the relatively larger DRAM and more powerful computation resources in the host.
Second, due to the large host-side DRAM, performing this step in the host leads to significantly fewer writes to the flash chips
Third, by leveraging the host system for this step, we enable pipelining and overlapping Step 1 with Step 2 (which searches the large, low-reuse database).
To efficiently execute Step 1 on the host system, we need to ensure that
First, partitioning the application between the host and the SSD does not incur significant overheads due to data transfer time.
Second, minimize performance and lifetime overheads even when the host DRAM cannot hold all the extracted query k-mers

## Slide 23: Step 1 Design
Divide k-mers into independent partitions by their alphabetical range
  Can overlap operations on different partitions
Pin partitions to the host system or the SSD
  Avoid unnecessary movement of k-mers due to page swaps
Host DRAM
Host CPU
Read
Input Queries
ACGTTACGATT…
ACGTT
⋯
Query
K-mers
CGTTA
GTTAC
MegIS-Enabled SSD
Partition
A
ACGTC
ACTTT
ATGAT
⋯
⋯
C
CATTA
CTATG
CCGCA
⋯
G
GTTAC
GGTCC
GACAG
⋯
⋯
A
ACGTC
ACTTT
ATGAT
⋯
CATTA
CTATG
CCGCA
⋯
Overlap Step 1’s sorting
with Data transfer
and Step 2’s In-storage operations
Notes: To this end, we design an input processing scheme
That extracts k-mers from the sample and
divides the k-mers into independent partitions, each corresponding to an alphabetical range.
This enables overlapping the sorting on one partition with transfer and operations of its previous partitions.
Second, for scenarios where even host DRAM is not large enough to buffer all query k-mers,
the fact that these partitions are independent allows megis to pin some partitions to the host dram
and pin the others to the SSD. This way, megis can
avoid unnecessary movement of k-mers due to page swaps

## Slide 24: Step 2 Overview
A large database
containing information
on many species
Metagenomic sample
with species that
are not known in advance
Abundance
Estimation
Chart: 
| Species#1 | Species#2 | Species#3
 | 0.6 | 0.25 | 0.15
Preparation
of Input Queries
Query
K-mers
…
GCTCA
CTCAT
TCATG
Step 1
Presence/Absence Identification
V. cholerae
E. coli
SARS-CoV-2
Step 2
Step 3

## Slide 25: Step 2 Overview
  Identify the intersecting k-mers between the query k-mers
  and the database k-mers
  Retrieve the species IDs
  of intersecting k-mers
MegIS executes Step 2 in the SSD
  Accesses large data with low reuse
  Involves lightweight computation
To execute Step 2 efficiently in the SSD, MegIS needs to:
  Leverage internal bandwidth efficiently
  Not require expensive hardware inside the SSD
  (e.g., large DRAM bandwidth/capacity and costly logic units)
Presence/Absence Identification
V. cholerae
E. coli
SARS-CoV-2
Notes: In Step 2, MegIS finds the species present in the sample
by 1) Identifying the intersecting k-mers between the query k-mers and the database
and 2) Retrieve the taxonomic IDs of intersecting k-mers
We perform this step inside the SSD since it requires streaming the
large database with low reuse and involves only lightweight computation.
To efficiently execute this step in the SSD,
MegIS should leverage the full internal bandwidth without requiring expensive hardware resources inside the SSD
(e.g., large internal DRAM size/bandwidth and costly logic units).

## Slide 26: Identifying the Intersecting K-mers
Challenge: Limited internal DRAM bandwidth
SSD DRAM
SSD Controller
MegIS-Enabled
SSD
Channel#1
Channel#N
AAAAA
TAACC
CAAAA
AGTTT
TTGGT
CCGTG
⋯
⋯
⋯
⋯
Database K-mers
Query K-mers
from the Host
CGTCA
⋯
Intersection
⋯
AGTTT
Database K-mers
from Flash Chips
Notes: Relying solely on the SSD’s internal DRAM to buffer
Database k-mers that are stored in the NAND flash chips and accessed at full channel bandwidth,
and
query k-mers from the host system
and buffering the results
During in-storage processing and
can pressure the valuable internal DRAM bandwidth

## Slide 27: Identifying the Intersecting K-mers
Challenge: Limited internal DRAM bandwidth
SSD DRAM
SSD Controller
MegIS-Enabled
SSD
Channel#1
Channel#N
AAAAA
TAACC
CAAAA
AGTTT
TTGGT
CCGTG
⋯
⋯
⋯
⋯
Database K-mers
Query K-mers
from the Host
CGTCA
⋯
Intersect
Intersect
Buffer
Buffer
Compute directly on the flash data streams
Reduce buffer size based on application features
K-mer Register
K-mer Register
K-mer Register
K-mer Register
Write to DRAM
Intersection
[Zou+, MICRO’22]
Notes: <9.5 mins>
To address this challenge, we adopt an approach that
processes data directly from flash chips without buffering it in internal DRAM.
we utilize key features of MegIS to determine the minimum required buffer size.
This approach allows MegIS to compute directly on the flash data stream using only two registers, thus maintaining a low cost.
Finally, we write the intersecting K-mers to the SSD DRAM to be analyzed in the next step

## Slide 28: Retrieving the Species ID
Space-Inefficient
MegIS retrieves the species IDs of the intersecting k-mers by looking up a sketch database
K-mer | ID
AAAAA | 1
AAAAC | 6
AATCC | 2
… | …
Space-Efficient
Inefficient inside the SSD
due to long NAND flash latency
7.5x Smaller
2.1× Larger
K-mer Sketch Streaming
K-mer Sketch Streaming is much more suitable for in-storage processing
due to its streaming accesses
Notes: Storing this information for many species can be space-inefficient
Therefore,
some approaches provide data structures to encode the k-mer information in a space-efficient manner.
Despite the benefits, these approaches typically require many pointer-chasing operations for each lookup.
Performing these operations inside the SSD is challenging due to large latency of NAND flash chips
We provide an intermediate approach, K-mer Sketch Streaming that is optimized for in-storage processing
KSS leads to
significantly smaller data structures compared to the baseline tables
but is still larger compared to state-of-the-art compact structures
However, it is much more suitable for ISP due to its more efficient streaming accesses

## Slide 29: Retrieving the Species ID
Space-Inefficient
MegIS retrieves the species IDs of the intersecting k-mers by looking up a sketch database
K-mer | ID
AAAAA | 1
AAAAC | 6
AATCC | 2
… | …
Space-Efficient
Inefficient inside the SSD
due to long NAND flash latency
7.5x Smaller
2.1× Larger
K-mer Sketch Streaming
K-mer Sketch Streaming is much more suitable for in-storage processing
due to its streaming accesses
Design details are in the paper
Notes: Storing this information for many species can be space-inefficient
Therefore,
some approaches provide data structures to encode the k-mer information in a space-efficient manner.
Despite the benefits, these approaches typically require many pointer-chasing operations for each lookup.
Performing these operations inside the SSD is challenging due to large latency of NAND flash chips
We provide an intermediate approach, K-mer Sketch Streaming that is optimized for in-storage processing
KSS leads to
significantly smaller data structures compared to the baseline tables
but is still larger compared to state-of-the-art compact structures
However, it is much more suitable for ISP due to its more efficient streaming accesses

## Slide 30: Step 3
A large database
containing information
on many species
Metagenomic sample
with species that
are not known in advance
Preparation
of Input Queries
Query
K-mers
…
GCTCA
CTCAT
TCATG
Step 1
Presence/Absence Identification
V. cholerae
E. coli
SARS-CoV-2
Step 2
Abundance
Estimation
Chart: 
| Species#1 | Species#2 | Species#3
 | 0.6 | 0.25 | 0.15
Step 3
Step 3 and MegIS FTL are in the paper

## Slide 31: Outline
Conclusion
Background
Motivation and Goal
MegIS
Evaluation

## Slide 32: Evaluation: Methodology Overview
Performance, Energy, and Power Analysis
Baseline Comparison Points
Performance-optimized software, Kraken2 [Genome Biology’19]
Accuracy-optimized software, Metalign [Genome Biology’20]
PIM hardware-accelerated tool (using processing-in-memory), Sieve [ISCA’21]
SSD Configurations
SSD-C: with SATA3 interface (0.5 GB/s sequential read bandwidth)
SSD-P: with PCIe Gen4 interface (7 GB/s sequential read bandwidth)
Hardware Components
Synthesized Verilog model for the in-storage accelerators
MQSim [Tavakkol+, FAST’18] for SSD’s internal operations
Ramulator [Kim+, CAL’15] for SSD’s internal DRAM
Software Components
Measure on a real system:
AMD® EPYC® CPU with 128 physical cores
1-TB DRAM
Notes: We model performance, energy, and power of the systems based on the latency and throughput of each hardware-based and software-based component
We valuate the following baselines:
...
We evaluate these tools on systems with cost-optimized and performance-optimized SSD configurations

## Slide 33: Evaluation: Speedup over the Software Baselines
MegIS provides significant speedup over both
Performance-Optimized and Accuracy-Optimized baselines
Speedup
Performance-Optimized
MegIS
Accuracy-Optimized
Sample Genetic Diversity
Chart: 
| Low | Med | High | GMean
P-Opt | 1 | 1 | 1 | 1
A-Opt | 0.43101 | 0.38921 | 0.35039 | 0.38881
MS | 5.3489 | 5.6406 | 6.3871 | 5.7761
SSD-C
5.8x
14.9x
Chart: 
| Low | Med | High | GMean
P-Opt | 1 | 1 | 1 | 1
A-Opt | 0.43101 | 0.38921 | 0.35039 | 0.38881
MS | 5.3489 | 5.6406 | 6.3871 | 5.7761
SSD-C
5.8x
Sample Genetic Diversity
14.9x
Notes: We analyze the benefits of MegIS for samples with low, medium, and high genetic diversity,
And here I am showing for a cost optimized-SSD
We observe that compared to both P-Opt and A-Opt
MegIS provides significant speedups

## Slide 34: Evaluation: Speedup over the Software Baselines
MegIS provides significant speedup over both
Performance-Optimized and Accuracy-Optimized baselines
Speedup
Performance-Optimized
MegIS
Accuracy-Optimized
Sample Genetic Diversity
Chart: 
| Low | Med | High | GMean
P-Opt | 1 | 1 | 1 | 1
A-Opt | 0.3836 | 0.29101 | 0.31974 | 0.32925
MS | 2.6617 | 3.6664 | 6.5218 | 3.9926
SSD-P
4.0x
12.1x
MegIS improves performance on both
cost-optimized and performance-optimized SSDs

## Slide 35: Evaluation: Speedup over the PIM Baseline
4.9x
Chart: 
| Low | Med | High | GMean
 | 1 | 1 | 1 | 1
 | 4.8422 | 4.8446 | 5.0596 | 4.9144
Chart: 
| Low | Med | High | GMean
 | 1 | 1 | 1 | 1
 | 1.462 | 1.7798 | 2.7359 | 1.9237
Speedup
SSD-C
PIM
MegIS
1.9x
SSD-P
Sample Genetic Diversity
Sample Genetic Diversity
PIM
MegIS
MegIS provides significant speedup over the PIM baseline
Notes: Similarly, we evaluate megis compared to the pim baseline
and show that on systems with cost-optimized
and performance-optimized ssds,
MegiS significantly outperforms the PIM baseline

## Slide 36: Evaluation: Reduction in Energy Consumption
On average across different input sets and SSDs
Chart: 
| Perf-Opt | Acc-Opt | PIM | MegIS
 | 1 | 0.35526 | 2.8421 | 5.4
GeoMean Energy Reduction
(Higher is Better)
MegIS provides significant energy reduction over
the Performance-Optimized, Accuracy-Optimized, and PIM baselines
5.4x
15.2x
1.9x
Notes: Next, we show megis's energy reduction on average accross different input sets and SSDs and observe that megis provides...

## Slide 37: Evaluation: Accuracy, Area, and Power
Accuracy
Same accuracy as the accuracy-optimized baseline
Significantly higher accuracy than the performance-optimized and PIM baselines
  4.6 – 5.2× higher F1 scores
  3 – 24% lower L1 norm error
Area and Power
Total for an 8-channel SSD:
Area: 0.04 mm2 (Only 1.7% of the area of three ARM Cortex R4 cores in an SSD controller)
Power: 7.658 mW
Notes: MegIS provides all these benefits while achieving high accuracy

## Slide 38: Evaluation: System Cost-Efficiency
GMean Speedup
Chart: 
| Perf-Opt ($) | Acc-Opt ($) | Perf-Opt($$$) | Acc-Opt ($$$) | MegIS ($)
 | 1 | 0.81324 | 6.8304 | 2.2454 | 16.1756
Cost-optimized system ($): With SSD-C and 64-GB DRAM
Performance-optimized system ($$$): With SSD-P and 1-TB DRAM
MegIS outperforms the baselines
even when running on a much less costly system
($)
($)
($$$)
($$$)
($)
7.2x
2.4x
Notes: Self-note (copy from arxiv version): For the performance-optimized system, we calculate the cost of 1TB
DRAM to be roughly 7080 USD (8 x 128GB modules [230]) and the cost of
SSD-P to be roughly 875 USD. For the performance-optimized system, we calculate
the cost of 64GB DRAM to be roughly 312 USD (8 x 8GB modules [231],
assuming the same number of memory channels as the performance-optimized
system) and the cost of SSD-C to be roughly 346 USD. Note that the cost of
the total storage system depends not only on the price of each SSD but also on
the available interconnection slots in the systems, as systems typically have
fewer PCIe slots (needed for SSD-P) than SATA slots (needed for SSD-C).

## Slide 39: Evaluation: System Cost-Efficiency
GMean Speedup
Chart: 
| Perf-Opt ($) | Acc-Opt ($) | Perf-Opt($$$) | Acc-Opt ($$$) | MegIS ($)
 | 1 | 0.81324 | 6.8304 | 2.2454 | 16.1756
Cost-optimized system ($): With SSD-C and 64-GB DRAM
Performance-optimized system ($$$): With SSD-P and 1-TB DRAM
MegIS outperforms the baselines
even when running on a much less costly system
($)
($)
($$$)
($$$)
($)
7.2x
2.4x
MegIS improves system cost-efficiency
and makes metagenomics more accessible
for wider adoption
Notes: Self-note (copy from arxiv version): For the performance-optimized system, we calculate the cost of 1TB
DRAM to be roughly 7080 USD (8 x 128GB modules [230]) and the cost of
SSD-P to be roughly 875 USD. For the performance-optimized system, we calculate
the cost of 64GB DRAM to be roughly 312 USD (8 x 8GB modules [231],
assuming the same number of memory channels as the performance-optimized
system) and the cost of SSD-C to be roughly 346 USD. Note that the cost of
the total storage system depends not only on the price of each SSD but also on
the available interconnection slots in the systems, as systems typically have
fewer PCIe slots (needed for SSD-P) than SATA slots (needed for SSD-C).

## Slide 40: More in the Paper
MegIS’s performance when running in-storage processing operations on the cores existing in the SSD controller
MegIS’s performance when using the same accelerators outside SSD
Sensitivity analysis with varying
  Database sizes
  Memory capacities
  #SSDs
  #Channels
  #Samples
MegIS’s performance for abundance estimation
Notes: Let me briefly talk about other results that are included in the paper before concluding this talk. These include the following:

## Slide 41: More in the Paper
MegIS’s performance with the cores in the SSD controller
MegIS’s performance outside SSD
Sensitivity analysis with varying
  Database sizes
  Memory capacities
  #SSDs
  #Channels
  #Samples
MegIS’s performance for abundance estimation
https://arxiv.org/abs/2406.19113

## Slide 42: Outline
Conclusion
Background
Motivation and Goal
MegIS
Evaluation

## Slide 43: Conclusion
Metagenomic analysis suffers from
significant storage I/O data movement overhead
The first in-storage processing system for end-to-end metagenomic analysis
Leverages and orchestrates processing inside and outside the storage system
MegIS
Improves performance
2.7×–37.2× over performance-optimized software
6.9×–100.2× over accuracy-optimized software
1.5×–5.1× over hardware-accelerated PIM baseline
Low area overhead
1.7% of the three cores
in an SSD controller
Reduces energy consumption
5.4× over performance-optimized software
15.2× over accuracy-optimized software
1.9× over hardware-accelerated PIM baseline
High accuracy
Same as accuracy-optimized
4.8× higher F1 scores
over performance-optimized/PIM

## Slide 44: MegIS High-Performance, Energy-Efficient, and Low-Cost Metagenomic Analysis with In-Storage Processing
Nika Mansouri Ghiasi
Mohammed Alser Jisung Park Onur Mutlu
Mohammad Sadrosadati Harun Mustafa Arvid Gollwitzer Can Firtina
Julien Eudine Haiyu Mao Joël Lindegger Meryem Banu Cavlak
Notes: Hi everyone, I am Nika, and today, I will talk about
MegIS: High-Performance, Energy-Efficient, and Low-Cost Metagenomic Analysis with In-Storage Processing

## Slide 45
Backup Slides
Notes: Hi everyone, I am Nika, and today, I will talk about
MegIS: High-Performance, Energy-Efficient, and Low-Cost Metagenomic Analysis with In-Storage Processing
12 mins
1 min conclusion
3 mins results
4 mins mech
+ 2 mins motivation
+ 2 mins background

## Slide 46: Executive Summary (I suggest not to present it due to time limits)
Problem: Metagenomic analysis suffers from significant storage I/O data movement overhead
Goal: Improve metagenomic analysis performance by reducing storage I/O data movement overhead in a cost-effective manner
Challenge: While in-storage processing can be a promising direction, existing metagenomic analysis approaches cannot be implemented in the SSD due to SSD hardware limitations
Idea: Cooperative ISP for metagenomics
Capitalize on the strengths of processing both inside and outside the storage system
MegIS: The first in-storage processing system for end-to-end metagenomic analysis pipeline
An efficient pipeline between the SSD and the host system to (i) leverage and(ii) orchestrate the capabilities of both via
  Task partitioning and mapping
  Data/computation flow coordination
  Storage-aware algorithms
  Lightweight in-storage accelerators
  Specialized data mapping scheme and Flash Translation Layer (FTL)
Results: Significant speedup (1.5x – 100.2x) and energy reduction (1.9x – 25.7x) with high accuracy and at low cost

## Slide 47: Step 2.2: Retrieving Tax IDs
KSS example when retrieving 5- and 4-mers
SSD Controller
Intersection
Curr. Register
MegIS-
Enabled
SSD
Channel#1
Channel#2
Internal
DRAM
5-mer | 5-mer ID
AAAAA | 1
AAAAC | 6
AATCC | 2
… | …
4-mer ID
-
3
…
AGTTT
⋯
AAAAC
Next Register
AATCC
❶ Intersect 5-mers
6
2
Curr. Register
Next Register
Intersect
Intersect

## Slide 48: Step 2.2: Retrieving Tax IDs
KSS example when retrieving 5- and 4-mers
SSD Controller
Intersection
Curr. Register
MegIS-
Enabled
SSD
Channel#1
Channel#2
Internal
DRAM
5-mer | 5-mer ID
AAAAA | 1
AAAAC | 6
AATCC | 2
… | …
4-mer ID
-
3
…
AGTTT
⋯
Idx.
Gen
AAAAC
Next Register
AATCC
Move to
Next 4-mer
❶ Intersect 5-mers
❷ Intersect 4-mers
6
2
Curr. Register
AAAA
Next Register
AATC
-
3
AATC
Intersect
Intersect
❸ Send Tax IDs

## Slide 49: Area and Power
Based on synthesis of MegIS accelerators using the Synopsys Design Compiler @ 65nm technology node
Only 1.7% of the area of three 28-nm ARM Cortex R4 cores
in a SATA SSD controller
Logic Unit | # of instances | Area [mm2] | Power [mW]
Intersect (120-bit) | 1 per channel | 0.001361 | 0.284
k-mer Registers (2 x 120-bit) | 1 per channel | 0.002821 | 0.645
Index Generator (64-bit) | 1 per channel | 0.000272 | 0.025
Control Unit | 1 per SSD | 0.000188 | 0.026
Total for an 8-channel SSD | - | 0.04 | 7.658
Notes: We find area and power values of MegIS by synthesizing MegIS using 65nm technology node,
And find that for an 8-channel SSD, the area of GS is 0.04 mm square and the power is 7.6 watts
BY scaling the area to lower technology nodes, we observe that the area overhead of MegIS is only 1.7% of the of the three ARM processors in a SATA SSD controller.