## Slide 1
A Lightweight Algorithm-Architecture Co-Design for Mitigating the Data Preparation Bottleneck in Large-Scale Genome Sequence Analysis
Nika Mansouri Ghiasi
Mohammad Sadrosadati Jisung Park Onur Mutlu
Talu Güloglu Harun Mustafa Can Firtina Konstantina Koliogeorgi
Konstantinos Kanellopoulos Haiyu Mao Rakesh Nadig

## Slide 2: Applications of Genome Sequence Analysis
Precision Medicine
Outbreak Prevention and Management
Agriculture
Scientific Discovery
& Many More…
Notes: 0:30

## Slide 3: DNA Under Electron Microscope
human chromosome #12
from a HeLa cell

## Slide 4: Digital Format for Analysis
CCTCCTCAGTGCCACCCAGCCCACTGGCAGCTCCCAAACAGGCTCTTATTAAAACACCCTGTTCCCTGCCCCTTGGAGTGAGGTGTCAAGGACCTAAACTAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTGCTAAACAGCACTTTTTTGACCATTATTTTGGATCTGAAAGAAATCAAGAATAAATGAAGGACTTGATACATTGGAAGAGGAGAGTCAAGGACCTACAGAAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTATGTCAAGGACCTAATGTCTGTGTTGCAGGTCTTCTTGCATCTTCCCTGTC

## Slide 5: High-Throughput Sequencers
… and more! All produce data with different properties.
Illumina MiSeq
Pacific Biosciences RS II
Illumina NovaSeq 6000
Oxford
Nanopore GridION
Pacific
Biosciences
Sequel II
Oxford
Nanopore
PromethION
Oxford Nanopore MinION

## Slide 6: High-Throughput Sequencers
… and more! All produce data with different properties.
Illumina MiSeq
Oxford Nanopore MinION
Pacific Biosciences RS II
Illumina NovaSeq 6000
Oxford
Nanopore SmidgION
Pacific
Biosciences
Sequel II
Oxford
Nanopore
PromethION
Current sequencing technologies
cannot sequence very long DNA molecules end-to-end
Instead, they extract smaller fragments of the original DNA sequence, known as reads
AAGCTTCCATGG
AAATGGGCTTTC
GCCCAAATGGTT
GCTTCCAGAATG
Notes: 1:10

## Slide 7: Genomic Data is Growing at a Fast Pace
Important Role in Many Fields
Significant Drop in Sequencing Cost
Fast growth in genomic data size
Chart: Year
Public Genomic Sequence Reads Data Size in Sequence Read Archive (SRA) Over Years
260.3x

## Slide 8: Large Efforts in Handling Fast-Growing Genomic Data
Store Genome Sequence Data in Highly-Compressed Formats
Accelerate Genome Sequence Analysis

## Slide 9: Data Preparation Bottleneck
Store Genome Sequence Data in Highly-Compressed Formats
Accelerate Genome Sequence Analysis
Genomic data is decompressed and formatted first before an accelerator can operate on it
Notes: 1:24

## Slide 10: Effect of the Data Preparation Bottleneck
Prep
Analysis
Analysis
Analysis
Base.
Acc. Analysis
w/ Ideal Prep.
Prep
Prep
Lost Benefit due to Data Prep. Bottleneck
Execution Timeline (Not drawn to scale)
Acc. Analysis
Potential Benefit of Genome Analysis Acceleration
Baseline Analysis (446 KRead/s)
Accelerated Analysis (69200 KRead/s)
Baseline Prep. (2563 KRead/s)
Ideal Prep. (> 69200 KRead/s)
Notes: 2:10

## Slide 11: Mitigating Data Preparation Bottleneck
We need to effectively mitigate the data preparation bottleneck while meeting four key requirements:
Meeting all these requirements is challenging
High performance
High compression ratio
Low overhead
High energy efficiency
Even more challenging in genome analysis systems used
in hardware resource-constrained environments
Notes: 2:50

## Slide 12: .
An algorithm-architecture co-design for highly-compressed storage and high-performance access of large-scale genomic sequence data
Key insight: information encoded in genomic data follows specific properties
We leverage these properties to co-design
  A lossless (de)compression algorithm
  Hardware for decompression with lightweight operations
  Storage data layout & Interface commands to access data
Higher performance (by 3.0×–32.1×)
High compression ratio
Low overhead
Higher energy efficiency (by 13.0×–34.0x)
Notes: 3:30

## Slide 13: Outline
Background
Motivation and Goal
SAGe
Evaluation
Conclusion

## Slide 14: Genomics-Specific Compression
Consensus
Sequence
ATACGTAGAAAAAGT
AGCAAATGTACGATG
TCGATGCTTGCATAA
CATAAGTCGATAGTT
ATACGTAGAAAAAGTCGATGCTTGCATAAGTCGATAGTT…
Read Set (A set of reads from a sample)
AAAAAGTCGATGCTT
…
Mismatch
Information
Notes: A genomic-specific compressor instead of storing reads, first stores a consensus sequence, which is
an approximation of the organism’s genome and stores the mismatch information of those reads in relation to the consensus

## Slide 15: Genomics-Specific Compression
Consensus
Sequence
ATACGTAGAAAAAGT
TCGATGCTTGCATAA
CATAAGTCGATAGTT
ATACGTAGAAAAAGTCGATGCTTGCATAAGTCGATAGTT…
Read Set (A set of reads from a sample)
AAAAAGTCGATGCTT
…
AGCAAATGTACGATG
Mismatch
Information
Notes: and, To do so, it first needs to map reads to the location they match in the consensus sequence.

## Slide 16: Genomics-Specific Compression
Consensus
Sequence
ATACGTAGAAAAAGT
AGCAAATGTACGATG
TCGATGCTTGCATAA
CATAAGTCGATAGTT
ATACGTAGAAAAAGTCGATGCTTGCATAAGTCGATAGTT…
Read Set (A set of reads from a sample)
AAAAAGTCGATGCTT
…
Mismatch
Information
Compressed with General-Purpose Compression Techniques
Matching Pos.
Mismatch Pos.
Mismatch Char.
Mismatch Type
Read N
7
+2, +4, +3
C, T, A
Subs, Subs, Ins
…
…
…
…
…
…
…
…
…
…
Notes: Now, let me give more details about the mismatch information using the example of this read ... Since these compressors use a consensus sequence, they better capture the inherent redundancy present in genomic data

## Slide 17: Genomics-Specific Compression
Consensus
Sequence
ATACGTAGAAAAAGT
AGCAAATGTACGATG
TCGATGCTTGCATAA
CATAAGTCGATAGTT
ATACGTAGAAAAAGTCGATGCTTGCATAAGTCGATAGTT…
Read Set (A set of reads from a sample)
AAAAAGTCGATGCTT
…
Mismatch
Information
Compressed with Back-End General-Purpose Compressors
Matching Pos.
Mismatch Pos.
Mismatch Base
Mismatch Type
Read N
7
+2, +3, +2
C, T, A
Sub, Sub, Ins
…
…
…
…
…
…
…
…
…
…
Genomics-specific compressors attain higher compression ratio (e.g., typically from ∼2 to ∼40) than general-purpose compressors (e.g., typically from ∼2 to ∼6)
Notes: 5

## Slide 18: Outline
Motivation and Goal
Background
SAGe
Evaluation
Conclusion

## Slide 19: Effect of the Data Preparation Bottleneck
Prep
Analysis
Analysis
Analysis
Base.
Acc. Analysis
w/ Ideal Prep.
Prep
Prep
Lost Benefit due to Data Prep. Bottleneck
Execution Timeline (Not drawn to scale)
Acc. Analysis
Potential Benefit of Genome Analysis Acceleration
Baseline Analysis (446 KRead/s)
Accelerated Analysis (69200 KRead/s)
Baseline Prep. (2563 KRead/s)
Ideal Prep. (> 69200 KRead/s)

## Slide 20: Data Preparation Bottleneck
End-to-end performance of a genome analysis application, which includes both data preparation and genome analysis
  Genome Analysis: GEM [Chen+, IEEE TPDS’23], a state-of-the-art hardware accelerator for read mapping (a fundamental task in genome analysis)
Chart: 
| RS1 | RS2 | RS3 | RS4 | RS5 | GMean
General-Purpose | 0.3207 | 0.22018 | 0.52661 | 0.42172 | 0.22321 | 0.32271
Genomics-Specific | 1 | 1 | 1 | 1 | 1 | 1
Ideal | 4.8537 | 2.2779 | 28.5302 | 2.0725 | 1.5084 | 3.9699
Normalized Throughput
28.5x
Data preparation greatly limits end-to-end performance
Read Set
Notes: 6min

## Slide 21: Challenges
Mitigating the data preparation bottleneck is challenging when aiming to achieve high performance, energy efficiency, high compression ratio, & low overhead
This is because prior approaches rely on
    Expensive computational units
    Large buffers, or large DRAM bandwidth or capacity
This challenge is exacerbated in genome analysis systems used in hardware resource-constrained environments
Portable Systems
Near-Data Processing Systems (e.g., in Main Memory or Storage System)
Notes: Which are needed due to many random accesses to large data structures for matching patterns

## Slide 22: Our Goal
Effectively mitigate the data preparation bottleneck, while meeting four key requirements:
High performance
Energy efficiency
High compression ratio
Low overhead
Notes: 6:45

## Slide 23: Outline
SAGe
Background
Motivation and Gaol
Evaluation
Conclusion

## Slide 24: .
Genome Analysis
System
Request Data with SAGe’s Interface Commands
Send Prepared Data
in Desired Format
Receive Compressed Data
SAGe-Compressed Genomic Data
Operate w/ SAGe
Data Layout
Decompress & Reformat
SAGe HW
An algorithm-architecture co-design for highly-compressed storage and high-performance access of large-scale genomic sequence data
Key insight: information encoded in genomic data follows specific properties We leverage these properties in our algorithm-architecture co-design

## Slide 25: SAGe’s Algorithm Architecture Co-Design
Genome Analysis
System
Request Data with SAGe’s Interface Commands
Send Prepared Data
in Desired Format
Receive Compressed Data
SAGe-Compressed Genomic Data
Operate w/ SAGe
Data Layout
Decompress & Reformat
SAGe HW
Notes: 7:30

## Slide 26: SAGe’s Algorithm Architecture Co-Design
Genome Analysis
System
Request Data with SAGe’s Interface Commands
Send Prepared Data
in Desired Format
Receive Compressed Data
SAGe-Compressed Genomic Data
Operate w/ SAGe
Data Layout
Decompress & Reformat
SAGe HW

## Slide 27: Compression Algorithm and Data Structures
Consensus
Sequence
ATACGTAGAAAAAGTCGATGCTTGCATAAGTCGATAGTT…
Mismatch
Information
Mismatch Pos.
Read 1
1, 0, 9
…
…
Read 2
Matching Pos.
7
…
10
1, 1, 0
Mismatch Base
C, T, A
…
A, T, T
Mismatch Type
Subs, Subs, Ins
…
Ins, Subs, Ins

## Slide 28: Compression Algorithm and Data Structures
Consensus
Sequence
ATACGTAGAAAAAGTCGATGCTTGCATAAGTCGATAGTT…
Sequentially Encode Mismatch Information in Lightweight Structures
Tune the Bit Counts Based on Read Set Properties
1 | 0 | 1001 | 1 | 1 | 0 | …
0 | 0 | 1 | 0 | 0 | 0 | …
Mismatch Pos. Array
Mismatch Pos. Guide Array
⓶
⓵
Mismatch
Information
Mismatch Pos.
Read 1
1, 0, 9
…
…
Read 2
Matching Pos.
7
…
10
1, 1, 0
Mismatch Base
C, T, A
…
A, T, T
Mismatch Type
Subs, Subs, Ins
…
Ins, Subs, Ins
0001 | 0000 | 1001 | 0001 | 0001 | 0000 | …
1 0 9
1 1 0
Indicates 1 bit
Indicates 4 bits
Notes: 8:30

## Slide 29: Compression Algorithm and Data Structures
Consensus
Sequence
ATACGTAGAAAAAGTCGATGCTTGCATAAGTCGATAGTT…
Sequentially Encode Mismatch Information in Lightweight Structures
Tune the Bit Counts Based on Read Set Properties
1 | 0 | 1001 | 1 | 1 | 0 | …
0 | 0 | 1 | 0 | 0 | 0 | …
Mismatch Pos. Array
Mismatch Pos. Guide Array
⓶
⓵
Mismatch
Information
Mismatch Pos.
Read 1
1, 0, 9
…
…
Read 2
Matching Pos.
7
…
10
1, 1, 0
Mismatch Base
C, T, A
…
A, T, T
Mismatch Type
Subs, Subs, Ins
…
Ins, Subs, Ins
0001 | 0000 | 1001 | 0001 | 0001 | 0000 | …
1 0 9
1 1 0
Indicates 1 bit
Indicates 4 bits
This is effective since the mismatch information in genomic datasets tends to follow specific properties
and by using a limited set of bit widths tailored to these properties, SAGe significantly reduces data size

## Slide 30: Example Properties of Mismatch Information
Chart: 
 | 23.9014 | 16.7779 | 11.6254 | 7.1821 | 7.3742 | 8.391 | 8.6975 | 7.778 | 5.413 | 2.3223 | 0.49269 | 0.043227 | 0.0011892 | 0 | 0
% of Mismatch
Positions
Needed #Bits
Most mismatch positions
need only a few bits to store
Based on the information encoded in histograms of each read set,
SAGe systematically searches for the best bit-counts for arrays and guide arrays
that minimize the total encoded size for that specific read set
Notes: This is due to two main factors that can lead to spatially nearby mismatches.
First, genetic mutations tend to cluster in some regions of the genome [291–293].
Second, a regional degradation in sequencing quality can cause clusters of incorrect bases in the read [294–296].

## Slide 31: Example Properties of Mismatch Information
Chart: 
 | 23.9014 | 16.7779 | 11.6254 | 7.1821 | 7.3742 | 8.391 | 8.6975 | 7.778 | 5.413 | 2.3223 | 0.49269 | 0.043227 | 0.0011892 | 0 | 0
% of Mismatch
Positions
Most delta-encoded mismatch positions
need only a few bits to store
Observations regarding properties of other parts of the mismatch information are in the paper
Based on the information encoded in histograms of each read set,
SAGe systematically searches for the best bit-counts for arrays and guide arrays
that minimize the total encoded size for that specific read set
Notes: 10:15 9:30

## Slide 32: Example Walkthrough of Decompression
111010101100101010…
Mismatch Pos. Array
00111011000110…
Mismatch Pos. Guide Array
Encoding of Guide Array Entry | #Bits for Array Entry
0 | 2
10 | 4
110 | 8
Association Table
Read#1 Mismatch Count (Fixed width)

## Slide 33: Example Walkthrough of Decompression
111010101100101010…
Mismatch Pos. Array
00111011000110…
Mismatch Pos. Guide Array
Encoding of Guide Array Entry | #Bits for Array Entry
0 | 2
10 | 4
110 | 8
Association Table
Read#1 Mismatch Count (Fixed width)
10
4
110
8
0
2
Read#2 Mismatch Count (Fixed width)
Sequential Scan
Notes: 11

## Slide 34: SAGe’s Algorithm Architecture Co-Design
Genome Analysis
System
Request Data with SAGe’s Interface Commands
Send Prepared Data
in Desired Format
Receive Compressed Data
SAGe-Compressed Genomic Data
Operate w/ SAGe
Data Layout
Decompress & Reformat
SAGe HW

## Slide 35: Hardware for Data Preparation
Decompressed
and Formatted Reads
Genome Analysis System
Scan Unit (SU)
Read Construction Unit (RCU)
Control Unit (CU)
Config. Registers
Position Arrays
Position Guide Arrays
Array Config. Parameters
Array Registers
Scan Logic
Consensus Sequence
Construction
Logic
Consensus
Sequence Register
Guide Array Registers

## Slide 36: Hardware for Data Preparation
Decompressed
and Formatted Reads
Genome Analysis System
Scan Unit (SU)
Read Construction Unit (RCU)
Control Unit (CU)
Config. Registers
Position Arrays
Position Guide Arrays
Array Config. Parameters
Array Registers
Scan Logic
Consensus Sequence
Construction
Logic
Consensus
Sequence Register
Guide Array Registers
SAGe’s hardware units decompress and reformat data into the desired format using lightweight operations and streaming accesses
Notes: 12:30

## Slide 37: Case Studies of SAGe’s Hardware Integration
Due to its lightweight design, SAGe can seamlessly integrate with genome analysis systems
Genome Analysis ACC
SAGe HW
SSD
Genome Analysis ACC
SSD
Host System
SAGe HW
Host System
SSD
Host System
Genome Analysis ACC
SAGe HW
Notes: 14

## Slide 38: SAGe’s Algorithm Architecture Co-Design
Genome Analysis
System
Request Data with SAGe’s Interface Commands
Send Prepared Data
in Desired Format
Receive Compressed Data
SAGe-Compressed Genomic Data
Operate w/ SAGe
Data Layout
Decompress & Reformat
SAGe HW
Details in the paper

## Slide 39: More in the Paper
https://arxiv.org/abs/2504.03732

## Slide 40: Outline
Evaluation
Background
Motivation and Gaol
SAGe
Conclusion

## Slide 41: Evaluation Methodology Overview (I)
Performance, Energy, and Power Analysis
Datasets: Read sets (RS)
From a variety of species (i.e., H. sapiens, T. cacao, M. acuminata malaccensis)
Sequenced with different sequencing technologies (i.e., Illumina and Oxford Nanopore Technologies)
End-to-end performance of a genome analysis application, which includes both data preparation and genome analysis
Hardware Components
Synthesized Verilog model for the hardware units
MQSim [Tavakkol+, FAST’18] for SSD’s internal operations
Ramulator [Kim+, CAL’15] for SSD’s internal DRAM
Software Components
Measure on a real system:
AMD® EPYC® CPU with 128 physical cores
1 TB DRAM
Notes: We model performance, energy, and power of the systems based on the latency and throughput of each hardware-based and software-based component

## Slide 42: Recall: Case Studies of SAGe’s Hardware Integration
Due to its lightweight design, SAGe can seamlessly integrate with genome analysis systems
Genome Analysis ACC
SAGe HW
SSD
Genome Analysis ACC
SSD
Host System
SAGe HW
Host System
SSD
Host System
Genome Analysis ACC
SAGe HW
Notes: 14

## Slide 43: Evaluation Methodology Overview (II)
Genome Analysis
A state-of-the-art hardware accelerator (GEM [Chen+, TPDS’23]), for read mapping
A state-of-the-art NDP accelerator (GenStore [Mansouri Ghiasi+, ASPLOS’22])
  Filters reads that do not require expensive computation in the SSD  Alleviates the burden of moving and analyzing a large amount of low-reuse data from the rest of the system
  Implemented in the resource-constrained environment of the SSD
SSD Controller
SSD’s
Internal
DRAM
⋯
Flash Cntrl.
Channel#N-1
Genome Analysis ACC
SSD
Flash Cntrl.
Channel#0
Genome Analysis ACC

## Slide 44: Evaluation Methodology Overview (II)
Data Preparation
pigz: Commonly-used general-purpose software ([Adler, JPL’15])
(N)Spr: Genomics-specific software for short (Spring [Chandak, Bioinformatics’18]) and long reads (NanoSpring [Meng+, Scientific Reports’23])
(N)SprAcc: (N)Spring hardware-accelerated
0TimeDec: an idealized decompressor (with zero decompression time), but inefficient for integration in resource-constrained environments
SAGe: SAGe implemented as an standalone accelerator for data preparation
SAGeSSD: SAGe inside the SSD, for integration with the NDP analysis system
SSD Controller
SSD’s
Internal
DRAM
SAGe FTL
Metadata
⋯
Flash Cntrl.
Channel#N-1
Genome Analysis ACC
SAGe HW
Double-Reg.
SSD
Flash Cntrl.
Channel#0
Genome Analysis ACC
SAGe HW
Double-Reg.
Notes: 14:30

## Slide 45: Speedup
Chart: 
| RS1 | RS2 | RS3 | RS4 | RS5 | GMean
pigz | 0.3207 | 0.22018 | 0.52661 | 0.42172 | 0.22321 | 0.32271
(N)Spr | 1 | 1 | 1 | 1 | 1 | 1
(N)SprAcc | 1.5353 | 1.2884 | 1.7302 | 1.086 | 1.0869 | 1.3221
SAGe | 4.8537 | 2.2779 | 28.5302 | 2.0725 | 1.5084 | 3.9699
0TimeDec | 4.8537 | 2.2779 | 28.5302 | 2.0725 | 1.5084 | 3.9699
SAGeSSD+NDP | 7.1782 | 10.3865 | 51.9319 | 2.0725 | 14.9719 | 10.3738
28.5
51.9
28.5
Speedup
15.0
3.9x
3.0x
12.3x
2.6x
SAGe provides significant speedup over both
general-purpose and genomics-specific baselines
SAGe achieves the same speedup as 0TimeDec
By efficiently integrating SAGeSSD with NDP SAGeSSD+NDP leads to large speedups
SAGeSSD+NDP
Notes: 15:30

## Slide 46: Reduction in Energy Consumption
  Normalized to (N)SprAcc (higher is better)
Chart: 
| RS1 | RS2 | RS3 | RS4 | RS5 | GMean
pigz | 0.25285 | 0.23041 | 0.38335 | 0.80657 | 0.45126 | 0.38195
(N)Spr | 0.67476 | 0.8028 | 0.57937 | 0.92535 | 0.92733 | 0.76922
SG | 9.3415 | 6.2919 | 45.2882 | 13.8158 | 10.0488 | 12.9878
Energy Reductuion
SAGe provides significant energy reduction over both
general-purpose and genomics-specific baselines
16.9x
34.0x

## Slide 47: Compression Ratio
Read Set | Uncompressed Size (MB) | Compression Ratio |  | 
Read Set | Uncompressed Size (MB) | pigz | (N)Spr | SAGe
RS1 | 5000 | 03.4 | 24.8 | 22.8
RS2 | 79000 | 12.5 | 40.2 | 36.8
RS3 | 4000 | 03.4 | 07.2 | 07.1
RS4 | 12000 | 03.9 | 04.8 | 04.5
RS5 | 88400 | 03.5 | 07.6 | 07.8
2.9× better average compression ratio than general-purpose baseline
comparable compression ratio to genomics-specific baseline (with a modest 4.6% average reduction)

## Slide 48: Area and Power
Based on Synthesis of SAGe’s hardware units using the Synopsys Design Compiler @ 22nm technology node
Logic unit | # of instances | Area [mm2] | Power [mW]
Comparator | 1 per channel | 0.000045 | 0.014
Read Construction Unit | 1 per channel | 0.000017 | 0.023
Double Registers | 1 per channel | 0.00020 | 0.035
Control Unit | 1 per channel | 0.000029 | 0.025
Total for an 8-channel SSD | - | 0.002 | 0.77
SAGe’s hardware units consume small area and power

## Slide 49: More in the Paper
Observations on different parts of mismatch information
  Matching positions
  Mismatch bases and types
  Mismatch counts
SAGe’s performance in software
Sensitivity analysis with varying the number of SSD
Impact of each of SAGe’s optimizations on compression ratio
SAGe’s performance for quality scores
SAGe’s resource requirements compared to other (de)compression accelerators
SAGe’s compression time
Notes: Let me briefly talk about other results that are included in the paper before concluding this talk. These include the following:

## Slide 50: More in the Paper
https://arxiv.org/abs/2504.03732
Notes: Let me briefly talk about other results that are included in the paper before concluding this talk. These include the following:

## Slide 51: Outline
Conclusion
Background
Motivation and Gaol
SAGe
Evaluation

## Slide 52: Conclusion
Data preparation bottleneck greatly limits end-to-end performance of genome analysis
SAGe
Improves performance
Improves the end-to-end performance of two state-of-the-art genome analysis accelerators
by 3.0×–32.1×
Low overhead
Area: 0.002 mm2
Power: 0.77 mW
Reduces energy consumption
Improves the end-to-end energy efficiency of two state-of-the-art genome analysis accelerators
by 13.0×–34.0×
High compression ratio 2.9× better than general-purpose baseline
and comparable to genomics-specific baseline (with a modest 4.6% average reduction)
An algorithm-architecture co-design for highly-compressed storage and high-performance access of large-scale genomic sequence data

## Slide 53
A Lightweight Algorithm-Architecture Co-Design for Mitigating the Data Preparation Bottleneck in Large-Scale Genome Sequence Analysis
Nika Mansouri Ghiasi
Mohammad Sadrosadati Jisung Park Onur Mutlu
Talu Güloglu Harun Mustafa Can Firtina Konstantina Koliogeorgi
Konstantinos Kanellopoulos Haiyu Mao Rakesh Nadig

## Slide 54: Backup Slides
Genomic Workflow
SAGe Compression
Properties of Mismatch Information
Tuning Arrays and Guide Arrays
Hardware Details
Data Preparation Performance
End-to-End Performance
Performance with Multiple SSDs
Compression Ratio Details
Effect of Different Optimizations
Resource Requirements
Compression Time
Summary
Background
Motivation and Goal
SAGe
Evaluation

## Slide 55: Genomic Workflow

## Slide 56: SAGe Compression High-Level Overview

## Slide 57: Properties of Mismatch Information (I)
Chart: 
| 0 | 1 | 2 | 3 | 4+
 | 78.4 | 14 | 3.3 | 1.3 | 0.9
% of Reads
#Mismatches per Read
Distribution of mismatch counts per short read

## Slide 58: Properties of Mismatch Information (II)
Cumulative distribution of (a) indel block lengths and (b) #bases in indel blocks of different lengths
Chart: 
 | 67.3471 | 85.8812 | 92.8234 | 96.1103 | 97.6941 | 98.4254 | 98.7746 | 99.0335 | 99.1639 | 99.3208
Chart: 
 | 38.199 | 59.224 | 71.0368 | 78.4941 | 82.9857 | 85.4744 | 86.8611 | 88.0355 | 88.7014 | 89.5915
Cumul. % of Indels
Cumul. % of Indel Bases
Indel Length
Indel Length
(a)
(b)

## Slide 59: Properties of Mismatch Information (III)
Distribution of #bits needed to store the delta-encoded matching position.
Chart: 
 | 34.3087 | 27.0759 | 24.6153 | 11.7102 | 2.0654 | 0.1676 | 0.040552 | 0.013403 | 0.00276 | 0.00022455 | 2.4686e-05 | 6.6079e-06 | 3.6157e-06 | 4.9871e-07 | 0
% of Matching Positions
Needed #Bits

## Slide 60: Example of a chimeric read
ACGTAGAAAAAGTAGT … CGCTTTCAGACCTAG
GTAAAAGTATGAGA
Matching Position#2
Matching Position#1
Chimeric reads: reads with sequences joined from different regions of the genome due to sequencing/library preparation errors, or structural variations
Chimeric Read

## Slide 61: Tuning Arrays and Guide Arrays

## Slide 62: Hardware for Data Preparation

## Slide 63: Data Preparation Performance
Only data preparation throughput, normalized to pigz

## Slide 64: End-to-End Performance
Speedup, with different SSDs

## Slide 65: Performance with Multiple SSDs
Chart: 
| 1× | 2× | 4× | 1× | 2× | 4× | 1× | 2× | 4× | 1× | 2× | 4× | 1× | 2× | 4× | RS1 | RS2 | RS3 | RS4 | RS5
SG | 4.835 | 4.8807 | 4.9038 | 2.2661 | 2.2795 | 2.2863 | 28.2644 | 32.5976 | 35.3038 | 2.0525 | 2.0732 | 2.0838 | 1.5078 | 1.5082 | 1.5085
SG+ISF | 7.1505 | 7.2508 | 7.3021 | 10.3328 | 10.6181 | 10.7667 | 58.6957 | 94.4623 | 121.4377 | 2.0525 | 2.0732 | 2.0838 | 15.0528 | 30.1057 | 60.2114
Speedup
#SSDs
Read Set

## Slide 66: Compression Ratio

## Slide 67: Effect of Different SAGe Optimizations
NO: no optimization on the raw mismatch information
O1: matching position optimization added to NO O2: mismatch positions and count optimizations added to O1
O3: mismatching base and type optimizations added to O2 O4: corner case optimizations added to O3

## Slide 68: Resource Requirements

## Slide 69: Compression Time
Chart: 
| pigz | (N)Spr | SAGe | pigz | (N)Spr | SAGe | pigz | (N)Spr | SAGe | pigz | (N)Spr | SAGe | pigz | (N)Spr | SAGe | RS1 | RS2 | RS3 | RS4 | RS5
Finding Mismatches | 0 | 0.92771 | 0.92771 | 0 | 0.94687 | 0.94687 | 0 | 0.93407 | 0.93407 | 0 | 0.93822 | 0.93822 | 0 | 0.97697 | 0.97697
Encoding | 0.051807 | 0.072289 | 0.012048 | 0.095825 | 0.053131 | 0.0018975 | 0.035714 | 0.065934 | 0.010989 | 0.036293 | 0.061776 | 0.011583 | 0.023659 | 0.023028 | 0.0018927
Norm. Comp. Time

## Slide 70
A Lightweight Algorithm-Architecture Co-Design for Mitigating the Data Preparation Bottleneck in Large-Scale Genome Sequence Analysis
When: Tuesday (Feb 3) @ 17:35 AEDT
Where: ICC Sydney, Coogee Room

## Slide 71: Effect of the Data Preparation Bottleneck
Prep
Analysis
Analysis
Analysis
Base.
Acc. Analysis
w/ Ideal Prep.
Prep
Prep
Lost Benefit due to Data Prep. Bottleneck
Execution Timeline (Not drawn to scale)
Acc. Analysis
Potential Benefit of Genome Analysis Acceleration
Baseline Analysis (446 KRead/s)
Accelerated Analysis (69200 KRead/s)
Baseline Prep. (2563 KRead/s)
Ideal Prep. (> 69200 KRead/s)
Notes: 2:10

## Slide 72: .
An algorithm-architecture co-design for highly-compressed storage and high-performance access of large-scale genomic sequence data
Key insight: information encoded in genomic data follows specific properties
We leverage these properties to co-design
  A lossless (de)compression algorithm
  Hardware for decompression with lightweight operations
  Storage data layout & Interface commands to access data
Higher performance (by 3.0×–32.1×)
High compression ratio
Low overhead
Higher energy efficiency (by 13.0×–34.0x)
Notes: 3:30