## Slide 1: Storage-Centric System Designs for Enabling Fast, Efficient, and Low-Cost Genomic and Metagenomic Analyses
Nika Mansourighiasi
Doctoral Examination
31.03.2026
Advisor:
Onur Mutlu (ETH Zurich)
Co-Examiners:
Can Alkan (Bilkent University)
Reetuparna Das (University of Michigan)
Wen-mei Hwu (NVIDIA & University of Illinois Urbana-Champaign)
Jangwoo Kim (Seoul National University & MangoBoost)
Yatish Turakhia (University of California San Diego)
Notes: Hi everyone, I am going to give you an overview of my thesis, titled “...”

## Slide 2: Applications of (Meta)Genome Analysis
Precision Medicine
Outbreak Prevention and Management
Agriculture
Scientific Discovery
& Many More…

## Slide 3: DNA Under Electron Microscope
human chromosome #12
from HeLa cell
Notes: To get the organisms' genomic information encoded in their nucleotide sequences, such as DNA, into a digital format for analysis…

## Slide 4: High-Throughput Sequencers
… and more! All produce data with different properties.
Illumina MiSeq
Pacific Biosciences RS II
Illumina NovaSeq 6000
Oxford
Nanopore GridION
Pacific
Biosciences
Sequel II
Oxford
Nanopore
PromethION
Oxford Nanopore MinION

## Slide 5: High-Throughput Sequencers
… and more! All produce data with different properties.
Illumina MiSeq
Oxford Nanopore MinION
Pacific Biosciences RS II
Illumina NovaSeq 6000
Oxford
Nanopore SmidgION
Pacific
Biosciences
Sequel II
Oxford
Nanopore
PromethION
Current sequencing technologies
cannot sequence very long DNA molecules end-to-end
Instead, they extract smaller fragments of the original DNA sequence, known as reads
AAGCTTCCATGG
AAATGGGCTTTC
GCCCAAATGGTT
GCTTCCAGAATG

## Slide 6: Genome Sequence Analysis
Read mapping: first key step in genome sequence analysis
…GCCCATATGGTTAAGCTTCCATGGAAATGGGCTTTCGCTTCCACAATG…
  Aligns reads to potential matching locations in the reference genome
Reference Genome
Differences
Differences
  For each matching location, the alignment step finds the degree of similarity (alignment score)
AAGCTTCCATGG
GCCCAAATGGTT
GCTTCCAGAATG
AAATGGGCTTTC
Calculating the alignment score requires computationally-expensive approximate string matching (ASM) to account for differences between reads and the reference genome
Notes: Read mapping is the first key step in genome sequence analysis [CLICK]
That Aligns reads to potential matching locations within the reference genome [CLICK]
For each matching location, the alignment step finds the degree of similarity between read and reference by calculating the alignment score
Calculating the alignment score requires computationally-expensive approximate string matching (ASM) to account for differences between reads and the reference genome. [CLICK]

## Slide 7: What is Metagenomics?
Metagenomics: Study of genome sequences of diverse organisms
within a shared environment (e.g., blood, ocean, soil)
A large database containing information
on many species
(e.g., > 100 TBs in emerging databases)
Notes: Since sometimes a sample contains organisms with different species, genomic analysis is complemented by metagenomic analysis
Which enables the Study of genome sequences of diverse organisms within a shared environment (e.g., blood, ocean, soil)

## Slide 8: Sequence Data is Growing at a Fast Pace
Important Role in Many Fields
Large Reduction in Sequencing Cost
Fast growth in sequence data size
Publicly-Hosted Genomic Sequence Reads Data Size in Sequence Read Archive (SRA) Over Years
Chart: Total Size (TB)
~1000000x

## Slide 9: Overheads of (Meta)Genomic Analyses
Computation overhead
Data movement overhead
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Data Movement
Storage
System

## Slide 10: Accelerating (Meta)Genome Sequence Analysis
Heuristics
Accelerators
Filters
Computation overhead
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
✓
Storage
System
Notes: Motivated by all these factors, there has been significant efforts into improving performance [CLICK]
Through… Although there have been significant efforts to improve the analysis of large-scale sequence data,

## Slide 11: Problems
Accessing stored sequence data and feeding it to the analysis units
Overhead of moving large amounts of low-reuse data from the storage system
& unnecessary computational burden on the rest of the system
Notes: In this thesis, we identify major outstanding problems in
accessing stored sequence data
and feeding it to the analysis units.

## Slide 12: Accelerating (Meta)Genome Sequence Analysis
Heuristics
Accelerators
Filters
Computation overhead
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Storage
System
Data movement overhead
✓
Notes: There has been significant effort into improving read mapping performance [CLICK]
Through efficient heuristics [CLICK]
hardware accelerators [CLICK]
and various filters that prune reads that do not require expensive computation [CLICK].
While these approaches address the computation overhead in read mapping [CLICK]
[While Reads Move] None of them alleviate the data movement overhead from storage, whose impact becomes even larger when the computation overhead gets alleviated [CLICK]

## Slide 13: Problems
Accessing stored sequence data and feeding it to the analysis units
Overhead of moving large amounts of low-reuse data from the storage system
& unnecessary computational burden on the rest of the system
Data preparation bottleneck, where compressed genomic sequence data needs to be first decompressed and formatted before it can be analyzed

## Slide 14: Effect of the Data Preparation Bottleneck
Prep
Analysis
Analysis
Analysis
Base.
Acc. Analysis
w/ Ideal Prep.
Prep
Prep
Lost Benefit due to Data Prep. Bottleneck
Execution Timeline (Not drawn to scale)
Acc. Analysis
Potential Benefit of Genome Analysis Acceleration
Baseline Analysis (446 KRead/s)
Accelerated Analysis (69200 KRead/s)
Baseline Prep. (2563 KRead/s)
Ideal Prep. (> 69200 KRead/s)
Notes: 2:10

## Slide 15: Thesis Statement
By designing customized storage-centric systems that efficiently
analyze genomic and metagenomic data inside the storage system
enable highly-compressed storage and high-performance access of large-scale sequence data
we can alleviate the overheads of
computation
data movement
data preparation
thereby, significantly improving
performance
energy efficiency
cost effectiveness
⓵
⓶

## Slide 16: Our Approach
Designing customized storage-centric systems that efficiently
we can alleviate the overheads of
computation
data movement
data preparation
thereby, significantly improving
performance
energy efficiency
cost effectiveness
analyze genomic and metagenomic data inside the storage system
⓵
enable highly-compressed storage and high-performance access of large-scale sequence data
⓶

## Slide 17: Our Approach
Designing customized storage-centric systems that efficiently
MegIS [ISCA’24] Cooperative in-storage processing for metagenomic analysis
GRAINS [ISCA’26] Storage-aware algorithm-architecture co-design for graph-based (meta)genomic analyses
GenStore [ASPLOS’22] In-storage filtering for genomic analysis
SAGe [HPCA’26] Algorithm-architecture co-design for storing and accessing sequence data
analyze genomic and metagenomic data inside the storage system
⓵
enable highly-compressed storage and high-performance access of large-scale sequence data
⓶

## Slide 18: Our Approach
Designing customized storage-centric systems that efficiently
MegIS [ISCA’24] Cooperative in-storage processing for metagenomic analysis
GRAINS [ISCA’26] Storage-aware algorithm-architecture co-design for graph-based (meta)genomic analyses
GenStore [ASPLOS’22] In-storage filtering for genomic analysis
SAGe [HPCA’26] Algorithm-architecture co-design for storing and accessing sequence data
analyze genomic and metagenomic data inside the storage system
⓵
enable highly-compressed storage and high-performance access of large-scale sequence data
⓶

## Slide 19: Key Idea
Storage
System
Non-matching reads
Do not have potential matching locations and can skip alignment
Filter reads that do not require alignment
inside the storage system
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Filtered Reads
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Exactly-matching reads
Do not need expensive approximate string matching during alignment
GenStore
MegIS
GRAINS
SAGe
Notes: Our key idea is to filter reads that do not require the expensive alignment computation in the storage system [CLICK] …
[While Reads Move] To fundamentally reduce the data movement overhead of read mapping
Examples of the reads that not require the costlt alignment step
Exactly-matching reads to the reference genome that do not need approximate string matching performed during alignment
Non-matching reads that have no potential matching locations in the reference genome hence skip the alignemt step

## Slide 20: Read Mapping Process
GCC | 7 |  | 
CCC | 8 |  | 
CAA | 1 |  | 
AAA | 31 | 101 | 
CCA | 25 | 230 | 400
… | … | … | …
…CAATTTGCCCATATGGTTAAGCTTCCATGGAAATGGGCTTTCGCTTTG…
Reference
> 3 billion characters for the human genome
Index
K-mer
Locations
GCCCAAATGGTT
Read
GCC
CCC
…
K-mers
Determine potential matching locations (seed hits) in the reference genome
Prune some seed hits in the reference genome
Determine the exact differences between the read and the reference genome
Seeding
Seed Filtering
(e.g., Chaining)
Alignment
Seed Hits
…
GenStore
MegIS
GRAINS
SAGe
Notes: Mapping reads to reference genome requires expensive computation on large datasets.
[CLICK] The search space in the Reference genome can be very large (for example the human reference genome contains more than three billion characters).
[CLICK] Therefore, read mappers typically use an index of the reference genome to reduce the search space. This index contains unique 𝑘-length subsequences ([CLICK] called 𝑘-mers) extracted from the reference genome, [CLICK] and locations of these 𝑘-mers in the reference genome.
Read mapping is a three step process. State-of-the-art read mappers involve several heuristics to reduce the cost of expensive alignment computation.
[CLICK] In the first step (seeding), the mapper determines the potential matching locations (seeds) in the large reference genome where the read could map.
[CLICK] To do so, the read mapper extracts k-mers from the read [CLICK] and looks up the k-mer fetched from a read in the reference index. [CLICK] For all the k-mers that hit in the index, the read mapper marks the locations of them in the reference genome as the read’s potential matching locations (or seeds).
To further reduce the cost of the computationally-expensive alignment, the read mapper performs a second step [CLICK] , called chaining or seed filtering, in which the mapper [CLICK] prunes the seeds in the reference to which the read would not align using a simple approximation of the alignment score.
At the end of this step, the reads that have all their locations filtered, skip the third step.
[CLICK] For the remaining reads, the thitd step, which is the costly alignment, determines the exact differences between a read and the reference genome [CLICK] via approximate string matching.

## Slide 21: GenStore
GenStore for Exactly-Matching Reads
GenStore for Non-Matching Reads
GenStore
MegIS
GRAINS
SAGe
Notes: by thorough analysis of mapping processes of reads with different properties and different degrees of genetic variation, we design two low-cost in-storage filters
[CLICK] 1) GenStore-EM for filtering exactly-matching reads
[CLICK] and 2) GenStore-NM for filtering most of the non-matching reads

## Slide 22: GenStore
GenStore for Exactly-Matching Reads
GenStore for Non-Matching Reads
GenStore
MegIS
GRAINS
SAGe
Notes: by thorough analysis of mapping processes of reads with different properties and different degrees of genetic variation, we design two low-cost in-storage filters
[CLICK] 1) GenStore-EM for filtering exactly-matching reads
[CLICK] and 2) GenStore-NM for filtering most of the non-matching reads

## Slide 23: GenStore for Exactly-Matching Reads
Efficient in-storage filter for reads with at least one exact match in the reference genome
Uses simple operations, without requiring alignment
Challenge: Large number of random accesses per read to the reference genome and its index
Expensive random accesses to flash chips
Limited DRAM capacity inside the SSD
GenStore
MegIS
GRAINS
SAGe
Notes: [CLICK] GenStore-EM accelerates read mapping by using an efficient in-storage filter to filter reads that have at least one exactly matching location in the reference genome
[CLICK] via simple operations, without requiring alignment.
The key challenge in designing GenStore-EM is the large number of random accesses to large data structures inside the SSD.
This is challenging because. [CLICK]
NAND flash memory exhibits poor performance for random access reads. [CLICK]
there is limited DRAM capacity available in SSD which is relatively small compared to the size of the data structures that need to be accessed.

## Slide 24: Data Structures
GCCCAAATGGTT
Read
GCC
CCC
…
K-mers
K-mer
Read-sized k-mers: to reduce the number of accesses per each read
Only one index lookup per read
Sorted read-sized k-mers: to avoid random accesses to the index
Sequential scan of the read set and the index
✓
✓
GenStore
MegIS
GRAINS
SAGe
Notes: To reduce the **number** of accesses per each read, we introduce read-sized k-mers.
Therefore, instead of extracting several k-mers per read and performing index lookup for each of them, [CLICK] we can use the whole read as one k-mer
[CLICK] And have only one index lookup per read
[CLICK] To avoid **random** accesses to the index, we introduce the **sorted** index of read-sized k-mers.
[CLICK] This sorted index allows finding exact matches via sequential scanning of the read sets and the index

## Slide 25: Index Optimization
Read-sized k-mer index takes up a large amount of space (126 GB for human index) due to the larger number of unique k-mers
K-mer | Loc.
AAAAAAAAAA | 1, 8, …
AAAAAAAAAC | 51
AAAAAAAAAT | 23, 37
… | …
Sorted K-mer Index
Strong Hash Value
1
4
7
…
Using strong hash values instead of read-sized k-mers
reduces the size of the index by 3.9x
GenStore
MegIS
GRAINS
SAGe
Notes: Despite the key benefits of the sorted read-sized k-mer index, this index takes up a large space (126 GB for human index) due to the large number of unique read-sized k-mers.
We further reduce the overheads of GenStore-EM, by replacing read-sized k-mers with a strong hash of each read that act as
Sorting criterion
Fingerprint of each entry
Using strong hash values instead of read-sized k-mers reduces the size of the index by 3.9x
While this index is still larger than the baseline k-mer index used in the conventional read mappers, our proposal is feasible for in-storage processing due to the large capacity and high internal bandwidth of modern NAND flash-based SSDs.

## Slide 26: Evaluation Methodology
Read Mappers
Base: state-of-the-art software or hardware read mappers
  Minimap2 [Bioinformatics’18]: software mapper for short and long reads
  GenCache [MICRO’19]: hardware mapper for short reads
  Darwin [ASPLOS’18]: hardware mapper for long reads
GS: Base integrated with GenStore
SSD Configurations
SSD-L: With SATA3 interface (0.5 GB/s sequential read bandwidth)
SSD-M: With PCIe Gen3 interface (3.5 GB/s sequential read bandwidth)
SSD-H: With PCIe Gen4 interface (7 GB/s sequential read bandwidth)
GenStore
MegIS
GRAINS
SAGe
Notes: We valuate the following systems:
[CLICK] Base: state-of-the-art software or hardware read mappers for both short and long reads
[CLICK] GS: Base integrated with the GenStore inside the SSD
We evaluate these mappers on systems with various SSD configurations, a low-end, medium-end, and high-end SSD
For other details about our methodology, please refer to the paper.

## Slide 27: GenStore for Exactly-Matching Reads
For a read set with 80% exactly-matching reads
Chart: 
| Base | GS | Base | GS | Base | GS | SSD-L | SSD-M | SSD-H
Other | 170.17 | 69.24 | 154.65 | 74.71 | 159.07 | 73.31
Alignment | 0 | 0 | 0 | 0 | 0 | 0
Exec. time [sec]
Chart: 
| Base | GS | Base | GS | Base | GS | SSD-L | SSD-M | SSD-H
 | 44 | 8.8 | 6.2857 | 2.8229 | 4.2832 | 2.8229
 | 0 | 0 | 0 | 0 | 0 | 0
With the Software Mapper
With the Hardware Mapper
2.1× - 2.5× speedup compared to the software Base
1.5× – 3.3× speedup compared to the hardware Base
On average 3.92× energy reduction
29
2.5x
2.1x
2.1x
3.3x
1.5x
2.5x
GenStore
MegIS
GRAINS
SAGe
Notes: We analyze the benefits of GenStore-EM for a 22-GB short read set where 80% of reads exactly match some subsequence in the reference genome and can be filtered.
We show the benefit of GS on software and hardware read mappers.
GS provides 2.1× - 2.5× speedup compared to the software Base
GS provides 1.5× – 3.3× speedup compared to the hardware Base
GS provides on average 3.92× energy reduction

## Slide 28: GenStore for Non-Matching Reads
For a read set with 99.7% non-matching reads
Chart: 
| Base | GS | Base | GS | Base | GS | SSD-L | SSD-M | SSD-H
 | 30.028 | 1.564 | 5.362 | 0.78198 | 5.36 | 0.78198
Exec. time [sec]
Log scale
With the Software Mapper
With the Hardware Mapper
22.4× – 27.9× speedup compared to the software Base
6.8× – 19.2× speedup compared to the hardware Base
On average 27.2× energy reduction
Chart: 
| Base | GS | Base | GS | Base | GS | SSD-L | SSD-M | SSD-H
Time | 34.84 | 1.5537 | 22.55 | 0.77687 | 21.72 | 0.77687
22.4
29x
27.9x
19.2x
6.8x
6.8x
GenStore
MegIS
GRAINS
SAGe
Notes: Similarly, when evaluating GenStore’s filter for non-matching reads, …

## Slide 29: Area and Power
Based on Synthesis of GenStore accelerators using the Synopsys Design Compiler @ 65nm technology node
Logic unit | # of instances | Area [mm2] | Power [mW]
Comparator | 1 per SSD | 0.0007 | 0.14
K -mer Window | 2 per channel | 0.0018 | 0.27
Hash Accelerator | 2 per SSD | 0.008 | 1.8
Location Buffer | 1 per channel | 0.00725 | 0.37375
Chaining Buffer | 1 per channel | 0.008 | 0.95
Chaining PE | 1 per channel | 0.004 | 0.98
Control | 1 per SSD | 0.0002 | 0.11
Total for an 8-channel SSD | - | 0.2 | 26.6
Only 0.006% of a 14nm Intel Processor, less than 9.5% of the three ARM processors in a SATA SSD controller
GenStore
MegIS
GRAINS
SAGe
Notes: We find area and power values of GenStore by synthesizing GenStore-EM and NM using 65nm technology node,
And find that for an 8-channel SSD, the area of GS is 0.2 mm square and the power is 26.6 watts
BY scaling the area to lower technology nodes, we observe that the area overhead of GS is 0.006% of an Intel processor and less than 9.5% of the of the three ARM processors in a SATA SSD controller.

## Slide 30: Our Approach
Designing customized storage-centric systems that efficiently
MegIS [ISCA’24] Cooperative in-storage processing for metagenomic analysis
GRAINS [ISCA’26] Storage-aware algorithm-architecture co-design for graph-based (meta)genomic analyses
GenStore [ASPLOS’22] In-storage filtering for genomic analysis
SAGe [HPCA’26] Algorithm-architecture co-design for storing and accessing sequence data
analyze genomic and metagenomic data inside the storage system
⓵
enable highly-compressed storage and high-performance access of large-scale sequence data
⓶

## Slide 31: Our Approach
Designing customized storage-centric systems that efficiently
MegIS [ISCA’24] Cooperative in-storage processing for metagenomic analysis
GRAINS [ISCA’26] Storage-aware algorithm-architecture co-design for graph-based (meta)genomic analyses
GenStore [ASPLOS’22] In-storage filtering for genomic analysis
SAGe [HPCA’26] Algorithm-architecture co-design for storing and accessing sequence data
analyze genomic and metagenomic data inside the storage system
⓵
enable highly-compressed storage and high-performance access of large-scale sequence data
⓶

## Slide 32: Challenges of Storage-Centric Computing
Metagenomic analysis tools cannot run in-storage due to SSD limits
  Long latency of NAND flash chips
  Limited DRAM capacity inside the SSD
  Limited DRAM bandwidth inside the SSD
SSD DRAM
⋯
SSD
Controller
Cores
FTL
⋯
SSD
Cntrl
Cntrl
Channel#N
Channel#1
GenStore
MegIS
GRAINS
SAGe
Notes: While ...,
none of the existing approaches can be effectively implemented
inside the SSD due to limited hardware resources in the SSD ...

## Slide 33: MegIS: Metagenomics In-Storage
First in-storage system for end-to-end metagenomic analysis
Idea: Cooperative in-storage processing for metagenomic analysis
  Algorithm-Architecture co-design between the storage system and host system
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
GenStore
MegIS
GRAINS
SAGe
Notes: Which is the first in-storage processing system for end-to-end metagenomic analysis
The key idea of megis is Cooperative ISP for metagenomics
Which is enabled by a synergistic hardware/software co-design between the storage system and the host system

## Slide 34: MegIS Algorithm-Architecture Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
GenStore
MegIS
GRAINS
SAGe
Notes: To (i) leverage and (ii) orchestrate the capabilities of both systems, megis includes hw/sw co-design in 5 directions

## Slide 35: MegIS Algorithm-Architecture Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Task partitioning and mapping
Each step executes
in its most suitable system
GenStore
MegIS
GRAINS
SAGe

## Slide 36: MegIS Algorithm-Architecture Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Task partitioning and mapping
Each step executes
in its most suitable system
GenStore
MegIS
GRAINS
SAGe

## Slide 37: MegIS Algorithm-Architecture Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Storage-aware algorithms
Enable efficient
access patterns to the SSD
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Task partitioning and mapping
Each step executes
in its most suitable system
GenStore
MegIS
GRAINS
SAGe

## Slide 38: MegIS Algorithm-Architecture Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
ACC
ACC
Cntrl
Cntrl
Channel#N
Channel#1
Lightweight in-storage accelerators
Minimize SRAM/DRAM buffer spaces needed inside the SSD
Storage-aware algorithms
Enable efficient
access patterns to the SSD
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Task partitioning and mapping
Each step executes
in its most suitable system
GenStore
MegIS
GRAINS
SAGe

## Slide 39: MegIS Algorithm-Architecture Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
⋯
MegIS-Enabled SSD
MegIS
FTL
MegIS
Metadata
Cntrl
Cntrl
Channel#N
Channel#1
Data mapping scheme and Flash Translation Layer (FTL)
Specialize to the characteristics of metagenomic analysis
Leverage the SSD’s full internal bandwidth
Storage-aware algorithms
Enable efficient
access patterns to the SSD
Lightweight in-storage accelerators
Minimize SRAM/DRAM buffer spaces needed inside the SSD
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Task partitioning and mapping
Each step executes
in its most suitable system
ACC
ACC
GenStore
MegIS
GRAINS
SAGe
Notes: 6 mins until here

## Slide 40: Evaluation Methodology Overview (I)
Performance, Energy, and Power Analysis
Baseline Comparison Points
Performance-optimized software, Kraken2 [Genome Biology’19]
Accuracy-optimized software, Metalign [Genome Biology’20]
PIM hardware-accelerated tool (using processing-in-memory), Sieve [ISCA’21]
SSD Configurations
SSD-C: With SATA3 interface (0.5 GB/s sequential read bandwidth)
SSD-P: With PCIe Gen4 interface (7 GB/s sequential read bandwidth)
Hardware Components
Synthesized Verilog model for the in-storage accelerators
MQSim [Tavakkol+, FAST’18] for SSD’s internal operations
Ramulator [Kim+, CAL’15] for SSD’s internal DRAM
Software Components
Measure on a real system:
AMD® EPYC® host CPU with 128 physical cores
1 TB host DRAM
GenStore
MegIS
GRAINS
SAGe
Notes: We model performance, energy, and power of the systems based on the latency and throughput of each hardware-based and software-based component
We valuate the following baselines:
...
We evaluate these tools on systems with cost-optimized and performance-optimized SSD configurations

## Slide 41: Speedup over Software (with Cost-Optimized SSD)
MegIS provides significant speedup over both
Performance-Optimized and Accuracy-Optimized baselines
Speedup
Performance-Optimized
MegIS
Accuracy-Optimized
Sample Genetic Diversity
Chart: 
| Low | Med | High | GMean
P-Opt | 1 | 1 | 1 | 1
A-Opt | 0.43101 | 0.38921 | 0.35039 | 0.38881
MS | 5.3489 | 5.6406 | 6.3871 | 5.7761
SSD-C
5.8x
14.9x
Chart: 
| Low | Med | High | GMean
P-Opt | 1 | 1 | 1 | 1
A-Opt | 0.43101 | 0.38921 | 0.35039 | 0.38881
MS | 5.3489 | 5.6406 | 6.3871 | 5.7761
SSD-C
5.8x
Sample Genetic Diversity
14.9x
GenStore
MegIS
GRAINS
SAGe
Notes: We analyze the benefits of MegIS for samples with low, medium, and high genetic diversity,
And here I am showing for a cost optimized-SSD
We observe that compared to both P-Opt and A-Opt
MegIS provides significant speedups

## Slide 42: Speedup over Software (with Performance-Optimized SSD)
MegIS provides significant speedup over both
Performance-Optimized and Accuracy-Optimized baselines
Speedup
Performance-Optimized
MegIS
Accuracy-Optimized
Sample Genetic Diversity
Chart: 
| Low | Med | High | GMean
P-Opt | 1 | 1 | 1 | 1
A-Opt | 0.3836 | 0.29101 | 0.31974 | 0.32925
MS | 2.6617 | 3.6664 | 6.5218 | 3.9926
SSD-P
4.0x
12.1x
MegIS improves performance on both
cost-optimized and performance-optimized SSDs
GenStore
MegIS
GRAINS
SAGe

## Slide 43: Speedup over the PIM Hardware Baseline
4.9x
Chart: 
| Low | Med | High | GMean
 | 1 | 1 | 1 | 1
 | 4.8422 | 4.8446 | 5.0596 | 4.9144
Chart: 
| Low | Med | High | GMean
 | 1 | 1 | 1 | 1
 | 1.462 | 1.7798 | 2.7359 | 1.9237
Speedup
SSD-C
PIM
MegIS
1.9x
SSD-P
Sample Genetic Diversity
Sample Genetic Diversity
PIM
MegIS
MegIS provides significant speedup over the PIM baseline
GenStore
MegIS
GRAINS
SAGe
Notes: Similarly, we evaluate megis compared to the pim baseline
and show that on systems with cost-optimized
and performance-optimized ssds,
MegiS significantly outperforms the PIM baseline

## Slide 44: Reduction in Energy Consumption
On average across different input sets and SSDs
Chart: 
| Perf-Opt | Acc-Opt | PIM | MegIS
 | 1 | 0.35526 | 2.8421 | 5.4
GeoMean Energy Reduction
(Higher is Better)
MegIS provides significant energy reduction over
the Performance-Optimized, Accuracy-Optimized, and PIM baselines
5.4x
15.2x
1.9x
Same
accuracy
GenStore
MegIS
GRAINS
SAGe
Notes: Next, we show megis's energy reduction on average accross different input sets and SSDs and observe that megis provides...

## Slide 45: Accuracy, Area, and Power
Accuracy
Same accuracy as the accuracy-optimized baseline
Significantly higher accuracy than the performance-optimized and PIM baselines
  4.6 – 5.2× higher F1 score
  3 – 24% lower L1 norm error
Area and Power
Total for an 8-channel SSD:
Area: 0.04 mm2
Power: 7.658 mW
(Only 1.7% of the area and 4.6% of the power consumption
of three ARM Cortex R4 cores in an SSD controller)
GenStore
MegIS
GRAINS
SAGe
Notes: MegIS provides all these benefits while achieving high accuracy

## Slide 46: System Cost-Efficiency
GMean Speedup
Chart: 
| Perf-Opt ($) | Acc-Opt ($) | Perf-Opt($$$) | Acc-Opt ($$$) | MegIS ($)
 | 1 | 0.81324 | 6.8304 | 2.2454 | 16.1756
Cost-optimized system ($): With SSD-C and 64-GB DRAM
Performance-optimized system ($$$): With SSD-P and 1-TB DRAM
MegIS outperforms the baselines
even when running on a much less costly system
($)
($)
($$$)
($$$)
($)
7.2x
2.4x
16.2x
19.9x
GenStore
MegIS
GRAINS
SAGe
Notes: Self-note (copy from arxiv version): For the performance-optimized system, we calculate the cost of 1TB
DRAM to be roughly 7080 USD (8 x 128GB modules [230]) and the cost of
SSD-P to be roughly 875 USD. For the performance-optimized system, we calculate
the cost of 64GB DRAM to be roughly 312 USD (8 x 8GB modules [231],
assuming the same number of memory channels as the performance-optimized
system) and the cost of SSD-C to be roughly 346 USD. Note that the cost of
the total storage system depends not only on the price of each SSD but also on
the available interconnection slots in the systems, as systems typically have
fewer PCIe slots (needed for SSD-P) than SATA slots (needed for SSD-C).

## Slide 47: Our Approach
Designing customized storage-centric systems that efficiently
MegIS [ISCA’24] Cooperative in-storage processing for metagenomic analysis
GRAINS [ISCA’26] Storage-aware algorithm-architecture co-design for graph-based (meta)genomic analyses
GenStore [ASPLOS’22] In-storage filtering for genomic analysis
SAGe [HPCA’26] Algorithm-architecture co-design for storing and accessing sequence data
analyze genomic and metagenomic data inside the storage system
⓵
enable highly-compressed storage and high-performance access of large-scale sequence data
⓶

## Slide 48: Our Approach
Designing customized storage-centric systems that efficiently
MegIS [ISCA’24] Cooperative in-storage processing for metagenomic analysis
GRAINS [ISCA’26] Storage-aware algorithm-architecture co-design for graph-based (meta)genomic analyses
GenStore [ASPLOS’22] In-storage filtering for genomic analysis
SAGe [HPCA’26] Algorithm-architecture co-design for storing and accessing sequence data
analyze genomic and metagenomic data inside the storage system
⓵
enable highly-compressed storage and high-performance access of large-scale sequence data
⓶

## Slide 49: Large-Scale Genome Graphs
Powerful and efficient representations of genomic data
✓
Great expressive power
Compact representations
✓
GenStore
MegIS
GRAINS
SAGe
Input Sequences
Critical for enabling massive, population-scale analyses
GTGG
TGGA
TATG
GTGGATTATGACGAGGCTA
ATGA
TGAC
GACG
ACGA
CGAG
…
…
GTGG
TGGA
GTGGATTATGCCGAGGCTA
TATG
…
…
ATGC
TGCC
GCCG
CCGA
CGAG
GTGG
TGGA
TATG
GTGGATTATGTCGAGGCTA
ATGT
TGTC
GTCG
TCGA
CGAG
…
…
Graph Representation
GTGGATTATG
ATGACGA
ATGCCGA
ATGTCGA
CGAGGCTA
GTGG
TGGA
TATG
GTGGATTATGACGAGGCTA
ATGA
TGAC
GACG
ACGA
CGAG
…
…
GTGG
TGGA
GTGGATTATGCCGAGGCTA
TATG
…
…
ATGC
TGCC
GCCG
CCGA
CGAG
GTGG
TGGA
TATG
GTGGATTATGTCGAGGCTA
ATGT
TGTC
GTCG
TCGA
CGAG
…
…
Notes: Unlike traditional models, which represent genomic databases as a collection of disjoint, linear sequences, sequences in a graph are represented by graph walks

## Slide 50: Challenges of Storage-Centric Computing
Graph-based sequence analysis tools cannot run in storage due to SSD limits
GenStore
MegIS
GRAINS
SAGe
Dependent and random accesses to the sequence graph
Different properties from conventional, non-genome graphs
New challenges due to:
SSD DRAM
⋯
SSD
Controller
Cores
FTL
⋯
SSD
Cntrl
Cntrl
Channel#N
Channel#1
Notes: Again, while analyzing large-scale genome graphs inside storage can provide large benefits,
No graph-based analysis tool can directly run inside storage due to limitations of modern SSDs, as discussed before
And these challenges are exacerbated due to…

## Slide 51: GRAINS
The first system for analysis with large-scale genome graphs in storage
Enabled via storage-aware algorithm-architecture co-design, based on the properties of large-scale genome graphs to
  Make the execution pipeline more storage-friendly
  Further improve performance, energy-efficiency, and cost-effectiveness via storage-centric computing
…
Flash
Cntrl.
Flash Cntrl.
Baseline
Metadata
SSD Controller
Internal DRAM
Channel#1
…
NAND Die#M
GRAINS-Enabled SSD
Host System
…
NAND Die#2
NAND Die#M
NAND Die#2
NAND Die#1
NAND Die#1
Channel#N
FTL
Cores
GenStore
MegIS
GRAINS
SAGe

## Slide 52: GRAINS’s Algorithm-Architecture Co-Design
…
Flash
Cntrl.
Flash Cntrl.
SSD Controller
Internal DRAM
Channel#1
…
NAND Die#M
GRAINS-Enabled SSD
Host System
…
NAND Die#2
NAND Die#M
NAND Die#2
NAND Die#1
NAND Die#1
Channel#N
Cores
New batching technique and execution flow
based on the unique features of genome graphs that reduces #random accesses
Input Query Processing
GenStore
MegIS
GRAINS
SAGe

## Slide 53: GRAINS’s Algorithm-Architecture Co-Design
…
Flash
Cntrl.
Flash Cntrl.
SSD Controller
Internal DRAM
Channel#1
…
NAND Die#M
GRAINS-Enabled SSD
Host System
…
NAND Die#2
NAND Die#M
NAND Die#2
NAND Die#1
NAND Die#1
Channel#N
Cores
New batching technique and execution flow
based on the unique features of genome graphs that reduces #random accesses
Input Query Processing
In-storage and In-flash processing to avoid transferring low-reused pages and bandwidth waste
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
GenStore
MegIS
GRAINS
SAGe

## Slide 54: GRAINS’s Algorithm-Architecture Co-Design
…
Flash
Cntrl.
Flash Cntrl.
GRAINS
Metadata
SSD Controller
Internal DRAM
Channel#1
…
NAND Die#M
GRAINS-Enabled SSD
Host System
…
NAND Die#2
NAND Die#M
NAND Die#2
NAND Die#1
NAND Die#1
Channel#N
GRAINS FTL
Cores
New batching technique and execution flow
based on the unique features of genome graphs that reduces #random accesses
Input Query Processing
In-storage and In-flash processing to avoid transferring low-reused pages and bandwidth waste
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
FTL and data placement based on genome graph properties, to leverage SSD’s full internal bandwidth
GenStore
MegIS
GRAINS
SAGe

## Slide 55: GRAINS’s Algorithm-Architecture Co-Design
…
Flash
Cntrl.
Flash Cntrl.
GRAINS
Metadata
SSD Controller
Internal DRAM
Channel#1
…
NAND Die#M
GRAINS-Enabled SSD
Host System
…
NAND Die#2
NAND Die#M
NAND Die#2
NAND Die#1
NAND Die#1
Channel#N
GRAINS FTL
Cores
New batching technique and execution flow
based on the unique features of genome graphs that reduces #random accesses
Input Query Processing
In-storage and In-flash processing to avoid transferring low-reused pages and bandwidth waste
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
ECCLITE
PE
FTL and data placement based on genome graph properties, to leverage SSD’s full internal bandwidth
Lightweight scheduling technique enabled by repurposing the existing SSD structures to leverage the full parallelism of all flash dies
Light Scheduler
Scheduler Tables
GenStore
MegIS
GRAINS
SAGe

## Slide 56: Evaluation Methodology Overview (I)
Performance, Energy, and Power Analysis
Baseline Comparison Points
Fulgor [WABI’23]: A state-of-the-art node-centric tool
MetaGraph [Nature’25]: A state-of-the-art edge-centric tool
AccIdealMem: An idealized accelerator for graph queries with no main memory overheads, but still suffers from the I/O overhead of moving a large amount of low-reuse data
SSD Configurations
SSD-G4: With PCIe Gen4 interface (7 GB/s sequential read bandwidth)
SSD-G5: With PCIe Gen5 interface (14.8 GB/s sequential read bandwidth)
Hardware Components
Synthesized Verilog model for the in-storage accelerators
MQSim [Tavakkol+, FAST’18] for SSD’s internal operations
Ramulator [Kim+, CAL’15] for SSD’s internal DRAM
Software Components
Measure on a real system:
AMD® EPYC® host CPU with 128 physical cores
1.5 TB host DRAM
GenStore
MegIS
GRAINS
SAGe
Notes: We model performance, energy, and power of the systems based on the latency and throughput of each hardware-based and software-based component
We valuate the following baselines:
...
We evaluate these tools on systems with cost-optimized and performance-optimized SSD configurations

## Slide 57: Benefits over Software
Chart: 
| QL | QM | QS | GMean
Fulgor | 1 | 1 | 1 | 1
MetaGraph | 0.62278 | 0.73413 | 0.77147 | 0.70655
GRAINS | 4.061 | 8.5634 | 17.2404 | 8.4322
Chart: 
| QL | QM | QS | GMean
FG | 1 | 1 | 1 | 1
MG | 0.55421 | 0.68284 | 0.74414 | 0.65546
GRN | 2.7391 | 5.196 | 11.9805 | 5.5452
22.3
Speedup
16.1
SSD-G4
GRAINS provides significant speedup over Fulgor and Metagraph baselines, with both SSD-G4 and SSD-G5
GRAINS improves average energy-efficiency by 11.3x and 21.5x over Fulgor and Metagraph, respectively
SSD-G5
5.5x
8.5x
8.4
11.9
GenStore
MegIS
GRAINS
SAGe

## Slide 58: Benefits over Hardware
Chart: 
| QL | QM | QS | GMean
IdealAccMem | 1 | 1 | 1 | 1
GRAINS | 2.8967 | 8.0711 | 17.0161 | 7.3547
Chart: 
| QL | QM | QS | GMean
PIM | 1 | 1 | 1 | 1
GRN | 1.5184 | 4.6311 | 11.6728 | 4.3459
SSD-G4
17.0
11.6
Speedup
SSD-G5
GRAINS provides significant speedups over AccIdealMem baseline
4.3x
7.4x
GRAINS improves average energy-efficiency by 3.1—20.7x over AccIdealMem
GenStore
MegIS
GRAINS
SAGe

## Slide 59: Area and Power
Based on Synthesis of GRAINS’s hardware units using the Synopsys Design Compiler @ 22nm technology node
ECCLITE area based on the original paper [AiF, ISCA’25]
On-controller logic units are 0.7% of the four cores on an SSD controller
Logic unit | Area [mm²] | Power [mW]
On SSD Controller | 0.0025 | 0.21
On Die (ECC_LITE) | 0.036 | 18.04
On Die (Others) | 0.000093 | 0.01
On-die logic units take only 0.2% of the flash die’s area and fit well within its power budget
GenStore
MegIS
GRAINS
SAGe

## Slide 60: Our Approach
Designing customized storage-centric systems that efficiently
MegIS [ISCA’24] Cooperative in-storage processing for metagenomic analysis
GRAINS [ISCA’26] Storage-aware algorithm-architecture co-design for graph-based (meta)genomic analyses
GenStore [ASPLOS’22] In-storage filtering for genomic analysis
SAGe [HPCA’26] Algorithm-architecture co-design for storing and accessing sequence data
analyze genomic and metagenomic data inside the storage system
⓵
enable highly-compressed storage and high-performance access of large-scale sequence data
⓶

## Slide 61: Our Approach
Designing customized storage-centric systems that efficiently
MegIS [ISCA’24] Cooperative in-storage processing for metagenomic analysis
GRAINS [ISCA’26] Storage-aware algorithm-architecture co-design for graph-based (meta)genomic analyses
GenStore [ASPLOS’22] In-storage filtering for genomic analysis
SAGe [HPCA’26] Algorithm-architecture co-design for storing and accessing sequence data
analyze genomic and metagenomic data inside the storage system
⓵
enable highly-compressed storage and high-performance access of large-scale sequence data
⓶

## Slide 62
Prep
Analysis
Analysis
Analysis
Base.
Acc. Analysis
w/ Ideal Prep.
Prep
Prep
Lost Benefit due to Data Prep. Bottleneck
Execution Timeline (Not drawn to scale)
Acc. Analysis
Potential Benefit of Genome Analysis Acceleration
Baseline Analysis (446 KRead/s)
Accelerated Analysis (69200 KRead/s)
Baseline Prep. (2563 KRead/s)
Ideal Prep. (> 69200 KRead/s)
Recall: Effect of Data Preparation Bottleneck
GenStore
MegIS
GRAINS
SAGe
Notes: 2:10

## Slide 63: Mitigating Data Preparation Bottleneck
We need to effectively mitigate the data preparation bottleneck while meeting four key requirements:
Meeting all these requirements is challenging
High performance
High compression ratio
Low overhead
High energy efficiency
Even more challenging in genome analysis systems used
in hardware resource-constrained environments
GenStore
MegIS
GRAINS
SAGe
Notes: 2:50

## Slide 64: .
Genome Analysis
System
Request Data with SAGe’s Interface Commands
Send Prepared Data
in Desired Format
Receive Compressed Data
SAGe-Compressed Genomic Data
Operate w/ SAGe
Data Layout
Decompress & Reformat
SAGe HW
An algorithm-architecture co-design for highly-compressed storage and high-performance access of large-scale genomic sequence data
Key insight: Information encoded in genomic data follows specific properties We leverage these properties in our algorithm-architecture co-design
GenStore
MegIS
GRAINS
SAGe

## Slide 65: Case Studies of SAGe’s Hardware Integration
Due to its lightweight design, SAGe can seamlessly integrate with genome analysis systems
Genome Analysis ACC
SAGe HW
SSD
Genome Analysis ACC
SSD
Host System
SAGe HW
Host System
SSD
Host System
Genome Analysis ACC
SAGe HW
GenStore
MegIS
GRAINS
SAGe
Notes: 14

## Slide 66: Evaluation Methodology Overview (I)
Performance, Energy, and Power Analysis
Datasets: Read sets (RS)
From a variety of species (i.e., H. sapiens, T. cacao, M. acuminata malaccensis)
Sequenced with different sequencing technologies (i.e., Illumina and Oxford Nanopore Technologies)
End-to-end performance of a genome analysis application, which includes both data preparation and genome analysis
Hardware Components
Synthesized Verilog model for the hardware units
MQSim [Tavakkol+, FAST’18] for SSD’s internal operations
Ramulator [Kim+, CAL’15] for SSD’s internal DRAM
Software Components
Measure on a real system:
AMD® EPYC® host CPU with 128 physical cores
1.5 TB host DRAM
GenStore
MegIS
GRAINS
SAGe
Notes: We model performance, energy, and power of the systems based on the latency and throughput of each hardware-based and software-based component

## Slide 67: Recall: Case Studies of SAGe’s Hardware Integration
Due to its lightweight design, SAGe can seamlessly integrate with genome analysis systems
Genome Analysis ACC
SAGe HW
SSD
Genome Analysis ACC
SSD
Host System
SAGe HW
Host System
SSD
Host System
Genome Analysis ACC
SAGe HW
GenStore
MegIS
GRAINS
SAGe
Notes: 14

## Slide 68: Evaluation Methodology Overview (II)
Genome Analysis
A state-of-the-art hardware accelerator (GEM [Chen+, TPDS’23]), for read mapping
Near-data processing (NDP) baseline: GenStore [Mansouri Ghiasi+, ASPLOS’22]
  Alleviates the burden of moving and analyzing a large amount of low-reuse data
  Implemented in the resource-constrained environment of the SSD
SSD Controller
SSD’s
Internal
DRAM
⋯
Flash Cntrl.
Channel#N-1
Genome Analysis ACC
SSD
Flash Cntrl.
Channel#0
Genome Analysis ACC
GenStore
MegIS
GRAINS
SAGe

## Slide 69: Evaluation Methodology Overview (II)
Data Preparation
pigz: Commonly-used general-purpose software ([Adler, JPL’15])
(N)Spr: Genomics-specific software for short (Spring [Chandak, Bioinformatics’18]) and long reads (NanoSpring [Meng+, Scientific Reports’23])
(N)SprAcc: (N)Spring hardware-accelerated
0TimeDec: An idealized decompressor (with zero decompression time), but inefficient for integration in resource-constrained environments
SAGe: SAGe implemented as a standalone accelerator for data preparation
SAGeSSD: SAGe inside the SSD, for integration with the NDP analysis system
SSD Controller
SSD’s
Internal
DRAM
SAGe FTL
Metadata
⋯
Flash Cntrl.
Channel#N-1
Genome Analysis ACC
SAGe HW
Double-Reg.
SSD
Flash Cntrl.
Channel#0
Genome Analysis ACC
SAGe HW
Double-Reg.
GenStore
MegIS
GRAINS
SAGe
Notes: 14:30

## Slide 70: Speedup
Chart: 
| RS1 | RS2 | RS3 | RS4 | RS5 | GMean
pigz | 0.3207 | 0.22018 | 0.52661 | 0.42172 | 0.22321 | 0.32271
(N)Spr | 1 | 1 | 1 | 1 | 1 | 1
(N)SprAcc | 1.5353 | 1.2884 | 1.7302 | 1.086 | 1.0869 | 1.3221
SAGe | 4.8537 | 2.2779 | 28.5302 | 2.0725 | 1.5084 | 3.9699
0TimeDec | 4.8537 | 2.2779 | 28.5302 | 2.0725 | 1.5084 | 3.9699
SAGeSSD+NDP | 7.1782 | 10.3865 | 51.9319 | 2.0725 | 14.9719 | 10.3738
28.5
51.9
28.5
Speedup
15.0
3.9x
3.0x
12.3x
2.6x
SAGe provides significant speedup over both
general-purpose and genomics-specific baselines
SAGe achieves the same speedup as 0TimeDec
By efficiently integrating SAGeSSD with NDP SAGeSSD+NDP leads to large speedups
SAGeSSD+NDP
GenStore
MegIS
GRAINS
SAGe

## Slide 71: Reduction in Energy Consumption
  Normalized to (N)SprAcc (higher is better)
Chart: 
| RS1 | RS2 | RS3 | RS4 | RS5 | GMean
pigz | 0.25285 | 0.23041 | 0.38335 | 0.80657 | 0.45126 | 0.38195
(N)Spr | 0.67476 | 0.8028 | 0.57937 | 0.92535 | 0.92733 | 0.76922
SG | 9.3415 | 6.2919 | 45.2882 | 13.8158 | 10.0488 | 12.9878
Energy Reductuion
SAGe provides significant energy reduction over both
general-purpose and genomics-specific baselines
16.9x
34.0x
GenStore
MegIS
GRAINS
SAGe
SAGe

## Slide 72: Compression Ratio
2.9× better average compression ratio than general-purpose baseline
Comparable compression ratio to genomics-specific baseline (with a modest 4.6% average reduction)
GenStore
MegIS
GRAINS
SAGe

## Slide 73: Area and Power
Based on Synthesis of SAGe’s hardware units using the Synopsys Design Compiler @ 22nm technology node
Logic unit | # of instances | Area [mm2] | Power [mW]
Comparator | 1 per channel | 0.000045 | 0.014
Read Construction Unit | 1 per channel | 0.000017 | 0.023
Double Registers | 1 per channel | 0.00020 | 0.035
Control Unit | 1 per channel | 0.000029 | 0.025
Total for an 8-channel SSD | - | 0.002 | 0.77
SAGe’s hardware units consume small area and power
GenStore
MegIS
GRAINS
SAGe

## Slide 74: Our Approach
Designing customized storage-centric systems that efficiently
MegIS [ISCA’24] Cooperative in-storage processing for metagenomic analysis
GRAINS [ISCA’26] Storage-aware algorithm-architecture co-design for graph-based (meta)genomic analyses
GenStore [ASPLOS’22] In-storage filtering for genomic analysis
SAGe [HPCA’26] Algorithm-architecture co-design for storing and accessing sequence data
analyze genomic and metagenomic data inside the storage system
⓵
enable highly-compressed storage and high-performance access of large-scale sequence data
⓶

## Slide 75: Conclusion
analyze genomic and metagenomic data inside the storage system
⓵
By designing customized storage-centric systems that efficiently
enable highly-compressed storage and high-performance access of large-scale sequence data
we can alleviate the overheads of
computation
data movement
data preparation
SAGe
MegIS
GRAINS
GenStore
⓵
⓶
Notes: To conclude, in this thesis, we show that

## Slide 76: Putting It All Together
Performance
Energy Efficiency
Cost Effectiveness
Make accurate (meta)genomic analysis more accessible for wider adoption
Storage-Centric Systems for (Meta)Genomics

## Slide 77: Future Directions
Advancing the capabilities of storage-centric computing for health and life sciences
  Extending the capabilities of the proposed designs for (meta)genomics
  Expanding to new areas: Transcriptomics, single-cell analysis
  Updating large-scale databases
Highly compressed storage and fast access of other biological data
  Raw genomic signals
  Transcriptomics, single-cell data
Alleviating the adoption challenges of storage-centric designs
  Privacy
  Applicability vs. cost tradeoffs
Facilitating portable (meta)genomics with storage-centric designs
1
2
3
4

## Slide 78: My Involvements During PhD
2020
Thesis
Publications
Other Storage-Centric Computing Works
Memory-Centric Computing
Bioinformatics Algorithms
Algorithm-Architecture Co-design
Improving Storage & Memory Systems
2021
2022
2023
2024
2025
2026
NMG+ ASPLOS
NMG+ HPCA
NMG+ ISCA
NMG+ ISCA
NMG+ IEEE TETC
NMG+ ACM TACO
First author publications
NMG+ PACT SRC
Oliveira+ ASPLOS
Chen+ ISCA
Nadig+ HPCA
Soysal+ ICS
Wang+ MICRO
Orosa+
ISCA
Bostanci, Kanellopoulos+ DSN
Nadig, Sadrosadati+
ISCA
Cavlak+
APBC
Firtina+
NARGAB
Firtina+
ISMB
Mustafa+
ISMB
Liu+
Nature Reviews
Sharma+
Under Sub.
Lindegger+
Bioinformatics
Cali+
ISCA
Lindegger+
IEEE Access
Liang+
HPCA
Eudine+
HPCA
Notes: This brings me to the last part of the presentation...
I am thankful that I had the chance to contribute to many other interesting projects beyond what contributed to my thesis

## Slide 79: Acknowledgments
Advisor: Onur Mutlu
Committee members: Can Alkan, Reetuparna Das, Wen-mei Hwu, Jangwoo Kim, Yatish Turakhia
Chair: Morteza Aramesh
Mentors: Jisung Park, Mohammad Sadrosadati, Nandita Vijaykumar, Juan Gómez-Luna
Mentees: Talu, Marc, Timur, Eirini, Akmuhammet
All SAFARI group members (especially Konstantinos Sr., Rahul, Konstantina, Geraldo, Giray, Can, Damla, Rakesh, Jeremie, Nisa, Ataberk, Lois, Yaohua, Haiyu, Christina)
Industrial partners & sponsors
Friends (especially Mehrasa, Yasmin, Hashem, Julia, Vesna, Pascal)
Family: Harun, Mehrangiz, Amir, Ali, Tuncel, Niyazi, Hazal, aunts, uncles, and cousins and in the loving memory of Khaleh Golshan and my grandmother, Narges
Notes: This thesis won’t have been possible without the help from numerous people, ...

## Slide 80: Storage-Centric System Designs for Enabling Fast, Efficient, and Low-Cost Genomic and Metagenomic Analyses
Nika Mansourighiasi
Doctoral Examination
31.03.2026
Advisor:
Onur Mutlu (ETH Zurich)
Co-Examiners:
Can Alkan (Bilkent University)
Reetuparna Das (University of Michigan)
Wen-mei Hwu (NVIDIA & University of Illinois Urbana-Champaign)
Jangwoo Kim (Seoul National University & MangoBoost)
Yatish Turakhia (University of California San Diego)
Notes: Hi everyone, I am going to give you an overview of my doctoral thesis, titled “...”
So, let’s get started ...

## Slide 81: Discussion
GenStore
SAGe
GRAINS
MegIS

## Slide 82: Putting It All Together
Motivation for combining the proposed designs into a unified system
  Storage-centric computing on compressed data
  Facilitating wider adoption
Design of the unified system
  Hardware units
    Only 6% of the four ARM cores on an SSD controller
  FTL
  Interface commands
    A single command initiates storage-centric acceleration, with a parameter selecting the specific mode (GenStore, MegIS, GRAINS, or SAGe)
    Each acceleration design retains its own interface commands

## Slide 83: Putting It All Together: SAGe + GenStore
Chart: 
| RS1 | RS2 | RS3 | RS4 | RS5 | GMean
pigz | 0.3207 | 0.22018 | 0.52661 | 0.42172 | 0.22321 | 0.32271
(N)Spr | 1 | 1 | 1 | 1 | 1 | 1
(N)SprAcc | 1.5353 | 1.2884 | 1.7302 | 1.086 | 1.0869 | 1.3221
SAGe | 4.8537 | 2.2779 | 28.5302 | 2.0725 | 1.5084 | 3.9699
0TimeDec | 4.8537 | 2.2779 | 28.5302 | 2.0725 | 1.5084 | 3.9699
SAGeSSD+NDP | 7.1782 | 10.3865 | 51.9319 | 2.0725 | 14.9719 | 10.3738
28.5
51.9
28.5
Speedup
15.0
3.9x
3.0x
12.3x
2.6x
SAGe provides significant speedup over both
general-purpose and genomics-specific baselines
SAGe achieves the same speedup as 0TimeDec
By efficiently integrating SAGeSSD with NDP SAGeSSD+NDP leads to large speedups
SAGeSSD+NDP
Notes: 15:30

## Slide 84: Putting It All Together: SAGe + MegIS
Chart: 
| P-Opt | A-Opt | MegIS
pigz | 1 | 0.33218 | 2.6759
(N)Spr | 1.0978 | 0.34231 | 3.5137
SAGe | 1.2198 | 0.35361 | 5.2285
Speedup Normalized to P-Opt+pigz
Speedup

## Slide 85: Putting It All Together: SAGe + GRAINS
Speedup Normalized to FG+pigz
Chart: 
| FG | MG | GRN
pigz | 1 | 0.63335 | 3.5765
(N)Spr | 0.99346 | 0.63072 | 3.4943
SAGe | 1.0463 | 0.65161 | 4.249
Speedup

## Slide 86: Compression Ratio for Metagenomic Data
Read Set | pigz | (N)Spr | SAGe
CAMI-L | 3.53 | 21.54 | 32.53
CAMI-M | 3.59 | 17.65 | 26.20
CAMI-H | 3.54 | 7.35 | 9.53
Better average compression ratio than general-purpose baseline
Comparable compression ratio to genomics-specific baseline

## Slide 87: Benefits Outside the SSD
Key benefits of storage-centric designs outside storage
  Alleviating the burden of moving and analyzing low-reuse data
  More storage-friendly execution pipelines: Efficient access patterns, and fewer random accesses
    Efficient use of the available I/O bandwidth
    Less reliance on large DRAM capacity
However, there are more benefits from analysis inside the storage
  Higher IFP/ISP bandwidth
  Avoid moving low-reuse data
  Does not rely on wider/more external interfaces

## Slide 88: Benefits Outside the SSD: MegIS

## Slide 89: Benefits Outside the SSD: GRAINS

## Slide 90: Benefits Outside the SSD: GenStore-EM
Chart: 
| Base | SIMD | GS-Ext | GS | Base | SIMD | GS-Ext | GS | Base | SIMD | GS-Ext | GS | SSD-L | SSD-M | SSD-H
Other | 101.8 | 128.44 | 119.24 | 52.78 | 73.98 | 81.378 | 31.69 | 31.69 | 86.17 | 94.787 | 31.92 | 31.92
Alignment | 68.37 | 16.46 | 16.46 | 16.46 | 80.67 | 43.02 | 43.02 | 43.02 | 72.9 | 41.39 | 41.39 | 41.39
Chart: 
| Base | GS-Ext | GS | Base | GS-Ext | GS | Base | GS-Ext | GS | SSD-L | SSD-M | SSD-H
 | 44 | 108.4 | 8.8 | 6.2857 | 15.4857 | 2.8229 | 4.2832 | 7.7429 | 2.8229
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Exec. time [sec]
44
108
15
With the Software Mapper
With the Hardware Mapper
Notes: GS-Ext provides significant performance
improvements over both Base and SIMD in SSD-M and SSD-H. However,
GS-Ext provides limited benefits over SIMD in SSD-L since
its performance is bottlenecked by the low external I/O bandwidth.

## Slide 91: Benefits Outside the SSD: GenStore-NM
Chart: 
| Base | GS | Base | GS | Base | GS | SSD-L | SSD-M | SSD-H
Time | 34.84 | 1.5537 | 22.55 | 0.77687 | 21.72 | 0.77687
Chart: 
| Base | GS-Ext | GS | Base | GS-Ext | GS | Base | GS-Ext | GS | SSD-L | SSD-M | SSD-H
 | 30.028 | 30.056 | 1.564 | 5.362 | 4.2937 | 0.78198 | 5.36 | 2.1469 | 0.78198
With the Software Mapper
With the Hardware Mapper
Exec. time [sec]
Notes: GS-Ext performs significantly slower than Base (2.28x - 1.91x) on all systems.

## Slide 92: GenStore: A High-Performance In-Storage Processing System for Genome Sequence Analysis
Nika Mansouri Ghiasi, Jisung Park, Harun Mustafa, Jeremie Kim, Ataberk Olgun,
Arvid Gollwitzer, Damla Senol Cali, Can Firtina, Haiyu Mao, Nour Almadhoun Alserr,
Rachata Ausavarungnirun, Nandita Vijaykumar, Mohammed Alser, and Onur Mutlu
Notes: Hi, I’m Nika, and today I will introduce GenStore: A High-Performance In-Storage Processing System
for Genome Sequence Analysis

## Slide 93: GenStore Discussion
Main presentation
Motivation details
Long read use cases
GenStore-NM detailed architecture
Detailed results
Effect of inputs

## Slide 94: Genome Sequence Analysis
Genome sequence analysis is critical for many applications
  Personalized medicine
  Outbreak tracing
  Evolutionary studies
Genome sequencing machines extract smaller fragments of the original DNA sequence, known as reads
AAGCTTCCATGG
AAATGGGCTTTC
GCCCAAATGGTT
GCTTCCAGAATG
Notes: Genome sequence analysis (GSA) is critical for many applications [CLICK]
Genome sequencing machines extract smaller fragments of the original DNA sequence, known as reads. [CLICK]

## Slide 95: Genome Sequence Analysis
Read mapping: first key step in genome sequence analysis
…GCCCATATGGTTAAGCTTCCATGGAAATGGGCTTTCGCTTCCACAATG…
  Aligns reads to potential matching locations in the reference genome
Reference Genome
Differences
Differences
  For each matching location, the alignment step finds the degree of similarity (alignment score)
AAGCTTCCATGG
GCCCAAATGGTT
GCTTCCAGAATG
AAATGGGCTTTC
Calculating the alignment score requires computationally-expensive approximate string matching (ASM) to account for differences between reads and the reference genome due to:
  Sequencing errors
  Genetic variation
Notes: Read mapping is the first key step in genome sequence analysis [CLICK]
That Aligns reads to potential matching locations within the reference genome [CLICK]
For each matching location, the alignment step finds the degree of similarity between read and reference by calculating the alignment score
Calculating the alignment score requires computationally-expensive approximate string matching (ASM) to account for differences between reads and the reference genome. [CLICK]

## Slide 96: Genome Sequence Analysis
Computation overhead
Data movement overhead
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Alignment
Data Movement from Storage
Storage
System
Notes: Read mapping performs alignment on large genomic datasets, containing millions of reads. [CLICK]
Therefore, read mapping is both computationally expensive [CLICK]
And incurs high data movement overhead [CLICK]

## Slide 97: Accelerating Genome Sequence Analysis
Heuristics
Accelerators
Filters
Computation overhead
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Storage
System
Data movement overhead
✓
Notes: There has been significant effort into improving read mapping performance [CLICK]
Through efficient heuristics [CLICK]
hardware accelerators [CLICK]
and various filters that prune reads that do not require expensive computation [CLICK].
While these approaches address the computation overhead in read mapping [CLICK]
[While Reads Move] None of them alleviate the data movement overhead from storage, whose impact becomes even larger when the computation overhead gets alleviated [CLICK]

## Slide 98: Key Idea
Storage
System
Non-matching reads
Do not have potential matching locations and can skip alignment
Filter reads that do not require alignment
inside the storage system
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Filtered Reads
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Exactly-matching reads
Do not need expensive approximate string matching during alignment
Notes: Our key idea is to filter reads that do not require the expensive alignment computation in the storage system [CLICK] …
[While Reads Move] To fundamentally reduce the data movement overhead of read mapping
Examples of the reads that not require the costlt alignment step
Exactly-matching reads to the reference genome that do not need approximate string matching performed during alignment
Non-matching reads that have no potential matching locations in the reference genome hence skip the alignemt step

## Slide 99: Challenges
Read mapping workloads can exhibit different behavior
There are limited hardware resources
in the storage system
Filter reads that do not require alignment
inside the storage system
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Filtered Reads
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Storage
System
Notes: However, filtering reads in a modern SSD can be challenging [CLICK]
Due to different behavior across read mapping workloads. [CLICK]
And the limited hardware resources in the SSD. By addressing these challenges [CLICK]

## Slide 100: GenStore
Computation overhead
Data movement overhead
  GenStore provides significant speedup (1.4x - 33.6x) and
  energy reduction (3.9x – 29.2x) at low cost
Filter reads that do not require alignment
inside the storage system
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
GenStore-Enabled
Storage
System
✓
✓
Notes: We propose GenStore, the first in-storage processing system designed for genome sequence analysis. [CLICK]
To reduce both the computation [CLICK]
And the data movement overhead [CLICK]
GenStore provides high-performance and energy benefits compared to state-of-the-art HW and SW baselines [CLICK]

## Slide 101: Outline
Conclusions
Background
Motivation and Goal
Experimental Methodology
Temperature Analysis
Aggressor Row Active Time Analysis
Spatial Variation Analysis
Implications on Attacks and Defenses
Conclusions
Motivation and Goal
GenStore
Evaluation
Notes: That was a summary of my talk. So let’s start with the background on read mapping so we can dive into the talk in more detail.

## Slide 102: Read Mapping Process
GCC | 7 |  | 
CCC | 8 |  | 
CAA | 1 |  | 
AAA | 31 | 101 | 
CCA | 25 | 230 | 400
… | … | … | …
…CAATTTGCCCATATGGTTAAGCTTCCATGGAAATGGGCTTTCGCTTTG…
Reference
> 3 billion characters
Index
K-mer
Locations
GCCCAAATGGTT
Read
GCC
CCC
…
K-mers
Determine potential matching locations (seeds) in the reference genome
Prune some seeds in the reference genome
Determine the exact differences between the read and the reference genome
Seeding
Seed Filtering
(e.g., Chaining)
Alignment
Seeds
…
Notes: Mapping reads to reference genome requires expensive computation on large datasets.
[CLICK] The search space in the Reference genome can be very large (for example the human reference genome contains more than three billion characters).
[CLICK] Therefore, read mappers typically use an index of the reference genome to reduce the search space. This index contains unique 𝑘-length subsequences ([CLICK] called 𝑘-mers) extracted from the reference genome, [CLICK] and locations of these 𝑘-mers in the reference genome.
Read mapping is a three step process. State-of-the-art read mappers involve several heuristics to reduce the cost of expensive alignment computation.
[CLICK] In the first step (seeding), the mapper determines the potential matching locations (seeds) in the large reference genome where the read could map.
[CLICK] To do so, the read mapper extracts k-mers from the read [CLICK] and looks up the k-mer fetched from a read in the reference index. [CLICK] For all the k-mers that hit in the index, the read mapper marks the locations of them in the reference genome as the read’s potential matching locations (or seeds).
To further reduce the cost of the computationally-expensive alignment, the read mapper performs a second step [CLICK] , called chaining or seed filtering, in which the mapper [CLICK] prunes the seeds in the reference to which the read would not align using a simple approximation of the alignment score.
At the end of this step, the reads that have all their locations filtered, skip the third step.
[CLICK] For the remaining reads, the thitd step, which is the costly alignment, determines the exact differences between a read and the reference genome [CLICK] via approximate string matching.

## Slide 103: Outline
Conclusions
Background
Motivation and Goal
Experimental Methodology
Temperature Analysis
Aggressor Row Active Time Analysis
Spatial Variation Analysis
Implications on Attacks and Defenses
Conclusions
Motivation and Goal
GenStore
Evaluation
Notes: We perform experimental studies to understand the potential of efficient in-storage filters for improving read mapping performance.

## Slide 104: Motivation
Case study on a real-world genomic read dataset
  Various read mapping systems
  Various state-of-the-art SSD configurations
The ideal in-storage filter significantly improves performance by
reducing the computation overhead
reducing the data movement overhead
Notes: We perform a case study on a real world genomic read dataset, on various read mapping systems and state-of-the-art SSD configirations.

## Slide 105: Motivation
Case study on a real-world genomic read dataset
  Various read mapping systems
  Various state-of-the-art SSD configurations
Filtering outside SSD provides lower performance benefit since it
does not reduce the data movement overhead
2) must compete with read mapping for system resources
A HW accelerator reduces the computation bottleneck,
which makes I/O a larger bottleneck in the system
Notes: We perform a case study on a real world genomic read dataset, on various read mapping systems and state-of-the-art SSD configirations.

## Slide 106: Our Goal
Design Objectives:
Design an in-storage filter for genome sequence analysis in a cost-effective manner
Provide high in-storage filtering performance to overlap the filtering with the read mapping of unfiltered data
Performance
Support reads with 1) different properties and 2) different degrees of genetic variation in the compared genomes
Applicability
Do not require significant hardware overhead
Low-cost
Notes: Motivated by these observations, Our goal is to design an in-storage filter for genome sequence analysis in a cost-effective manner. [CLICK]
We have three key objectives in designing our new system. [CLICK]
First, the system should Provide high in-storage filtering performance to overlap the filtering with the read mapping of unfiltered data
Second, the design should Support reads with 1) different properties and 2) different degrees of genetic variation
Third, it should not require significant additional hardware overhead

## Slide 107: Outline
Conclusions
Background
Motivation and Goal
Experimental Methodology
Temperature Analysis
Aggressor Row Active Time Analysis
Spatial Variation Analysis
Implications on Attacks and Defenses
Conclusions
Motivation and Goal
GenStore
Evaluation
Notes: To this end, we propose GenStore…

## Slide 108: GenStore
SSD Controller
Core
Core
Core
In-SSD DRAM
L2P
Mappings
Flash
Ctrl.#1
Flash
Ctrl.#N
⋯
NAND
Die#4
NAND
Die#1
⋯
NAND
Die#4
NAND
Die#1
⋯
Host System
FTL
ACC
ACC
ACC
GenStore
Metadata
GenStore
FTL
Reads that need
substantial processing
Key idea: Filter reads that do not require alignment inside the storage system
Challenges
  Different behavior across read mapping workloads
  Limited hardware resources in the SSD
Notes: Which is the first in-storage processing system designed for genome sequence analysis
Our key idea is to Filter reads that do not require alignment inside the storage system and send the unfiltered data to the host system for further processing
However, filtering reads in a modern SSD can be challenging [CLICK]
Due to different behavior across read mapping workloads. [CLICK]
And the limited hardware resources in the SSD.

## Slide 109: Filtering Opportunities
Sequencing machines produce one of two kinds of reads
  Short reads: highly accurate and short
  Long reads: less accurate and long
High sequencing error rates (long reads) or
High genetic variation (short or long reads)
Non-matching reads
Do not have potential matching locations, so they skip alignment
Low sequencing error rates (short reads) combined with
Low genetic variation
Exactly-matching reads
Do not need expensive approximate string matching during alignment
Reads that do not require the expensive alignment step:
Notes: Let’s take a look at filtering opportunities based on the input reads.
Sequencing machines produce one of two kinds of reads
  Short reads: highly accurate (99.9%) and short (e.g., up to a few hundreds of DNA characters)
  Long reads: less accurate (85-90%) and long (e.g., from hundreds to millions of DNA characters)
Based on these, We leverage two filtering opportunities
First, we can filter exactly matching reads, which are reads that match exactly to one or more subsequences of the reference genome and do not require approximate string matching during alignment. Exact matches can frequently occur in short read sets with low sequencing errors and low genetic variations
Second, we can filter non-matching reads. Such reads do not have any potential matching locations in the reference genome can skip the expensive alignment step. Non-matching reads can frequently occur in long read sets with high sequencing errors and short or long read sets with high genetic variations

## Slide 110: GenStore
GenStore-EM for Exactly-Matching Reads
GenStore-NM for Non-Matching Reads
Notes: by thorough analysis of mapping processes of reads with different properties and different degrees of genetic variation, we design two low-cost in-storage filters
[CLICK] 1) GenStore-EM for filtering exactly-matching reads
[CLICK] and 2) GenStore-NM for filtering most of the non-matching reads

## Slide 111: GenStore
GenStore-EM for Exactly-Matching Reads
GenStore-NM for Non-Matching Reads
Notes: Let's take a closer look at GenStore-EM

## Slide 112: GenStore-EM
Efficient in-storage filter for reads with at least one exact match in the reference genome
Uses simple operations, without requiring alignment
Challenge: large number of random accesses per read to the reference genome and its index
Expensive random accesses to flash chips
Limited DRAM capacity inside the SSD
Notes: [CLICK] GenStore-EM accelerates read mapping by using an efficient in-storage filter to filter reads that have at least one exactly matching location in the reference genome
[CLICK] via simple operations, without requiring alignment.
The key challenge in designing GenStore-EM is the large number of random accesses to large data structures inside the SSD.
This is challenging because. [CLICK]
NAND flash memory exhibits poor performance for random access reads. [CLICK]
there is limited DRAM capacity available in SSD which is relatively small compared to the size of the data structures that need to be accessed.

## Slide 113: GenStore-EM: Data Structures
GCCCAAATGGTT
Read
GCC
CCC
…
K-mers
K-mer
Read-sized k-mers: to reduce the number of accesses per each read
Only one index lookup per read
Sorted read-sized k-mers: to avoid random accesses to the index
Sequential scan of the read set and the index
✓
✓
Notes: To reduce the **number** of accesses per each read, we introduce read-sized k-mers.
Therefore, instead of extracting several k-mers per read and performing index lookup for each of them, [CLICK] we can use the whole read as one k-mer
[CLICK] And have only one index lookup per read
[CLICK] To avoid **random** accesses to the index, we introduce the **sorted** index of read-sized k-mers.
[CLICK] This sorted index allows finding exact matches via sequential scanning of the read sets and the index

## Slide 114: GenStore-EM: Data Structures
K-mer | Loc.
AAAAAAAAAA | 1, 8, …
AAAAAAAAAC | 51
AAAAAAAAAT | 23, 37
… | …
Sorted Read Table
ID | Read
873 | AAAAAAAAAA
232 | AAAAAAAAAG
17 | AAAAAAAACT
… | …
Sorted K-mer Index
Sorted
Read-sized
K-mers
Read
AAAAAAAAAA
Notes: I show the key idea of GenStore-EM with a simplified example in which each short read consists of 10 characters.
Suppose that we have two data structures:
[CLICK] 1) a sorted read table, each entry of which stores a read [CLICK] and its unique ID, and
[CLICK] 2) a sorted k-mer index, which contains all unique read sized k-mers of the reference genome,
[CLICK] along with each k-mer’s corresponding locations in the reference genome.
[CLICK] Each data structure is sorted by read/k-mer in alphabetical order.

## Slide 115: GenStore-EM: Finding a Match
K-mer | Loc.
AAAAAAAAAA | 1, 8, …
AAAAAAAAAC | 51
AAAAAAAAAT | 23, 37
… | …
Sorted Read Table
ID | Read
873 | AAAAAAAAAA
232 | AAAAAAAAAG
17 | AAAAAAAACT
… | …
Sorted K-mer Index
Comparator
Read = K-mer
Next
Exact match  Filter the read
Next
Notes: We sequentially scan through these data structures in three different ways based on the [CLICK] comparison result of the current read and k-mer.
[CLICK] First, when the current read and k-mer are identical,
[CLICK] we record the read as an exactly-matching read that can be filtered from further read mapping process
[CLICK] Then, we move to the next element in both arrays. [CLICK]

## Slide 116: GenStore-EM: Not Finding a Match
K-mer | Loc.
AAAAAAAAAA | 1, 8, …
AAAAAAAAAC | 51
AAAAAAAAAT | 23, 37
… | …
Sorted Read Table
ID | Read
873 | AAAAAAAAAA
232 | AAAAAAAAAG
17 | AAAAAAAACT
… | …
Sorted K-mer Index
Next
Comparator
Read > K-mer
Notes: if the read is alphabetically larger than the k-mer,
we conclude that the k-mer does not match any read
and go to the next element in the index (so that we can examine if the next k-mer).

## Slide 117: GenStore-EM: Not Finding a Match
Next
K-mer | Loc.
AAAAAAAAAA | 1, 8, …
AAAAAAAAAC | 51
AAAAAAAAAT | 23, 37
… | …
Sorted Read Table
ID | Read
873 | AAAAAAAAAA
232 | AAAAAAAAAG
17 | AAAAAAAACT
… | …
Sorted K-mer Index
Comparator
Read < K-mer
Not an exact match  Send to read mapper
Notes: if the k-mer is alphabeticall larger than the read,
we conclude that the read does not match any k-mer in index, and needs to be sent for the full read mapping process
Then, we go to the next element in the sorted read table (so that we can examine the next read).
Using this technique, GenStore-EM avoids random accesses and performs filtering using only simple low-cost logic

## Slide 118: GenStore-EM: Not Finding a Match
Next
K-mer | Loc.
AAAAAAAAAA | 1, 8, …
AAAAAAAAAC | 51
AAAAAAAAAT | 23, 37
… | …
Sorted Read Table
ID | Read
873 | AAAAAAAAAA
232 | AAAAAAAAAG
17 | AAAAAAAACT
… | …
Sorted K-mer Index
Comparator
Read < K-mer
Not an exact match  Send to read mapper
Avoids random accesses
Simple low-cost logic
✓
✓
Notes: if the k-mer is alphabeticall larger than the read,
we conclude that the read does not match any k-mer in index, and needs to be sent for the full read mapping process
Then, we go to the next element in the sorted read table (so that we can examine the next read).
Using this technique, GenStore-EM avoids random accesses and performs filtering using only simple low-cost logic

## Slide 119: GenStore-EM: Optimization
Read-sized k-mer index takes up a large amount of space (126 GB for human index) due to the larger number of unique k-mers
K-mer | Loc.
AAAAAAAAAA | 1, 8, …
AAAAAAAAAC | 51
AAAAAAAAAT | 23, 37
… | …
Sorted K-mer Index
Strong Hash Value
1
4
7
16
Using strong hash values instead of read-sized k-mers
reduces the size of the index by 3.9x
Notes: Despite the key benefits of the sorted read-sized k-mer index, this index takes up a large space (126 GB for human index) due to the large number of unique read-sized k-mers.
We further reduce the overheads of GenStore-EM, by replacing read-sized k-mers with a strong hash of each read that act as
Sorting criterion
Fingerprint of each entry
Using strong hash values instead of read-sized k-mers reduces the size of the index by 3.9x
While this index is still larger than the baseline k-mer index used in the conventional read mappers, our proposal is feasible for in-storage processing due to the large capacity and high internal bandwidth of modern NAND flash-based SSDs.

## Slide 120: GenStore-EM: Design
GenStore-Enabled SSD
Host System
Die#1
Plane#1
Plane#2
Die#4
P#1
P#2
⋯
Die#1
P#1
P#2
Die#4
P#1
P#2
⋯
Die#1
P#1
P#2
Die#4
P#1
P#2
⋯
⋯
Channel#1
Channel#2
Channel#N
❷ Exact-match filtering
SSD Controller
NAND Flash Array
SRTable
SKIndex
❶ Sequential Reads
DRAM
Batch#i-1
Batch#i
Batch#j-1
Batch#j
Comparator
SRTable Buffer
SKIndex Buffer
Data is evenly distributed between channels, dies, and planes
to leverage the full internal bandwidth of the SSD
Steps 1 and 2 are pipelined.
During filtering, GenStore-EM sends the unfiltered reads
to the host system.
Notes: Now I show the overall operational flow of GenStore-EM, [CLICK]
with SRTable and SKIndex in the NAND flash memory, [CLICK]
distributed across all channels and dies. [CLICK]
And the comparator logic located on the SSD controller.
GenStore-EM consists of two steps: [CLICK]
Step 1 reads the two data structures from NAND flash chips to the SSD’s internal DRAM [CLICK] in a batched manner
Step 2 performs exact-match filtering within each read batch, using simple comparator logic.
Steps 1 and 2 are performed in a pipelined manner. During filtering, GenStore-EM sends the unfiltered reads to the host system for full read mapping.

## Slide 121: GenStore
GenStore-EM for Exactly-Matching Reads
GenStore-NM for Non-Matching Reads
Notes: Now, let’s take a closer look at GenStore-NM

## Slide 122: GenStore-NM
Efficient chaining-based in-storage filter to prune most of the non-matching reads
Challenge: how to perform chaining inside the SSD
  For a read with Seeds to , the chaining score for can be calculated as
i > j > 1
Costly dynamic programming on many seeds in each read
Particularly challenging for long reads with many seeds
Determine potential matching locations (seeds) in the reference genome
Prune some seeds in the reference genome
Determine the exact differences between the read and the reference genome
Seeding
Seed Filtering
(e.g., Chaining)
Alignment
Notes: Using chaing, GenStore-NM filters most of the nonmatching reads, i.e., reads that would not align to any subsequence in the reference genome. Recall that chaining filter calculates a similarity score for each read (called chaining score) and filters read with no high-scoring potential matching locations.
Calculating a chaining score in the SSD is challenging
because finding the best chaining score requires performing [CLICK] many iterations of a dynamic programming algorithm for all seeds within a read,
This is particularly challenging for long reads since they have a large number of k-mers per read

## Slide 123: GenStore-NM: Mechanism
  Filters many non-aligning reads without costly hardware resources in the SSD
Probability
Chart: 
Number of seeds per read
High Alignment Probability
Alignment
Reads with a sufficiently large number of seeds
are very likely to align to the reference genome
GenStore-NM uses a light-weight chaining filter
  Selectively performs chaining only on reads with a small number of seeds
  Directly sends reads that require more complex chaining to the host system
✓
Notes: [CLICK] To reduce the cost of chaining, GenStore-NM GenStore-NM uses a light-weight chaining filter
[CLICK] Selectively performs chaining only on reads with a small number of seeds
[CLICK] And Directly send reads that require more complex chaining to the host system
This idea is based on our observation from analyzing a wide range of real world genomic read sets.
[CLICK] This figure shows alignment probability of a read in a long read dataset to subsequences in the reference genome, as a function of the number of seeds per read.
[CLICK] We observe that reads with a sufficiently large number of seeds are very likely to align to subsequences in the reference
genome. Such reads can be directly sent to the CPU for full read mapping (bypassing the in-storage filter).
[CLICK] We conclude that the selective light-weight chaining approach can filter many non-aligning reads without costly hardware resources in the SSD

## Slide 124: GenStore-NM: Mechanism
  Can filter many non-aligning reads without costly hardware resources in the SSD
Probability
Chart: 
Number of seeds per read
High Alignment Probability
Alignment
Reads with a sufficiently large number of seeds
are very likely to align to the reference genome
GenStore-NM uses a light-weight chaining filter
  Selectively performs chaining only on reads with a small number of seeds
  Directly sends reads that require more complex chaining to the host system
Details on GenStore-NM’s design are in the paper
Notes: [CLICK] To reduce the cost of chaining, GenStore-NM GenStore-NM uses a light-weight chaining filter
[CLICK] Selectively performs chaining only on reads with a small number of seeds
[CLICK] And Directly send reads that require more complex chaining to the host system
This idea is based on our observation from analyzing a wide range of real world genomic read sets.
[CLICK] This figure shows alignment probability of a read in a long read dataset to subsequences in the reference genome, as a function of the number of seeds per read.
[CLICK] We observe that reads with a sufficiently large number of seeds are very likely to align to subsequences in the reference
genome. Such reads can be directly sent to the CPU for full read mapping (bypassing the in-storage filter).
[CLICK] We conclude that the selective light-weight chaining approach can filter many non-aligning reads without costly hardware resources in the SSD

## Slide 125: Outline
Conclusions
Background
Motivation and Goal
Experimental Methodology
Temperature Analysis
Aggressor Row Active Time Analysis
Spatial Variation Analysis
Implications on Attacks and Defenses
Conclusions
Motivation and Goal
GenStore
Evaluation
Notes: I will now go into our results

## Slide 126: Evaluation Methodology
Read Mappers
Base: state-of-the-art software or hardware read mappers
  Minimap2 [Bioinformatics’18]: software mapper for short and long reads
  GenCache [MICRO’19]: hardware mapper for short reads
  Darwin [ASPLOS’18]: hardware mapper for long reads
GS: Base integrated with GenStore
SSD Configurations
SSD-L: with SATA3 interface (0.5 GB/s sequential read bandwidth)
SSD-M: with PCIe Gen3 interface (3.5 GB/s sequential read bandwidth)
SSD-H: with PCIe Gen4 interface (7 GB/s sequential read bandwidth)
Notes: We valuate the following systems:
[CLICK] Base: state-of-the-art software or hardware read mappers for both short and long reads
[CLICK] GS: Base integrated with the GenStore inside the SSD
We evaluate these mappers on systems with various SSD configurations, a low-end, medium-end, and high-end SSD
For other details about our methodology, please refer to the paper.

## Slide 127: Performance – GenStore-EM
For a read set with 80% exactly-matching reads
Chart: 
| Base | GS | Base | GS | Base | GS | SSD-L | SSD-M | SSD-H
Other | 170.17 | 69.24 | 154.65 | 74.71 | 159.07 | 73.31
Alignment | 0 | 0 | 0 | 0 | 0 | 0
Exec. time [sec]
Chart: 
| Base | GS | Base | GS | Base | GS | SSD-L | SSD-M | SSD-H
 | 44 | 8.8 | 6.2857 | 2.8229 | 4.2832 | 2.8229
 | 0 | 0 | 0 | 0 | 0 | 0
With the Software Mapper
With the Hardware Mapper
2.1× - 2.5× speedup compared to the software Base
1.5× – 3.3× speedup compared to the hardware Base
On average 3.92× energy reduction
29
2.5x
2.1x
2.1x
3.3x
1.5x
2.5x
Notes: We analyze the benefits of GenStore-EM for a 22-GB short read set where 80% of reads exactly match some subsequence in the reference genome and can be filtered.
We show the benefit of GS on software and hardware read mappers.
GS provides 2.1× - 2.5× speedup compared to the software Base
GS provides 1.5× – 3.3× speedup compared to the hardware Base
GS provides on average 3.92× energy reduction

## Slide 128: Performance – GenStore-NM
For a read set with 99.7% non-matching reads
Chart: 
| Base | GS | Base | GS | Base | GS | SSD-L | SSD-M | SSD-H
 | 30.028 | 1.564 | 5.362 | 0.78198 | 5.36 | 0.78198
Exec. time [sec]
Log scale
With the Software Mapper
With the Hardware Mapper
22.4× – 27.9× speedup compared to the software Base
6.8× – 19.2× speedup compared to the hardware Base
On average 27.2× energy reduction
Chart: 
| Base | GS | Base | GS | Base | GS | SSD-L | SSD-M | SSD-H
Time | 34.84 | 1.5537 | 22.55 | 0.77687 | 21.72 | 0.77687
22.4
29x
27.9x
19.2x
6.8x
6.8x
Notes: We analyze the benefits of GenStore-NM for a 12-GB long read set with very high genetic variation compared the the reference genome where 99.7% of reads do not match any subsequence in the reference genome.
We show the benefit of GS on software and hardware read mappers.
GS provides 22.4× – 27.9× speedup compared to the software Base
GS provides 6.8× – 19.2× speedup compared to the hardware Base
GS provides on average 27.2× energy reduction

## Slide 129: Area and Power
Based on Synthesis of GenStore accelerators using the Synopsys Design Compiler @ 65nm technology node
Logic unit | # of instances | Area [mm2] | Power [mW]
Comparator | 1 per SSD | 0.0007 | 0.14
K -mer Window | 2 per channel | 0.0018 | 0.27
Hash Accelerator | 2 per SSD | 0.008 | 1.8
Location Buffer | 1 per channel | 0.00725 | 0.37375
Chaining Buffer | 1 per channel | 0.008 | 0.95
Chaining PE | 1 per channel | 0.004 | 0.98
Control | 1 per SSD | 0.0002 | 0.11
Total for an 8-channel SSD | - | 0.2 | 26.6
Only 0.006% of a 14nm Intel Processor, less than 9.5% of the three ARM processors in a SATA SSD controller
Notes: We find area and power values of GenStore by synthesizing GenStore-EM and NM using 65nm technology node,
And find that for an 8-channel SSD, the area of GS is 0.2 mm square and the power is 26.6 watts
BY scaling the area to lower technology nodes, we observe that the area overhead of GS is 0.006% of an Intel processor and less than 9.5% of the of the three ARM processors in a SATA SSD controller.

## Slide 130: Other Results in the Paper
Effect of read set features on performance
  Data size (up to 440 GB)
  Filter ratio
Performance benefit of an implementation of GenStore outside the SSD
  In some cases, it provides performance benefits due more efficient streaming accesses
  Provides significantly lower benefit compared to GenStore
More detailed characterization of non-matching reads across different read mapping use cases and species
Notes: Let me briefly talk about other results that are included in the paper before concluding this talk. These include the following:

## Slide 131: Outline
Conclusions
Background
Motivation and Goal
Experimental Methodology
Temperature Analysis
Aggressor Row Active Time Analysis
Spatial Variation Analysis
Implications on Attacks and Defenses
Conclusions
Motivation and Goal
GenStore
Evaluation
Notes: Now, let me conclude by giving the summary.

## Slide 132: Conclusion
There has been significant effort into improving read mapping performance through efficient heuristics, hardware acceleration, accurate filters
Problem: while these approaches address the computation overhead, none of them alleviate the data movement overhead from storage
Goal: improve the performance of genome sequence analysis by effectively reducing unnecessary data movement from the storage system
Idea: filter reads that do not require the expensive alignment computation in the storage system to fundamentally reduce the data movement overhead
Challenges:
  Read mapping workloads can exhibit different behavior
  There are limited available hardware resources in the storage system
GenStore: the first in-storage processing system designed for genome sequence analysis to reduce both the computation and data movement overhead
Key Results: GenStore provides significant speedup (1.4x - 33.6x) and energy reduction (3.9x – 29.2x) at low cost
Notes: [CLICK] There has been significant effort into improving read mapping performance through efficient heuristics, hardware accelerators, and various filters that prune reads that do not require expensive computation.
[CLICK] While these approaches address the computation overhead in read mapping, None of them alleviate the data movement overhead from storage, whose impact becomes even larger when the computation overhead gets alleviated
[CLICK] Our goal is to Improve the performance of genome sequence analysis by effectively reducing unnecessary data movement from the storage system
[CLICK] The key idea is to Filter reads that do not require the expensive ASM computation in the storage system to fundamentally reduce the data movement overhead
CLICK] however, filtering reads inside SSD is challebging 1) Read mapping workloads can exhibit different behavior, and 2) There are limited available hardware resources in the storage system
[CLICK] To this end, we propose GenStore, The first in-storage processing system designed for genome sequence analysis to reduce both the computation/data movement overhead
[CLICK] GenStore provides high-performance and energy benefits compared to state-of-the-art HW and SW baselines

## Slide 133: GenStore: A High-Performance In-Storage Processing System for Genome Sequence Analysis
Nika Mansouri Ghiasi, Jisung Park, Harun Mustafa, Jeremie Kim, Ataberk Olgun,
Arvid Gollwitzer, Damla Senol Cali, Can Firtina, Haiyu Mao, Nour Almadhoun Alserr,
Rachata Ausavarungnirun, Nandita Vijaykumar, Mohammed Alser, and Onur Mutlu
Notes: Hi, I’m Nika, and today I will introduce GenStore: A High-Performance In-Storage Processing System
for Genome Sequence Analysis

## Slide 134: End-to-End Workflow of Genome Sequence Analysis
There are three key initial steps in a standard genome sequencing and analysis workflow
  Collection, preparation, and sequencing of a DNA sample in the laboratory
  Basecalling
  Read mapping
Genomic read sets can be obtained by
  Sequencing a DNA sample and storing the generated read set into the SSD of a sequencing machine
  Downloading read sets from publicly available repositories and storing them into an SSD
We focus on optimizing the performance of read mapping because sequencing and basecalling are performed only once per read set, whereas read mapping can be performed many times
  Analyzing the differences between a reads from an individual and many reference genomes of other individuals
  Repeating the read mapping step many times to improve the outcome of read mapping
Improving read mapping performance is critical in almost all genomic analyses that use sequencing
  45% of the execution time when discovering sequence variants in cancer genomics studies
  60% of the execution time when profiling the species composition of a multi-species (i.e., metagenomic) read

## Slide 135: Motivation
SSD-L
SSD-M
SSD-H
DRAM
Chart: 
| Base | SW-filtered | Ideal-ISF | Accelerator | Ideal-ISF+ACC
SSD-L | 97.56 | 76.6218 | 32.943 | 24.8 | 10.08
SSD-M | 78.44 | 55.588 | 25.1038 | 3.5428 | 1.44
SSD-H | 78.35 | 55.489 | 25.0669 | 2.0101 | 0.72203
DRAM | 75.16 | 51.98 | 1.6422
Chart: 
| Accelerator | ACC+Ideal-ISF
SSD-L | 24.8 | 10.08
SSD-M | 3.5428 | 1.44
SSD-H | 2.0101 | 0.72203
DRAM | 1.6422 | 1e-08
N/A
24.8
N/A
3.54
2.01
1.64
1.44
0.72
10.1
Execution time [sec]
ACC
SW-filter

## Slide 136: Motivation
State-of-the-art software read mapper, Minimap2
Chart: 
| Base | SW-filter | Ideal-ISF
SSD-L | 97.56 | 76.6218 | 32.943
SSD-H | 78.35 | 55.489 | 25.0669
DRAM | 75.16 | 51.98
Execution time [sec]
Base integrated with a software filter
that prunes 80% of exactly-matching reads
Base integrated with an
ideal in-storage filter
N/A
Notes: This plot shows the execution time of three read mapping systems.
Base refers to a State-of-the-art software read mapper, Minimap2
SW-filter refers to Base integrated with a software filter that prunes 80% of exactly-matching reads
Ideal-ISF refers to base integrated with an ideal in-storage filter than prunes 80% exactly matching reads inside the SSD

## Slide 137: Motivation
Chart: 
| Base | SW-filter | Ideal-ISF
SSD-L | 97.56 | 76.6218 | 32.943
SSD-H | 78.35 | 55.489 | 25.0669
DRAM | 75.16 | 51.98
Execution time [sec]
Low-end SSD with SATA3 interface (0.5 GB/s)
High-end SSD with PCIe Gen4 interface (7 GB/s)
Data preloaded in DRAM,
with no I/O overhead
N/A
Notes: To assess the impact of the storage subsystem, we evaluate each of the three mappers with different configurations
A low-end SSD, a high-end SSD, and DRAM which refers to an idealized scenario where all needed data is preloaded in DRAM with no I/O overhead

## Slide 138: Benefits of Ideal In-Storage Filter
Chart: 
| Base | SW-filter | Ideal-ISF
SSD-L | 97.56 | 76.6218 | 32.943
SSD-H | 78.35 | 55.489 | 25.0669
DRAM | 75.16 | 51.98
Execution time [sec]
The ideal in-storage filter significantly improves performance by
Reducing computation overhead
Reducing data movement overhead
N/A
Notes: Based on this plot, we make several observations, First…

## Slide 139: Overheads of Software Mappers
Chart: 
| Base | SW-filter | Ideal-ISF
SSD-L | 97.56 | 76.6218 | 32.943
SSD-H | 78.35 | 55.489 | 25.0669
DRAM | 75.16 | 51.98
Execution time [sec]
I/O has a significant impact on application performance
which can be alleviated at the cost of
expensive storage devices and interfaces
N/A
Notes: By comparing the high-end SSD, low-end SSD, and DRAM with no I/O overhead, we observe that
[CLICK] I/O has a significant impact on application performance
[CLICK] which can be alleviated at the cost of expensive storage devices and interfaces
However, it is challenging to scale a storage system’s capacity using only the high-end SSDs due to
[CLICK] the relatively smaller number of the PCIe slots in a server
[CLICK] And their significantly-higher prices

## Slide 140: Overheads of Software Mappers
Chart: 
| Base | SW-filter | Ideal-ISF
SSD-L | 97.56 | 76.6218 | 32.943
SSD-H | 78.35 | 55.489 | 25.0669
DRAM | 75.16 | 51.98
Execution time [sec]
SW-filter provides limited benefits compared to Base
N/A
The filtering process outside the SSD must compete
with the read mapping process for the resources in the system
Notes: Third, by comparing Base and SW-filter, we observe that despite a large number of needs that can be filtered, SW-filter does not provide significant benefits compared to base.
The limited speedup is mainly due to large number of accesses to the index structure for several k-mers per each read.
[CLICK] This shows that as opposed to the instorage filter, the filtering process outside the SSD must compete with the read mapping process for the resources in the system

## Slide 141: Overheads of Hardware Mappers
Chart: 
| Accelerator | Ideal-ISF
SSD-L | 24.8 | 10.08
SSD-H | 2.0101 | 0.72203
DRAM | 1.6422 | 1e-08
Execution time [sec]
24.8
10.1
23%
The ideal in-storage filter significantly improves performance
Even the high-end SSD does not fully alleviate the storage bottleneck
N/A
Notes: This figures shows similar analysis but with a state-of-the-art hardware read mapper, gencache, and its integration with the ideal in-storage filter.
We observe that Even the high-end SSD does not fully alleviate the storage bottleneck in this case
This is because by addressing computation overhead using the accelerator, I/O turns into a more serious bottleneck.
However, we observe that the ideal n-storage filter significantly improves performance since it addresses both the computation and data movement overheads.

## Slide 142: Ideal-OSF
Execution time of an ideal in-storage filter:
Execution time of an ideal outside-storage filter:
  60% slower than Ideal-ISF in our analysis

## Slide 143: Comparison to PIM
Even though read mapping applications could also benefit from other near-data, in-storage processing can fundamentally address the data movement problem by filtering large, low-reuse data where the data initially resides.
Even if an ideal accelerator achieved a zero execution time, there would still exist the need to bring the data from storage to the accelerator.
  2.15x slower than the execution time that Ideal-ISF+ACC provides in our motivational analysis
In-storage filter can be integrated with any read mapping accelerator, including PIM accelerators, to alleviate their data movement overhead.

## Slide 144: Long Read Use Cases

## Slide 145: FTL
GenStore-Enabled SSD
GenStore SSD Controller
Core
Core
Core
SSD-LV
ACC
DRAM
L2P
Mappings
Flash
Ctrl.#1
Flash
Ctrl.#N
⋯
⋯
CH-LV
ACC#1
CH-LV
ACC#N
GenStore
Metadata
① Start analysis
⑤ Unfiltered data
NAND
Die#4
NAND
Die#1
⋯
NAND
Die#4
NAND
Die#1
⋯
③ Full-bandwidth read
② Preparation
Flush
Load
GenStore
FTL
④ Filtering
Host System
❷
❸
❶

## Slide 146: FTL: Metadata
GenStore metadata includes the mapping information of the data structures necessary for read mapping acceleration
In accelerator mode, GenStore also keeps in internal DRAM other metadata structures of the regular FTL
  Examples include the page status table and block read counts which need to be updated during the filtering process
We carefully design GenStore to only sequentially access the underlying NAND flash chips while operating as an accelerator
  Requires only a small amount of metadata to access the stored data

## Slide 147: FTL: Data Placement
GenStore needs to properly place its data structures to enable the full utilization of the internal SSD bandwidth
When each data structure is initially written to the SSD, GenStore sequentially and evenly distributes it across NAND flash chips
GenStore can specify the physical location of a 30-GB data structure by maintaining only the list of 1,250 (30 GB/24 MB) physical block addresses
It significantly reduces the size of the necessary mapping information from 300 MB (with conventional 4-KiB page mapping) to only 5 KB (1,250 4 bytes)

## Slide 148: FTL: SSD Management Tasks
In accelerator mode, GenStore only reads data structures to perform filtering, and does not write any new data
  GenStore does not require any write-related SSD-management tasks such as garbage collection and wear-leveling
The other tasks necessary for ensuring data reliability can be done before or after the filtering process
  GenStore significantly limits the amount of data whose retention age would exceed the manufacturer-specified threshold since GenStore’s filtering process takes a short time.
  GenStore-FTL can easily avoid read disturbance errors for data with high read counts since GenStore sequentially reads NAND flash blocks only once during filtering

## Slide 149: Data Sizes
Conventional k-mer index in Minimap2 + reference genome: 7 GB (k = 15)
Read-sized k-mer index before optimization: 126 GB (k= 150)
Read-sized k-mer index after optimization: 32 GB (k = 150)

## Slide 150: SSD Specs
SSD-L: SATA3 interface (0.5 GB/s sequential read)
  1.2 GB/s per channel bandwidth
  8 channels
SSD-L: PCIe Gen3 M.2 interface (3.5 GB/s sequential read)
  1.2 GB/s per channel bandwidth
  16 channels
SSD-L: PCIe Gen4 interface (7 GB/s sequential read)
  1.2 GB/s per channel bandwidth
  16 channels

## Slide 151: Evaluation Methodology
Performance modeling
  Ramulator for DRAM timing
  MQSim for SSD timing
  We model the end-to-end throughput of GenStore based on the throughput of each GenStore pipeline stage
    Accessing NAND flash chips
    Accessing internal DRAM
    Accelerator computation
    Transferring unfiltered data to the host
Real system results
  AMD EPYC 7742 CPU
  1TB DDR4 DRAM
  AMD μProf
Notes: I won’t go into details, but you can refer to our paper for more details about our evaluation methdology.

## Slide 152: GenStore-NM
GenStore-Enabled SSD
Host System
Flash Array
Input
Read Set
SSD Controller
DRAM
KmerIndex
Seed Finder
Location Buffer
① Reads
Chaining-Based Filter
(Filters low-score reads)
❸
M ≤ # of Seeds < N
Seed Count-Based Filter
(Filters if # of Seeds < M)
❷
# of Seeds ≥ N
High chaining score
❶
④ Seeds
③ Query
K-mer Window
Hash Acc.
K-mers
②

## Slide 153: Chaining Processing Element

## Slide 154: GenStore-EM
Chart: 
| Base | SIMD | GS-Ext | GS | Base | SIMD | GS-Ext | GS | Base | SIMD | GS-Ext | GS | SSD-L | SSD-M | SSD-H
Other | 101.8 | 128.44 | 119.24 | 52.78 | 73.98 | 81.378 | 31.69 | 31.69 | 86.17 | 94.787 | 31.92 | 31.92
Alignment | 68.37 | 16.46 | 16.46 | 16.46 | 80.67 | 43.02 | 43.02 | 43.02 | 72.9 | 41.39 | 41.39 | 41.39
Chart: 
| Base | GS-Ext | GS | Base | GS-Ext | GS | Base | GS-Ext | GS | SSD-L | SSD-M | SSD-H
 | 44 | 108.4 | 8.8 | 6.2857 | 15.4857 | 2.8229 | 4.2832 | 7.7429 | 2.8229
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Exec. time [sec]
44
108
15
GS-Ext provides significant performance improvements
over both Base and SIMD in SSD-M and SSD-H.
GS-Ext provides limited benefits over SIMD in SSD-L
due to low external I/O bandwidth.
With the Software Mapper
With the Hardware Mapper
Notes: GS-Ext provides significant performance
improvements over both Base and SIMD in SSD-M and SSD-H. However,
GS-Ext provides limited benefits over SIMD in SSD-L since
its performance is bottlenecked by the low external I/O bandwidth.

## Slide 155: GenStore-NM
Chart: 
| Base | GS | Base | GS | Base | GS | SSD-L | SSD-M | SSD-H
Time | 34.84 | 1.5537 | 22.55 | 0.77687 | 21.72 | 0.77687
Chart: 
| Base | GS-Ext | GS | Base | GS-Ext | GS | Base | GS-Ext | GS | SSD-L | SSD-M | SSD-H
 | 30.028 | 30.056 | 1.564 | 5.362 | 4.2937 | 0.78198 | 5.36 | 2.1469 | 0.78198
GS-Ext performs significantly slower than Base (2.28x - 1.91x)
on all systems.
With the Software Mapper
With the Hardware Mapper
Notes: GS-Ext performs significantly slower than Base (2.28x - 1.91x) on all systems.

## Slide 156: Effect of Inputs on GenStore-EM
Normalized exec. time
Read set size:
Exact match:
Chart: 
| 75% | 85% | 75% | 85% | 75% | 85% | 1x | 10x | 20x
Base | 1 | 1 | 1 | 1 | 1 | 1
GS | 0.50504 | 0.30763 | 0.27598 | 0.19436 | 0.28937 | 0.16534
Chart: 
| 75% | 85% | 75% | 85% | 75% | 85% | 1x | 10x | 20x
Base | 1 | 1 | 1 | 1 | 1 | 1
GS | 0.65906 | 0.65906 | 0.33838 | 0.33838 | 0.31986 | 0.31986
With the Software Mapper
With the Hardware Mapper

## Slide 157: Effect of Inputs on GenStore-NM
Chart: 
| 0.3% | 37% | 0.3% | 37% | 0.3% | 37% | 1x | 10x | 20x
Base | 1 | 1 | 1 | 1 | 1 | 1
GS | 0.029734 | 0.68811 | 0.03427 | 0.67399 | 0.035084 | 0.66259
Chart: 
| 0.3% | 37% | 0.3% | 37% | 0.3% | 37% | 1x | 10x | 20x
Base | 1 | 1 | 1 | 1 | 1 | 1
GS | 0.14589 | 0.37024 | 0.14582 | 0.37002 | 0.14581 | 0.37001
Normalized exec. time
Read set size:
Align. rate:
0.69
0.67
0.66
With the Software Mapper
With the Hardware Mapper

## Slide 158: MegIS High-Performance, Energy-Efficient, and Low-Cost Metagenomic Analysis with In-Storage Processing
Nika Mansouri Ghiasi
Mohammed Alser Jisung Park Onur Mutlu
Mohammad Sadrosadati Harun Mustafa Arvid Gollwitzer Can Firtina
Julien Eudine Haiyu Mao Joël Lindegger Meryem Banu Cavlak
Notes: Hi everyone, I am Nika, and today, I will talk about
MegIS: High-Performance, Energy-Efficient, and Low-Cost Metagenomic Analysis with In-Storage Processing

## Slide 159: MegIS Discussion
Main presentation
Detailed motivation
Overview of MegIS’s steps
MegIS FTL
Multi-sample analysis
SSD configurations
Detailed results

## Slide 160: Outline
Conclusion
Background
Motivation and Goal
MegIS
Evaluation

## Slide 161: What is Metagenomics?
Metagenomics: Study of genome sequences of diverse organisms
within a shared environment (e.g., blood, ocean, soil)
Overcomes the limitations of traditional genomics
  Bypasses the need for analyzing individual species in isolation
Notes: Metagenomics: Study of genome sequences of diverse organisms within a shared environment (e.g., blood, ocean, soil)
Metagenomics overcomes the limitations of traditional genomics
Because it bypasses the need for culturing individual species in isolation,
which is not feasible in many important clinical and environmental use cases

## Slide 162: What is Metagenomics?
Has led to groundbreaking advances
Precision medicine
Understanding microbial diversity of an environment
Discovering early warnings of communicable diseases
Metagenomics: Study of genome sequences of diverse organisms
within a shared environment (e.g., blood, ocean, soil)
Notes: Therefore, metagenomics has led to ground-breaking advances
In many fields such as
Precision medicine
Understanding microbial diversity of an environment
Discovering early warnings of communicable diseases

## Slide 163: Metagenomic Analysis
A large database
containing information
on many species
Metagenomic sample
with species that
are not known in advance
Preparation
of Input Queries
Query
K-mers
…
GCTCA
CTCAT
TCATG
Presence/Absence Identification
Abundance
Estimation
V. cholerae
E. coli
SARS-CoV-2
Chart: 
| Species#1 | Species#2 | Species#3
 | 0.6 | 0.25 | 0.15
(e.g., > 100 TBs in emerging databases)
Notes: Since the species that are present in a metagenomic sample are not known in advance,
Metagenomic analysis performs tasks to enable an understanding of the sample’s composition.
Here, I am going to start with showing the genomic sequences of the organisms in the metagenomic sample,
To perform metagenomic analysis
First, many tools extract k-mers (i.e., subsequences of length k) from the input queries in a sample
Second, they find species present/absent in the sample by searching the query k-mers against a large metagenomic database containing information on many species’ genomes.
Many databases used for various use cases can be very large, for example, to several TBs or more than a hundred TBs in emerging databases
This step outputs the IDs of the species that are identified to be present in the sample
Finally, some applications perform a third optional step of abundance estimatimation,
which calculates the relative frequencies of the occurrence of different species in the sample

## Slide 164: Outline
Conclusion
Background
Motivation and Goal
MegIS
Evaluation

## Slide 165: Motivation
Case study of the performance of metagenomic analysis tools
With various state-of-the-art SSD configurations
Normalized Throughput
Database Size (Terabyte)
I/O data movement causes significant performance overhead
Chart: 
| 0.7 | 1.4
No I/O | 1 | 1
Performance-Optimized | 0.31054 | 0.24299
Cost-Optimized | 0.03627 | 0.025496
3.2x
4.1x
27.6x
39.2x
Notes: We perform a case study on the throughput of metagenomic analysis tools
with various state-of-the-art cost-optimized or performance-optimized SSD configurations
And normalized throughput compared to a hypothetical configuration with zero performance overhead due to storage I/O
We observe that I/O data movement causes significant performance overhead

## Slide 166: Motivation
Case study on the throughput of metagenomic analysis tools
With Various state-of-the-art SSD configurations
Normalized Throughput
Database Size (Terabyte)
Chart: 
| 0.7 | 1.4
SSD-C | 0.03627 | 0.025496
SSD-P | 0.31054 | 0.24299
No-I/O | 1 | 1
I/O data movement causes significant performance overhead
Cost-Optimized
Performance-Optimized
No I/O
I/O becomes an even larger overhead (by 2.7x)
in systems where other bottlenecks are alleviated

## Slide 167: I/O Overhead is Hard to Avoid
I/O overhead due to accessing large, low-reuse data is hard to avoid
Sampling techniques to shrink database sizes
Keeping all data required by metagenomic analysis
completely and always resident in main memory
Reduce accuracy to levels unacceptable for many use cases
Energy inefficient, costly, unscalable, and unsustainable
Database sizes increase rapidly (doubling every few months)
Different analyses need different databases
[Wood+, Genome Biology’19], [Ounit+, BMC Genomics’15], [Kim+, Genome Research’16], …
Notes: I/O overhead from moving large, low-reuse data is hard to avoid
One might think it is possible to avoid this overhead by
using sampling techniques to shrink database sizes
However, this approach inevitably reduces accuracy to levels unacceptable for many use cases
Or another potential solution might seem to be
Keeping all data required by metagenomic analysis
completely and always resident in main memory
However, this is energy inefficient, costly, unscalable, and unsustainable due to two reasons
First, the sizes of metagenomic databases (which are already large, i.e., in some recent examples, exceeding a hundred terabytes) have been increasing rapidly.
For example, recent trends show the doubling of different important databases in only several months
Second, regardless of the sizes of individual databases, different analyses need different databases,
with information from different sets of genomes or with varying parameters.
Therefore, it is inefficient and unsustainable to maintain all data required by all possible analyses in main memory at all times

## Slide 168: Our Goal
Improve metagenomic analysis performance
by reducing large data movement overhead
from the storage system
in a cost-effective manner and with high accuracy
Notes: Motivated by these points, Our Goal is to Improve metagenomic analysis performance
by reducing the large data movement overhead from the storage system in a cost-effective manner

## Slide 169: Challenges of In-Storage Processing
No metagenomic analysis tools can run in-storage due to SSD limits
  Long latency of NAND flash chips
  Limited DRAM capacity inside the SSD
  Limited DRAM bandwidth inside the SSD
SSD DRAM
⋯
SSD
Controller
Cores
FTL
⋯
SSD
Cntrl
Cntrl
Channel#N
Channel#1
Notes: While In-Storage Processing (ISP) can be a promising direction to achieve our goal by processing data directly inside the storage device,
none of the existing approaches can be effectively implemented
as an ISP system due to limited hardware resources in the SSD such as
  Long latency of NAND flash chips
  Limited DRAM capacity inside the SSD
  And its limited bandwidth

## Slide 170: Outline
Conclusion
Background
Motivation and Goal
MegIS
Evaluation

## Slide 171: MegIS: Metagenomics In-Storage
First in-storage system for end-to-end metagenomic analysis
Idea: Cooperative in-storage processing for metagenomic analysis
  Hardware/software co-design between the storage system and host system
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Notes: Which is the first in-storage processing system for end-to-end metagenomic analysis
The key idea of megis is Cooperative ISP for metagenomics
Which is enabled by a synergistic hardware/software co-design between the storage system and the host system

## Slide 172: MegIS’s Steps
A large database
containing information
on many species
Metagenomic sample
with species that
are not known in advance
Preparation
of Input Queries
Query
K-mers
…
GCTCA
CTCAT
TCATG
Presence/Absence Identification
V. cholerae
E. coli
SARS-CoV-2
Abundance
Estimation
Chart: 
| Species#1 | Species#2 | Species#3
 | 0.6 | 0.25 | 0.15
Step 1
Step 2
Step 3

## Slide 173: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Notes: To (i) leverage and (ii) orchestrate the capabilities of both systems, megis includes hw/sw co-design in 5 directions

## Slide 174: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Step 1
Task partitioning and mapping
Each step executes
in its most suitable system
Step 2
Step 3

## Slide 175: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Step 1
Step 2
Step 3
Task partitioning and mapping
Each step executes
in its most suitable system

## Slide 176: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Storage-aware algorithms
Enable efficient
access patterns to the SSD
Step 1
Step 2
Step 3
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Task partitioning and mapping
Each step executes
in its most suitable system

## Slide 177: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
ACC
ACC
Cntrl
Cntrl
Channel#N
Channel#1
Lightweight in-storage accelerators
Minimize SRAM/DRAM buffer spaces needed inside the SSD
Step 1
Step 2
Step 3
Storage-aware algorithms
Enable efficient
access patterns to the SSD
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Task partitioning and mapping
Each step executes
in its most suitable system

## Slide 178: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
MegIS
FTL
MegIS
Metadata
Cntrl
Cntrl
Channel#N
Channel#1
Data mapping scheme and Flash Translation Layer (FTL)
Specialize to the characteristics of metagenomic analysis
Leverage the SSD’s full internal bandwidth
Step 1
Step 2
Step 3
Storage-aware algorithms
Enable efficient
access patterns to the SSD
Lightweight in-storage accelerators
Minimize SRAM/DRAM buffer spaces needed inside the SSD
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Task partitioning and mapping
Each step executes
in its most suitable system
ACC
ACC
Notes: 6 mins until here

## Slide 179: Step 1 Overview
A large database
containing information
on many species
Metagenomic sample
with species that
are not known in advance
Presence/Absence Identification
V. cholerae
E. coli
SARS-CoV-2
Abundance
Estimation
Chart: 
| Species#1 | Species#2 | Species#3
 | 0.6 | 0.25 | 0.15
Preparation
of Input Queries
Query
K-mers
…
GCTCA
CTCAT
TCATG
Step 1
Step 2
Step 3

## Slide 180: Step 1 Overview
MegIS employs sorted data structures
to avoid expensive random accesses to the SSD
  Extract k-mers from the sample
  Sort the k-mers (database is sorted offline)
Preparation
of Input Queries
Query
K-mers
…
GCTCA
CTCAT
TCATG
MegIS executes Step 1 in the host system
  Benefits from larger DRAM and more powerful computation
  Incurs fewer writes to NAND flash chips (than processing this step in the SSD)
  Enables overlapping Step 1 with Step 2
To execute Step 1 efficiently in the host system, MegIS needs to:
  Avoid significant overhead due to data transfer time between the steps
  Minimize performance and lifetime overheads even when host DRAM cannot hold all query k-mers
Notes: MegIS works with lexicographically-sorted data structures to avoid expensive random accesses to the SSD
Therefore, to prepare the input queries, MegIS 1) extracts k-mers from the sample,
2) sorts the k-mers
We execute this step in the host system for three reasons.
First, this step benefits from the relatively larger DRAM and more powerful computation resources in the host.
Second, due to the large host-side DRAM, performing this step in the host leads to significantly fewer writes to the flash chips
Third, by leveraging the host system for this step, we enable pipelining and overlapping Step 1 with Step 2 (which searches the large, low-reuse database).
To efficiently execute Step 1 on the host system, we need to ensure that
First, partitioning the application between the host and the SSD does not incur significant overheads due to data transfer time.
Second, minimize performance and lifetime overheads even when the host DRAM cannot hold all the extracted query k-mers

## Slide 181: Step 1 Design
Divide k-mers into independent partitions by their alphabetical range
  Can overlap operations on different partitions
Host DRAM
Host CPU
Read
Input Queries
ACGTTACGATT…
ACGTT
⋯
Query
K-mers
CGTTA
GTTAC
MegIS-Enabled SSD
Partition
A
ACGTC
ACTTT
ATGAT
⋯
⋯
C
CATTA
CTATG
CCGCA
⋯
G
GTTAC
GGTCC
GACAG
⋯
⋯
A
ACGTC
ACTTT
ATGAT
⋯
CATTA
CTATG
CCGCA
⋯
Overlap Step 1’s sorting
with Data transfer
and Step 2’s In-storage operations
Notes: To this end, we design an input processing scheme
That extracts k-mers from the sample and
divides the k-mers into independent partitions, each corresponding to an alphabetical range.
This enables overlapping the sorting on one partition with transfer and operations of its previous partitions.
Second, for scenarios where even host DRAM is not large enough to buffer all query k-mers,
the fact that these partitions are independent allows megis to pin some partitions to the host dram
and pin the others to the SSD. This way, megis can
avoid unnecessary movement of k-mers due to page swaps

## Slide 182: Step 2 Overview
A large database
containing information
on many species
Metagenomic sample
with species that
are not known in advance
Abundance
Estimation
Chart: 
| Species#1 | Species#2 | Species#3
 | 0.6 | 0.25 | 0.15
Preparation
of Input Queries
Query
K-mers
…
GCTCA
CTCAT
TCATG
Step 1
Presence/Absence Identification
V. cholerae
E. coli
SARS-CoV-2
Step 2
Step 3

## Slide 183: Step 2 Overview
  Identify the common k-mers between the query k-mers
  and the database k-mers
  Retrieve the species IDs
  of the common k-mers
MegIS executes Step 2 in the SSD
  Accesses large data with low reuse
  Involves lightweight computation
To execute Step 2 efficiently in the SSD, MegIS needs to:
  Leverage internal bandwidth efficiently
  Not require expensive hardware inside the SSD
  (e.g., large DRAM bandwidth/capacity and costly logic units)
Presence/Absence Identification
V. cholerae
E. coli
SARS-CoV-2
Notes: In Step 2, MegIS finds the species present in the sample
by 1) Identifying the intersecting k-mers between the query k-mers and the database
and 2) Retrieve the taxonomic IDs of intersecting k-mers
We perform this step inside the SSD since it requires streaming the
large database with low reuse and involves only lightweight computation.
To efficiently execute this step in the SSD,
MegIS should leverage the full internal bandwidth without requiring expensive hardware resources inside the SSD
(e.g., large internal DRAM size/bandwidth and costly logic units).

## Slide 184: Step 2 Design: Identifying the Common K-mers
Challenge: Limited internal DRAM bandwidth
SSD DRAM
SSD Controller
MegIS-Enabled
SSD
Channel#1
Channel#N
AAAAA
TAACC
CAAAA
AGTTT
TTGGT
CCGTG
⋯
⋯
⋯
⋯
Database K-mers
Query K-mers
from the Host
CGTCA
⋯
Common
K-mers
⋯
AGTTT
Database K-mers
from Flash Chips
Notes: Relying solely on the SSD’s internal DRAM to buffer
Database k-mers that are stored in the NAND flash chips and accessed at full channel bandwidth,
and
query k-mers from the host system
and buffering the results
During in-storage processing and
can pressure the valuable internal DRAM bandwidth

## Slide 185: Step 2 Design: Identifying the Common K-mers
Challenge: Limited internal DRAM bandwidth
SSD DRAM
SSD Controller
MegIS-Enabled
SSD
Channel#1
Channel#N
AAAAA
TAACC
CAAAA
AGTTT
TTGGT
CCGTG
⋯
⋯
⋯
⋯
Database K-mers
Query K-mers
from the Host
CGTCA
⋯
Intersect
Intersect
Buffer
Buffer
Compute directly on the flash data streams
Reduce buffer size based on application features
K-mer Register
K-mer Register
K-mer Register
K-mer Register
Write to DRAM
Common K-mers
[Zou+, MICRO’22]
Notes: To address this challenge, we adopt an approach that
processes data directly from flash chips without buffering it in internal DRAM.
we utilize key features of MegIS to determine the minimum required buffer size.
This approach allows MegIS to compute directly on the flash data stream using only two registers, thus maintaining a low cost.
Finally, we write the intersecting K-mers to the SSD DRAM to be analyzed in the next step

## Slide 186: Step 2 Design: Retrieving the Species ID
Space-Inefficient
MegIS retrieves the species IDs of the common k-mers by looking up a sketch database
K-mer | ID
AAAAA | 1,5
AAAAC | 6
AATCC | 2, 9
… | …
Space-Efficient
Slow inside the SSD
due to long
NAND flash latency
Notes: Storing this information for many species can be space-inefficient
Therefore,
some approaches provide data structures to encode the k-mer information in a space-efficient manner.
Despite the benefits, these approaches typically require many pointer-chasing operations for each lookup.
Performing these operations inside the SSD is challenging due to large latency of NAND flash chips
We provide an intermediate approach, K-mer Sketch Streaming that is optimized for in-storage processing
KSS leads to
significantly smaller data structures compared to the baseline tables
but is still larger compared to state-of-the-art compact structures
However, it is much more suitable for ISP due to its more efficient streaming accesses

## Slide 187: Step 2 Design: Retrieving the Species ID
Space-Inefficient
MegIS retrieves the species IDs of the common k-mers by looking up a sketch database
K-mer | ID
AAAAA | 1,5
AAAAC | 6
AATCC | 2, 9
… | …
Space-Efficient
7.5x Smaller
2.1× Larger
K-mer Sketch Streaming
K-mer Sketch Streaming is much more suitable for in-storage processing
due to its streaming accesses
Notes: Storing this information for many species can be space-inefficient
Therefore,
some approaches provide data structures to encode the k-mer information in a space-efficient manner.
Despite the benefits, these approaches typically require many pointer-chasing operations for each lookup.
Performing these operations inside the SSD is challenging due to large latency of NAND flash chips
We provide an intermediate approach, K-mer Sketch Streaming that is optimized for in-storage processing
KSS leads to
significantly smaller data structures compared to the baseline tables
but is still larger compared to state-of-the-art compact structures
However, it is much more suitable for ISP due to its more efficient streaming accesses

## Slide 188: Step 2 Design: Retrieving the Species ID
Space-Inefficient
MegIS retrieves the species IDs of the common k-mers by looking up a sketch database
K-mer | ID
AAAAA | 1,5
AAAAC | 6
AATCC | 2, 9
… | …
Space-Efficient
7.5x Smaller
2.1× Larger
K-mer Sketch Streaming
K-mer Sketch Streaming is much more suitable for in-storage processing
due to its streaming accesses
Design details are in the paper
Notes: Storing this information for many species can be space-inefficient
Therefore,
some approaches provide data structures to encode the k-mer information in a space-efficient manner.
Despite the benefits, these approaches typically require many pointer-chasing operations for each lookup.
Performing these operations inside the SSD is challenging due to large latency of NAND flash chips
We provide an intermediate approach, K-mer Sketch Streaming that is optimized for in-storage processing
KSS leads to
significantly smaller data structures compared to the baseline tables
but is still larger compared to state-of-the-art compact structures
However, it is much more suitable for ISP due to its more efficient streaming accesses

## Slide 189: Step 3
A large database
containing information
on many species
Metagenomic sample
with species that
are not known in advance
Preparation
of Input Queries
Query
K-mers
…
GCTCA
CTCAT
TCATG
Step 1
Presence/Absence Identification
V. cholerae
E. coli
SARS-CoV-2
Step 2
Abundance
Estimation
Chart: 
| Species#1 | Species#2 | Species#3
 | 0.6 | 0.25 | 0.15
Step 3

## Slide 190: Step 3
MegIS performs additional analysis on species identified in the sample to estimate their abundance
MegIS can flexibly integrate with different approaches
Lightweight statistical approaches: Directly uses the output of Step 2
More accurate and costly read mapping: MegIS facilitates integration by preparing mapping indexes in the SSD
Abundance
Estimation
Chart: 
| Species#1 | Species#2 | Species#3
 | 0.6 | 0.25 | 0.15
Step 3 and MegIS FTL are in the paper

## Slide 191: Outline
Conclusion
Background
Motivation and Goal
MegIS
Evaluation

## Slide 192: Evaluation Methodology Overview (I)
Performance, Energy, and Power Analysis
Baseline Comparison Points
Performance-optimized software, Kraken2 [Genome Biology’19]
Accuracy-optimized software, Metalign [Genome Biology’20]
PIM hardware-accelerated tool (using processing-in-memory), Sieve [ISCA’21]
SSD Configurations
SSD-C: with SATA3 interface (0.5 GB/s sequential read bandwidth)
SSD-P: with PCIe Gen4 interface (7 GB/s sequential read bandwidth)
Hardware Components
Synthesized Verilog model for the in-storage accelerators
MQSim [Tavakkol+, FAST’18] for SSD’s internal operations
Ramulator [Kim+, CAL’15] for SSD’s internal DRAM
Software Components
Measure on a real system:
AMD® EPYC® CPU with 128 physical cores
1-TB DRAM
Notes: We model performance, energy, and power of the systems based on the latency and throughput of each hardware-based and software-based component
We valuate the following baselines:
...
We evaluate these tools on systems with cost-optimized and performance-optimized SSD configurations

## Slide 193: Evaluation Methodology Overview (II)
Metagenomic Analysis Task
Finding species present in the sample
Analysis of the abundance estimation task is in the paper
Metagenomic Samples
With varying degrees of genetic diversity
  Low
  Medium
  High

## Slide 194: Speedup over Software (with Cost-Optimized SSD)
MegIS provides significant speedup over both
Performance-Optimized and Accuracy-Optimized baselines
Speedup
Performance-Optimized
MegIS
Accuracy-Optimized
Sample Genetic Diversity
Chart: 
| Low | Med | High | GMean
P-Opt | 1 | 1 | 1 | 1
A-Opt | 0.43101 | 0.38921 | 0.35039 | 0.38881
MS | 5.3489 | 5.6406 | 6.3871 | 5.7761
SSD-C
5.8x
14.9x
Chart: 
| Low | Med | High | GMean
P-Opt | 1 | 1 | 1 | 1
A-Opt | 0.43101 | 0.38921 | 0.35039 | 0.38881
MS | 5.3489 | 5.6406 | 6.3871 | 5.7761
SSD-C
5.8x
Sample Genetic Diversity
14.9x
Notes: We analyze the benefits of MegIS for samples with low, medium, and high genetic diversity,
And here I am showing for a cost optimized-SSD
We observe that compared to both P-Opt and A-Opt
MegIS provides significant speedups

## Slide 195: Speedup over Software (with Performance-Optimized SSD)
MegIS provides significant speedup over both
Performance-Optimized and Accuracy-Optimized baselines
Speedup
Performance-Optimized
MegIS
Accuracy-Optimized
Sample Genetic Diversity
Chart: 
| Low | Med | High | GMean
P-Opt | 1 | 1 | 1 | 1
A-Opt | 0.3836 | 0.29101 | 0.31974 | 0.32925
MS | 2.6617 | 3.6664 | 6.5218 | 3.9926
SSD-P
4.0x
12.1x
MegIS improves performance on both
cost-optimized and performance-optimized SSDs

## Slide 196: Speedup over the PIM Hardware Baseline
4.9x
Chart: 
| Low | Med | High | GMean
 | 1 | 1 | 1 | 1
 | 4.8422 | 4.8446 | 5.0596 | 4.9144
Chart: 
| Low | Med | High | GMean
 | 1 | 1 | 1 | 1
 | 1.462 | 1.7798 | 2.7359 | 1.9237
Speedup
SSD-C
PIM
MegIS
1.9x
SSD-P
Sample Genetic Diversity
Sample Genetic Diversity
PIM
MegIS
MegIS provides significant speedup over the PIM baseline
Notes: Similarly, we evaluate megis compared to the pim baseline
and show that on systems with cost-optimized
and performance-optimized ssds,
MegiS significantly outperforms the PIM baseline

## Slide 197: Reduction in Energy Consumption
On average across different input sets and SSDs
Chart: 
| Perf-Opt | Acc-Opt | PIM | MegIS
 | 1 | 0.35526 | 2.8421 | 5.4
GeoMean Energy Reduction
(Higher is Better)
MegIS provides significant energy reduction over
the Performance-Optimized, Accuracy-Optimized, and PIM baselines
5.4x
15.2x
1.9x
Same
accuracy
Notes: Next, we show megis's energy reduction on average accross different input sets and SSDs and observe that megis provides...

## Slide 198: Accuracy, Area, and Power
Accuracy
Same accuracy as the accuracy-optimized baseline
Significantly higher accuracy than the performance-optimized and PIM baselines
  4.6 – 5.2× higher F1 score
  3 – 24% lower L1 norm error
Area and Power
Total for an 8-channel SSD:
Area: 0.04 mm2
Power: 7.658 mW
(Only 1.7% of the area and 4.6% of the power consumption
of three ARM Cortex R4 cores in an SSD controller)
Notes: MegIS provides all these benefits while achieving high accuracy

## Slide 199: System Cost-Efficiency
GMean Speedup
Chart: 
| Perf-Opt ($) | Acc-Opt ($) | Perf-Opt($$$) | Acc-Opt ($$$) | MegIS ($)
 | 1 | 0.81324 | 6.8304 | 2.2454 | 16.1756
Cost-optimized system ($): With SSD-C and 64-GB DRAM
Performance-optimized system ($$$): With SSD-P and 1-TB DRAM
MegIS outperforms the baselines
even when running on a much less costly system
($)
($)
($$$)
($$$)
($)
7.2x
2.4x
16.2x
19.9x
Notes: Self-note (copy from arxiv version): For the performance-optimized system, we calculate the cost of 1TB
DRAM to be roughly 7080 USD (8 x 128GB modules [230]) and the cost of
SSD-P to be roughly 875 USD. For the performance-optimized system, we calculate
the cost of 64GB DRAM to be roughly 312 USD (8 x 8GB modules [231],
assuming the same number of memory channels as the performance-optimized
system) and the cost of SSD-C to be roughly 346 USD. Note that the cost of
the total storage system depends not only on the price of each SSD but also on
the available interconnection slots in the systems, as systems typically have
fewer PCIe slots (needed for SSD-P) than SATA slots (needed for SSD-C).

## Slide 200: System Cost-Efficiency
GMean Speedup
Chart: 
| Perf-Opt ($) | Acc-Opt ($) | Perf-Opt($$$) | Acc-Opt ($$$) | MegIS ($)
 | 1 | 0.81324 | 6.8304 | 2.2454 | 16.1756
Cost-optimized system ($): With SSD-C and 64-GB DRAM
Performance-optimized system ($$$): With SSD-P and 1-TB DRAM
MegIS outperforms the baselines
even when running on a much less costly system
($)
($)
($$$)
($$$)
($)
7.2x
2.4x
16.2x
19.9x
MegIS improves system cost-efficiency
and makes accurate metagenomics more accessible
for wider adoption
Notes: Self-note (copy from arxiv version): For the performance-optimized system, we calculate the cost of 1TB
DRAM to be roughly 7080 USD (8 x 128GB modules [230]) and the cost of
SSD-P to be roughly 875 USD. For the performance-optimized system, we calculate
the cost of 64GB DRAM to be roughly 312 USD (8 x 8GB modules [231],
assuming the same number of memory channels as the performance-optimized
system) and the cost of SSD-C to be roughly 346 USD. Note that the cost of
the total storage system depends not only on the price of each SSD but also on
the available interconnection slots in the systems, as systems typically have
fewer PCIe slots (needed for SSD-P) than SATA slots (needed for SSD-C).

## Slide 201: More in the Paper
MegIS’s performance when running in-storage processing operations on the cores existing in the SSD controller
MegIS’s performance when using the same accelerators outside SSD
Sensitivity analysis with varying
  Database sizes
  Memory capacities
  #SSDs
  #Channels
  #Samples
MegIS’s performance for abundance estimation
Notes: Let me briefly talk about other results that are included in the paper before concluding this talk. These include the following:

## Slide 202: More in the Paper
MegIS’s performance with the cores in the SSD controller
MegIS’s performance outside SSD
Sensitivity analysis with varying
  Database sizes
  Memory capacities
  #SSDs
  #Channels
  #Samples
MegIS’s performance for abundance estimation
https://arxiv.org/abs/2406.19113

## Slide 203: Outline
Conclusion
Background
Motivation and Goal
MegIS
Evaluation

## Slide 204: Conclusion
Metagenomic analysis suffers from
significant storage I/O data movement overhead
The first in-storage processing system for end-to-end metagenomic analysis
Leverages and orchestrates processing inside and outside the storage system
MegIS
Improves performance
2.7×–37.2× over performance-optimized software
6.9×–100.2× over accuracy-optimized software
1.5×–5.1× over hardware-accelerated PIM baseline
Small area/power
Area: 0.04 mm2
Power: 7.658 mW
Reduces energy consumption
5.4× over performance-optimized software
15.2× over accuracy-optimized software
1.9× over hardware-accelerated PIM baseline
High accuracy
Same as accuracy-optimized
4.8× higher F1 score
over performance-optimized/PIM

## Slide 205: MegIS High-Performance, Energy-Efficient, and Low-Cost Metagenomic Analysis with In-Storage Processing
https://arxiv.org/abs/2406.19113
Notes: Hi everyone, I am Nika, and today, I will talk about
MegIS: High-Performance, Energy-Efficient, and Low-Cost Metagenomic Analysis with In-Storage Processing

## Slide 206
Backup Slides
Notes: Hi everyone, I am Nika, and today, I will talk about
MegIS: High-Performance, Energy-Efficient, and Low-Cost Metagenomic Analysis with In-Storage Processing
12 mins
1 min conclusion
3 mins results
4 mins mech
+ 2 mins motivation
+ 2 mins background

## Slide 207: Motivational Analysis
Database access patterns
Random Query
Streaming Query

## Slide 208: Overview of MegIS’s Steps

## Slide 209: More Details on Step 1

## Slide 210: K-mer Sketch Data Structures

## Slide 211: K-mer Sketch Streaming Hardware Design
SSD Controller
Intersection
Curr. Register
MegIS-
Enabled
SSD
Channel#1
Channel#2
Internal
DRAM
5-mer | 5-mer ID
AAAAA | 1
AAAAC | 6
AATCC | 2
… | …
4-mer ID
-
3
…
AGTTT
⋯
Idx.
Gen
AAAAC
Next Register
AATCC
Move to
Next 4-mer
❶ Intersect 5-mers
❷ Intersect 4-mers
6
2
Curr. Register
AAAA
Next Register
AATC
-
3
AATC
Intersect
Intersect
❸ Send Tax IDs

## Slide 212: Index Generation in Step 3

## Slide 213: MegIS FTL

## Slide 214: Multi-Sample Analysis

## Slide 215: SSD Configurations

## Slide 216: Impact of Different Optimizations

## Slide 217: Impact of Different Optimizations

## Slide 218: Speedup with Different Database Sizes

## Slide 219: Speedup with Different #SSDs

## Slide 220: Speedup with Different Main Memory Capacities

## Slide 221: Speedup with Varying SSD Internal Bandwidth

## Slide 222: Speedup of Abundance Estimation

## Slide 223: Multi-Sample Use Case

## Slide 224: Area and Power
Based on synthesis of MegIS accelerators using the Synopsys Design Compiler @ 65nm technology node
Only 1.7% of the area of three 28-nm ARM Cortex R4 cores
in a SATA SSD controller
Logic Unit | # of instances | Area [mm2] | Power [mW]
Intersect (120-bit) | 1 per channel | 0.001361 | 0.284
k-mer Registers (2 x 120-bit) | 1 per channel | 0.002821 | 0.645
Index Generator (64-bit) | 1 per channel | 0.000272 | 0.025
Control Unit | 1 per SSD | 0.000188 | 0.026
Total for an 8-channel SSD | - | 0.04 | 7.658
Notes: We find area and power values of MegIS by synthesizing MegIS using 65nm technology node,
And find that for an 8-channel SSD, the area of GS is 0.04 mm square and the power is 7.6 watts
BY scaling the area to lower technology nodes, we observe that the area overhead of MegIS is only 1.7% of the of the three ARM processors in a SATA SSD controller.

## Slide 225: GRAINS Enabling High-Performance and Low-Cost Graph-Based Genome Analysis via Storage-Aware Algorithm-Architecture Co-Design
Nika Mansouri Ghiasi
Mohammad Sadrosadati Jisung Park Onur Mutlu
Harun Mustafa Talu Güloglu Rakesh Nadig Konstantina Koliogeorgi
Susana Rebolledo Ruiz Marc Rautmann Furkan Eris
Notes: Hi everyone, I am Nika, and today, I will talk about
MegIS: High-Performance, Energy-Efficient, and Low-Cost Metagenomic Analysis with In-Storage Processing

## Slide 226: GRAINS Discussion
Main presentation
Unique characteristics of genome graphs
De Bruijn Graphs
Graph-based genome analysis
SSD Configurations
Detailed results

## Slide 227: Large-Scale Genome Graphs
More powerful and efficient representations of genomic data
✓
Input Sequences
TATGACGAG
ATGA
TATG
TATGCCGAG
ATGC
TATG
TATGGCGAG
ATGG
TATG
…
…
…
TATGTCGAG
ATGT
TATG
…
TATG
ATGACGA
ATGCCGA
ATGGCGA
ATGTCGA
CGAG
Graph Representation
More compact representations of massive, population-scale databases
Greater expressive power
✓

## Slide 228: Unique Characteristics of Genome Graphs
Different Node and Edge Encodings
  Traditional graphs must explicitly store O(N) to O(N²) edges
  DBGs store only nodes or edges and the other is derived implicitly
  Enabled by the inherent overlap structure of encoded sequences
Different Structural Characteristics
  In/out-degrees capped at 4 (A, C, G, T), regardless of graph size
  Power-law hub optimizations from conventional graphs are inapplicable
  Necessitates fundamentally different optimization approaches
Different Access Pattern Optimizations
  Compressed data structures enforce node orderings  no reordering possible
  Structural coupling between queries and graph enables unique locality optimizations
  Query reads sharing k-mer substrings map to nearby index regions

## Slide 229: Motivation
Case study of the performance of genome graph analysis tools
With various state-of-the-art SSD configurations and data sizes
Chart: 
| 100K | 1M | 10M
SSD-G4 | 0.013012 | 0.057486 | 0.28671
SSD-G5 | 0.025689 | 0.10872 | 0.44565
No-I/O | 1 | 1 | 1
Chart: 
| 100K | 1M | 10M
SSD-G4 | 0.040448 | 0.13429 | 0.43735
SSD-G5 | 0.077752 | 0.23679 | 0.60855
No-I/O | 1 | 1 | 1
#Query Reads
#Query Reads
Normalized Throughput
(i)
(ii)
Chart: 
| MetaSUB (659 GB)
SSD-G4 | 0.23154 | 0.057486
SSD-G5 | 0.37602 | 0.10872
No-I/O | 1 | 1
Chart: 
| SRArep (231 GB) | MetaSUB (822 GB)
SSD-G4 | 0.13249 | 0.057486
SSD-G5 | 0.23398 | 0.10872
Ideal | 1 | 1
SRArep (161 GB) MetaSUB (659 GB)
SRArep (161 GB) MetaSUB (659 GB)
Graph Database
Graph Database
Normalized Throughput
(i)
(ii)
I/O data movement causes significant performance overhead

## Slide 230: Goal
Improve the performance and energy-efficiency of
graph-based genome analysis
by alleviating its data movement overheads from storage
in a cost-effective manner.

## Slide 231: GRAINS
The first system for analysis with large-scale genome graphs in storage
Enabled via storage-aware algorithm architecture co-design to
  Make the pipelines more storage-friendly
  Further improve performance, energy-efficiency, and cost-effectiveness via in-storage (ISP) and in-flash (IFP) processing
Notes: GRAINS’s design is versatile and flexible as it supports key operations on genome graphs and can be integrated in various analysis pipelines.

## Slide 232: GRAINS Hardware-Software Co-Design
A new batching technique and execution flow, that reduces #random accesses
ISP and IFP to avoid transferring low-reuse/unused pages and bandwidth waste
An effective, yet lightweight, scheduling technique, enabled by repurposing the existing SSD structures in a new way
to enable leveraging the full parallelism of all flash dies during IFP

## Slide 233: Overview of Graph Structure and K-Mer Queries
g = ACATCCTGAAAATTGA
Minimizer
Sizes
Offsets
ACGTAGCTGACTATCCTGAAGTTCGATCGATGCTAGCTTCTT.GATAGCTGCGTAGTAGCTAGTCGATTTTCGAAGCTAGTCGTTGC.TAGTCGAGCCATCAGTCGACTGCCGAT.CGTAGCGACATCCTGAAAATTGACTAGTCTAGTTCGTTTAGGCCAATGCTAGCTAGTC.GATCGTAGGACTGCTA…
Strings
42 86 113 145…
Uniting End Points in Strings
29 | 172 | 20 | 50 | 329 | 0 | 246 | 9 | 118 | 364 | 105 | 30 | 319 | …
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | …
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | …
0 | 1 | 2 | 3 | 5 | 7 | 9 | 10 | 11 | 12 | 13 | 15 | 16 | …
Hash

## Slide 234: Overview of Graph Color Encoding
Strings
ACGTAGCTGACTATCCTGAAGTTCGATCGATGCTAGCTTCTT.GATAGCTGCGTAGTAGCTAGTCGATTTTCGAAGCTAGTCGTTGC.TAGTCGAGCCATCAGTCGACTGCCGAT.CGTAGCGACATCCTGAAAATTGACTAGTCTAGTTCGTTTAGGCCAATGCTAGCTAGTC.GATCGTAGGACTGC.…
0
0
1
0
1
…
Graph Metadata for Unitigs with Color C1
Graph Metadata for Unitigs with Color C2
…
Color Bitmap
C1
C2
C3

## Slide 235: Step 1: Query Processing
Performed in the host system to avoid excessive writes to NAND flash dies during k-mer extraction
Leverages the key property of the underlying data structures: The small Sizes
ACTAGTCGT…
Read:
ACTAG
…
K-mers:
❶ K-mer Extraction
Hash
❷ Sizes Lookup
Batch#1
…
❸ Batching
0..m-1
Sizes
ACTAG
0
TTACT
1
CTAGT
0
Batch#2
…
m..2m-1
TAAAG
2m-8
AAAGC
CTCTA
…
2m-8
2m-3
Batch#1
…
❹ Sorting and Compaction
0..m-1
CTAG
0
TTACT
1
Batch#2
…
m..2m-1
CTCTA
2m-3
…
A-
-T
AAAG
2m-8
T-
-C
CTAGT

## Slide 236: Step 2.1: Accessing Graph Offsets
Performed in the storage system to avoid the data movement overhead of a large amount of low re-use data

## Slide 237: Step 2.2: Access Graph Strings
Performed in the storage system to avoid the data movement overhead of a large amount of low re-use data
Lightweight in-storage scheduler to enable full die-level parallelism
  Small L2P data mapping  Leverage internal DRAM to store per-die scheduling table
  Ensures all requests to different dies and planes can be issues concurrently

## Slide 238: Step 2.3: Accessing Graph Colors
Performed in the storage system to avoid the data movement overhead of a large amount of low re-use data
Streams through color bitmaps sequentially
Sends the colors to the host system in a pipelined manner

## Slide 239: Performance
Chart: 
| QL | QM | QS | GMean
FG | 1 | 1 | 1 | 1
MG | 0.62278 | 0.73413 | 0.77147 | 0.70655
GRN-Ext | 1.3523 | 3.0465 | 9.9586 | 3.449
GRN | 4.061 | 8.5634 | 17.2404 | 8.4322
Chart: 
| QL | QM | QS | GMean
FG | 1 | 1 | 1 | 1
MG | 0.55421 | 0.68284 | 0.74414 | 0.65546
GRN-Ext | 1.4712 | 2.9918 | 8.8301 | 3.3873
GRN | 2.7391 | 5.196 | 11.9805 | 5.5452
17.2
22.3
Speedup
12.0
16.1
SSD-G4
SSD-G5
Performance of k-mer set lookups
Across different tools and storage configurations
On systems with SSD-G4 (SSD-G5) GRN outperforms FG and MG by 8.4× (8.5×) and 11.9× (8.5×), on average across all inputs, respectively
GRN provides 2× larger average speedup over GRN-Ext

## Slide 240: Comparison to PIM
Chart: 
| QL | QM | QS | GMean
PIM | 1 | 1 | 1 | 1
GRN | 2.8967 | 8.0711 | 17.0161 | 7.3547
Chart: 
| QL | QM | QS | GMean
PIM | 1 | 1 | 1 | 1
GRN | 1.5184 | 4.6311 | 11.6728 | 4.3459
SSD-G4
17.0
11.6
Speedup
SSD-G5
Performance of k-mer set lookups
Compared to an idealized PIM system without memory overheads for graph lookups
on the system with SSD-G4 (SSD-G5), GRN provides 7.4× (4.3×) average speedup over PIM

## Slide 241: Performance of Alignment-Based Mapping
GRAINS integrated with a state-of-the-art sequence-to-graph alignment accelerator, SeGraM
GRAINS finds the relevant parts of the graph and passes them to SeGraM to go through alignment
Chart: 
| QL | QM | QS | GMean
FG+SeGraM | 1 | 1 | 1 | 1
MG+SeGraM | 0.64145 | 0.73588 | 0.77164 | 0.71416
GRN+SeGraM | 3.2849 | 8.0216 | 16.9804 | 7.6485
Chart: 
| QL | QM | QS | GMean
FG+SeGraM | 1 | 1 | 1 | 1
MG+SeGraM | 0.58417 | 0.68648 | 0.74449 | 0.66836
GRN+SeGraM | 2.2824 | 4.8547 | 11.7408 | 5.067
SSD-G4
Speedup
SSD-G5
SeGraM+GRN provides 6.2× and 9.0× average speedup over SeGraM+FG and SeGraM+MG

## Slide 242: Area and Power
Based on Synthesis of GRAINS’s hardware units using the Synopsys Design Compiler @ 22nm technology node
ECCLITE area based on the original paper [AiF, ISCA’25]
On-controller logic units are 0.7% of the four cores on an SSD controller On-die logic area is mainly (99%) for ECCLITE, which takes only 0.2% of the flash chip’s area and fits well within its power budget
Notes: On-controller units are 0.0025mm2 (0.7%of thefourARMcores [228]onanSSD controller).GRAINS’son-die logicarea ismainly(99%) for ECCLITE,which,asreportedby[116], takesonly0.2%of the flashchip’sareaandfitswellwithinitspowerbudget.

## Slide 243: GRAINS Enabling High-Performance and Low-Cost Graph-Based Genome Analysis via Storage-Aware Algorithm-Architecture Co-Design
Nika Mansouri Ghiasi
Mohammad Sadrosadati Jisung Park Onur Mutlu
Harun Mustafa Talu Güloglu Rakesh Nadig Konstantina Koliogeorgi
Susana Rebolledo Ruiz Marc Rautmann Furkan Eris
Notes: Hi everyone, I am Nika, and today, I will talk about
MegIS: High-Performance, Energy-Efficient, and Low-Cost Metagenomic Analysis with In-Storage Processing

## Slide 244: Backup Slides

## Slide 245: De Bruijn Graphs
Input
Sequences
(48 k-mers)
GTGG
TGGA
TATG
GTGGATTATGACGAGGCTA
ATGA
TGAC
GACG
ACGA
CGAG
…
…
GTGG
TGGA
TATG
GTGGATTATGTCGAGGCTA
ATGT
TGTC
GTCG
TCGA
CGAG
…
…
Compacted de Bruijn Graph
(5 nodes)
GTGGATTATG
ATGACGA
ATGCCGA
ATGTCGA
CGAGGCTA
De Bruijn Graph
(24 nodes)
TATG
ATGA
TGAC
GACG
ACGA
ATGC
TGCC
GCCG
CCGA
ATGT
TGTC
GTCG
TCGA
CGAG
GTGG
…
GCTA
…
GTGG
TGGA
GTGGATTATGCCGAGGCTA
TATG
…
…
ATGC
TGCC
GCCG
CCGA
CGAG
k - 1 overlap

## Slide 246: Graph-Based Genome Analysis

## Slide 247: SSD Configurations

## Slide 248: Execution Time Breakdown

## Slide 249: Ablation Analysis

## Slide 250: Speedup with Different #SSDs

## Slide 251
A Lightweight Algorithm-Architecture Co-Design for Mitigating the Data Preparation Bottleneck in Large-Scale Genome Sequence Analysis
Nika Mansouri Ghiasi
Mohammad Sadrosadati Jisung Park Onur Mutlu
Talu Güloglu Harun Mustafa Can Firtina Konstantina Koliogeorgi
Konstantinos Kanellopoulos Haiyu Mao Rakesh Nadig

## Slide 252: Applications of Genome Sequence Analysis
Precision Medicine
Outbreak Prevention and Management
Agriculture
Scientific Discovery
& Many More…
Notes: 0:30

## Slide 253: DNA Under Electron Microscope
human chromosome #12
from a HeLa cell

## Slide 254: Digital Format for Analysis
CCTCCTCAGTGCCACCCAGCCCACTGGCAGCTCCCAAACAGGCTCTTATTAAAACACCCTGTTCCCTGCCCCTTGGAGTGAGGTGTCAAGGACCTAAACTAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTGCTAAACAGCACTTTTTTGACCATTATTTTGGATCTGAAAGAAATCAAGAATAAATGAAGGACTTGATACATTGGAAGAGGAGAGTCAAGGACCTACAGAAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTATGTCAAGGACCTAATGTCTGTGTTGCAGGTCTTCTTGCATCTTCCCTGTC

## Slide 255: High-Throughput Sequencers
… and more! All produce data with different properties.
Illumina MiSeq
Pacific Biosciences RS II
Illumina NovaSeq 6000
Oxford
Nanopore GridION
Pacific
Biosciences
Sequel II
Oxford
Nanopore
PromethION
Oxford Nanopore MinION

## Slide 256: High-Throughput Sequencers
… and more! All produce data with different properties.
Illumina MiSeq
Oxford Nanopore MinION
Pacific Biosciences RS II
Illumina NovaSeq 6000
Oxford
Nanopore SmidgION
Pacific
Biosciences
Sequel II
Oxford
Nanopore
PromethION
Current sequencing technologies
cannot sequence very long DNA molecules end-to-end
Instead, they extract smaller fragments of the original DNA sequence, known as reads
AAGCTTCCATGG
AAATGGGCTTTC
GCCCAAATGGTT
GCTTCCAGAATG
Notes: 1:10

## Slide 257: Genomic Data is Growing at a Fast Pace
Important Role in Many Fields
Significant Drop in Sequencing Cost
Fast growth in genomic data size
Chart: Year
Public Genomic Sequence Reads Data Size in Sequence Read Archive (SRA) Over Years
260.3x

## Slide 258: Large Efforts in Handling Fast-Growing Genomic Data
Store Genome Sequence Data in Highly-Compressed Formats
Accelerate Genome Sequence Analysis

## Slide 259: Data Preparation Bottleneck
Store Genome Sequence Data in Highly-Compressed Formats
Accelerate Genome Sequence Analysis
Genomic data is decompressed and formatted first before an accelerator can operate on it
Notes: 1:24

## Slide 260: Effect of the Data Preparation Bottleneck
Prep
Analysis
Analysis
Analysis
Base.
Acc. Analysis
w/ Ideal Prep.
Prep
Prep
Lost Benefit due to Data Prep. Bottleneck
Execution Timeline (Not drawn to scale)
Acc. Analysis
Potential Benefit of Genome Analysis Acceleration
Baseline Analysis (446 KRead/s)
Accelerated Analysis (69200 KRead/s)
Baseline Prep. (2563 KRead/s)
Ideal Prep. (> 69200 KRead/s)
Notes: 2:10

## Slide 261: Mitigating Data Preparation Bottleneck
We need to effectively mitigate the data preparation bottleneck while meeting four key requirements:
Meeting all these requirements is challenging
High performance
High compression ratio
Low overhead
High energy efficiency
Even more challenging in genome analysis systems used
in hardware resource-constrained environments
Notes: 2:50

## Slide 262: .
An algorithm-architecture co-design for highly-compressed storage and high-performance access of large-scale genomic sequence data
Key insight: information encoded in genomic data follows specific properties
We leverage these properties to co-design
  A lossless (de)compression algorithm
  Hardware for decompression with lightweight operations
  Storage data layout & Interface commands to access data
Higher performance (by 3.0×–32.1×)
High compression ratio
Low overhead
Higher energy efficiency (by 13.0×–34.0x)
Notes: 3:30

## Slide 263: Outline
Background
Motivation and Goal
SAGe
Evaluation
Conclusion

## Slide 264: Genomics-Specific Compression
Consensus
Sequence
ATACGTAGAAAAAGT
AGCAAATGTACGATG
TCGATGCTTGCATAA
CATAAGTCGATAGTT
ATACGTAGAAAAAGTCGATGCTTGCATAAGTCGATAGTT…
Read Set (A set of reads from a sample)
AAAAAGTCGATGCTT
…
Mismatch
Information
Notes: A genomic-specific compressor instead of storing reads, first stores a consensus sequence, which is
an approximation of the organism’s genome and stores the mismatch information of those reads in relation to the consensus

## Slide 265: Genomics-Specific Compression
Consensus
Sequence
ATACGTAGAAAAAGT
TCGATGCTTGCATAA
CATAAGTCGATAGTT
ATACGTAGAAAAAGTCGATGCTTGCATAAGTCGATAGTT…
Read Set (A set of reads from a sample)
AAAAAGTCGATGCTT
…
AGCAAATGTACGATG
Mismatch
Information
Notes: and, To do so, it first needs to map reads to the location they match in the consensus sequence.

## Slide 266: Genomics-Specific Compression
Consensus
Sequence
ATACGTAGAAAAAGT
AGCAAATGTACGATG
TCGATGCTTGCATAA
CATAAGTCGATAGTT
ATACGTAGAAAAAGTCGATGCTTGCATAAGTCGATAGTT…
Read Set (A set of reads from a sample)
AAAAAGTCGATGCTT
…
Mismatch
Information
Compressed with General-Purpose Compression Techniques
Matching Pos.
Mismatch Pos.
Mismatch Char.
Mismatch Type
Read N
7
+2, +4, +3
C, T, A
Subs, Subs, Ins
…
…
…
…
…
…
…
…
…
…
Notes: Now, let me give more details about the mismatch information using the example of this read ... Since these compressors use a consensus sequence, they better capture the inherent redundancy present in genomic data

## Slide 267: Genomics-Specific Compression
Consensus
Sequence
ATACGTAGAAAAAGT
AGCAAATGTACGATG
TCGATGCTTGCATAA
CATAAGTCGATAGTT
ATACGTAGAAAAAGTCGATGCTTGCATAAGTCGATAGTT…
Read Set (A set of reads from a sample)
AAAAAGTCGATGCTT
…
Mismatch
Information
Compressed with Back-End General-Purpose Compressors
Matching Pos.
Mismatch Pos.
Mismatch Base
Mismatch Type
Read N
7
+2, +3, +2
C, T, A
Sub, Sub, Ins
…
…
…
…
…
…
…
…
…
…
Genomics-specific compressors attain higher compression ratio (e.g., typically from ∼2 to ∼40) than general-purpose compressors (e.g., typically from ∼2 to ∼6)
Notes: 5

## Slide 268: Outline
Motivation and Goal
Background
SAGe
Evaluation
Conclusion

## Slide 269: Effect of the Data Preparation Bottleneck
Prep
Analysis
Analysis
Analysis
Base.
Acc. Analysis
w/ Ideal Prep.
Prep
Prep
Lost Benefit due to Data Prep. Bottleneck
Execution Timeline (Not drawn to scale)
Acc. Analysis
Potential Benefit of Genome Analysis Acceleration
Baseline Analysis (446 KRead/s)
Accelerated Analysis (69200 KRead/s)
Baseline Prep. (2563 KRead/s)
Ideal Prep. (> 69200 KRead/s)

## Slide 270: Data Preparation Bottleneck
End-to-end performance of a genome analysis application, which includes both data preparation and genome analysis
  Genome Analysis: GEM [Chen+, IEEE TPDS’23], a state-of-the-art hardware accelerator for read mapping (a fundamental task in genome analysis)
Chart: 
| RS1 | RS2 | RS3 | RS4 | RS5 | GMean
General-Purpose | 0.3207 | 0.22018 | 0.52661 | 0.42172 | 0.22321 | 0.32271
Genomics-Specific | 1 | 1 | 1 | 1 | 1 | 1
Ideal | 4.8537 | 2.2779 | 28.5302 | 2.0725 | 1.5084 | 3.9699
Normalized Throughput
28.5x
Data preparation greatly limits end-to-end performance
Read Set
Notes: 6min

## Slide 271: Challenges
Mitigating the data preparation bottleneck is challenging when aiming to achieve high performance, energy efficiency, high compression ratio, & low overhead
This is because prior approaches rely on
    Expensive computational units
    Large buffers, or large DRAM bandwidth or capacity
This challenge is exacerbated in genome analysis systems used in hardware resource-constrained environments
Portable Systems
Near-Data Processing Systems (e.g., in Main Memory or Storage System)
Notes: Which are needed due to many random accesses to large data structures for matching patterns

## Slide 272: Our Goal
Effectively mitigate the data preparation bottleneck, while meeting four key requirements:
High performance
Energy efficiency
High compression ratio
Low overhead
Notes: 6:45

## Slide 273: Outline
SAGe
Background
Motivation and Gaol
Evaluation
Conclusion

## Slide 274: .
Genome Analysis
System
Request Data with SAGe’s Interface Commands
Send Prepared Data
in Desired Format
Receive Compressed Data
SAGe-Compressed Genomic Data
Operate w/ SAGe
Data Layout
Decompress & Reformat
SAGe HW
An algorithm-architecture co-design for highly-compressed storage and high-performance access of large-scale genomic sequence data
Key insight: information encoded in genomic data follows specific properties We leverage these properties in our algorithm-architecture co-design

## Slide 275: SAGe’s Algorithm Architecture Co-Design
Genome Analysis
System
Request Data with SAGe’s Interface Commands
Send Prepared Data
in Desired Format
Receive Compressed Data
SAGe-Compressed Genomic Data
Operate w/ SAGe
Data Layout
Decompress & Reformat
SAGe HW
Notes: 7:30

## Slide 276: SAGe’s Algorithm Architecture Co-Design
Genome Analysis
System
Request Data with SAGe’s Interface Commands
Send Prepared Data
in Desired Format
Receive Compressed Data
SAGe-Compressed Genomic Data
Operate w/ SAGe
Data Layout
Decompress & Reformat
SAGe HW

## Slide 277: Compression Algorithm and Data Structures
Consensus
Sequence
ATACGTAGAAAAAGTCGATGCTTGCATAAGTCGATAGTT…
Mismatch
Information
Mismatch Pos.
Read 1
1, 0, 9
…
…
Read 2
Matching Pos.
7
…
10
1, 1, 0
Mismatch Base
C, T, A
…
A, T, T
Mismatch Type
Subs, Subs, Ins
…
Ins, Subs, Ins

## Slide 278: Compression Algorithm and Data Structures
Consensus
Sequence
ATACGTAGAAAAAGTCGATGCTTGCATAAGTCGATAGTT…
Sequentially Encode Mismatch Information in Lightweight Structures
Tune the Bit Counts Based on Read Set Properties
1 | 0 | 1001 | 1 | 1 | 0 | …
0 | 0 | 1 | 0 | 0 | 0 | …
Mismatch Pos. Array
Mismatch Pos. Guide Array
⓶
⓵
Mismatch
Information
Mismatch Pos.
Read 1
1, 0, 9
…
…
Read 2
Matching Pos.
7
…
10
1, 1, 0
Mismatch Base
C, T, A
…
A, T, T
Mismatch Type
Subs, Subs, Ins
…
Ins, Subs, Ins
0001 | 0000 | 1001 | 0001 | 0001 | 0000 | …
1 0 9
1 1 0
Indicates 1 bit
Indicates 4 bits
Notes: 8:30

## Slide 279: Compression Algorithm and Data Structures
Consensus
Sequence
ATACGTAGAAAAAGTCGATGCTTGCATAAGTCGATAGTT…
Sequentially Encode Mismatch Information in Lightweight Structures
Tune the Bit Counts Based on Read Set Properties
1 | 0 | 1001 | 1 | 1 | 0 | …
0 | 0 | 1 | 0 | 0 | 0 | …
Mismatch Pos. Array
Mismatch Pos. Guide Array
⓶
⓵
Mismatch
Information
Mismatch Pos.
Read 1
1, 0, 9
…
…
Read 2
Matching Pos.
7
…
10
1, 1, 0
Mismatch Base
C, T, A
…
A, T, T
Mismatch Type
Subs, Subs, Ins
…
Ins, Subs, Ins
0001 | 0000 | 1001 | 0001 | 0001 | 0000 | …
1 0 9
1 1 0
Indicates 1 bit
Indicates 4 bits
This is effective since the mismatch information in genomic datasets tends to follow specific properties
and by using a limited set of bit widths tailored to these properties, SAGe significantly reduces data size

## Slide 280: Example Properties of Mismatch Information
Chart: 
 | 23.9014 | 16.7779 | 11.6254 | 7.1821 | 7.3742 | 8.391 | 8.6975 | 7.778 | 5.413 | 2.3223 | 0.49269 | 0.043227 | 0.0011892 | 0 | 0
% of Mismatch
Positions
Needed #Bits
Most mismatch positions
need only a few bits to store
Based on the information encoded in histograms of each read set,
SAGe systematically searches for the best bit-counts for arrays and guide arrays
that minimize the total encoded size for that specific read set
Notes: This is due to two main factors that can lead to spatially nearby mismatches.
First, genetic mutations tend to cluster in some regions of the genome [291–293].
Second, a regional degradation in sequencing quality can cause clusters of incorrect bases in the read [294–296].

## Slide 281: Example Properties of Mismatch Information
Chart: 
 | 23.9014 | 16.7779 | 11.6254 | 7.1821 | 7.3742 | 8.391 | 8.6975 | 7.778 | 5.413 | 2.3223 | 0.49269 | 0.043227 | 0.0011892 | 0 | 0
% of Mismatch
Positions
Most delta-encoded mismatch positions
need only a few bits to store
Observations regarding properties of other parts of the mismatch information are in the paper
Based on the information encoded in histograms of each read set,
SAGe systematically searches for the best bit-counts for arrays and guide arrays
that minimize the total encoded size for that specific read set
Notes: 10:15 9:30

## Slide 282: Example Walkthrough of Decompression
111010101100101010…
Mismatch Pos. Array
00111011000110…
Mismatch Pos. Guide Array
Encoding of Guide Array Entry | #Bits for Array Entry
0 | 2
10 | 4
110 | 8
Association Table
Read#1 Mismatch Count (Fixed width)

## Slide 283: Example Walkthrough of Decompression
111010101100101010…
Mismatch Pos. Array
00111011000110…
Mismatch Pos. Guide Array
Encoding of Guide Array Entry | #Bits for Array Entry
0 | 2
10 | 4
110 | 8
Association Table
Read#1 Mismatch Count (Fixed width)
10
4
110
8
0
2
Read#2 Mismatch Count (Fixed width)
Sequential Scan
Notes: 11

## Slide 284: SAGe’s Algorithm Architecture Co-Design
Genome Analysis
System
Request Data with SAGe’s Interface Commands
Send Prepared Data
in Desired Format
Receive Compressed Data
SAGe-Compressed Genomic Data
Operate w/ SAGe
Data Layout
Decompress & Reformat
SAGe HW

## Slide 285: Hardware for Data Preparation
Decompressed
and Formatted Reads
Genome Analysis System
Scan Unit (SU)
Read Construction Unit (RCU)
Control Unit (CU)
Config. Registers
Position Arrays
Position Guide Arrays
Array Config. Parameters
Array Registers
Scan Logic
Consensus Sequence
Construction
Logic
Consensus
Sequence Register
Guide Array Registers

## Slide 286: Hardware for Data Preparation
Decompressed
and Formatted Reads
Genome Analysis System
Scan Unit (SU)
Read Construction Unit (RCU)
Control Unit (CU)
Config. Registers
Position Arrays
Position Guide Arrays
Array Config. Parameters
Array Registers
Scan Logic
Consensus Sequence
Construction
Logic
Consensus
Sequence Register
Guide Array Registers
SAGe’s hardware units decompress and reformat data into the desired format using lightweight operations and streaming accesses
Notes: 12:30

## Slide 287: Case Studies of SAGe’s Hardware Integration
Due to its lightweight design, SAGe can seamlessly integrate with genome analysis systems
Genome Analysis ACC
SAGe HW
SSD
Genome Analysis ACC
SSD
Host System
SAGe HW
Host System
SSD
Host System
Genome Analysis ACC
SAGe HW
Notes: 14

## Slide 288: SAGe’s Algorithm Architecture Co-Design
Genome Analysis
System
Request Data with SAGe’s Interface Commands
Send Prepared Data
in Desired Format
Receive Compressed Data
SAGe-Compressed Genomic Data
Operate w/ SAGe
Data Layout
Decompress & Reformat
SAGe HW
Details in the paper

## Slide 289: More in the Paper
https://arxiv.org/abs/2504.03732

## Slide 290: Outline
Evaluation
Background
Motivation and Gaol
SAGe
Conclusion

## Slide 291: Evaluation Methodology Overview (I)
Performance, Energy, and Power Analysis
Datasets: Read sets (RS)
From a variety of species (i.e., H. sapiens, T. cacao, M. acuminata malaccensis)
Sequenced with different sequencing technologies (i.e., Illumina and Oxford Nanopore Technologies)
End-to-end performance of a genome analysis application, which includes both data preparation and genome analysis
Hardware Components
Synthesized Verilog model for the hardware units
MQSim [Tavakkol+, FAST’18] for SSD’s internal operations
Ramulator [Kim+, CAL’15] for SSD’s internal DRAM
Software Components
Measure on a real system:
AMD® EPYC® CPU with 128 physical cores
1 TB DRAM
Notes: We model performance, energy, and power of the systems based on the latency and throughput of each hardware-based and software-based component

## Slide 292: Recall: Case Studies of SAGe’s Hardware Integration
Due to its lightweight design, SAGe can seamlessly integrate with genome analysis systems
Genome Analysis ACC
SAGe HW
SSD
Genome Analysis ACC
SSD
Host System
SAGe HW
Host System
SSD
Host System
Genome Analysis ACC
SAGe HW
Notes: 14

## Slide 293: Evaluation Methodology Overview (II)
Genome Analysis
A state-of-the-art hardware accelerator (GEM [Chen+, TPDS’23]), for read mapping
A state-of-the-art NDP accelerator (GenStore [Mansouri Ghiasi+, ASPLOS’22])
  Filters reads that do not require expensive computation in the SSD  Alleviates the burden of moving and analyzing a large amount of low-reuse data from the rest of the system
  Implemented in the resource-constrained environment of the SSD
SSD Controller
SSD’s
Internal
DRAM
⋯
Flash Cntrl.
Channel#N-1
Genome Analysis ACC
SSD
Flash Cntrl.
Channel#0
Genome Analysis ACC

## Slide 294: Evaluation Methodology Overview (II)
Data Preparation
pigz: Commonly-used general-purpose software ([Adler, JPL’15])
(N)Spr: Genomics-specific software for short (Spring [Chandak, Bioinformatics’18]) and long reads (NanoSpring [Meng+, Scientific Reports’23])
(N)SprAcc: (N)Spring hardware-accelerated
0TimeDec: an idealized decompressor (with zero decompression time), but inefficient for integration in resource-constrained environments
SAGe: SAGe implemented as an standalone accelerator for data preparation
SAGeSSD: SAGe inside the SSD, for integration with the NDP analysis system
SSD Controller
SSD’s
Internal
DRAM
SAGe FTL
Metadata
⋯
Flash Cntrl.
Channel#N-1
Genome Analysis ACC
SAGe HW
Double-Reg.
SSD
Flash Cntrl.
Channel#0
Genome Analysis ACC
SAGe HW
Double-Reg.
Notes: 14:30

## Slide 295: Speedup
Chart: 
| RS1 | RS2 | RS3 | RS4 | RS5 | GMean
pigz | 0.3207 | 0.22018 | 0.52661 | 0.42172 | 0.22321 | 0.32271
(N)Spr | 1 | 1 | 1 | 1 | 1 | 1
(N)SprAcc | 1.5353 | 1.2884 | 1.7302 | 1.086 | 1.0869 | 1.3221
SAGe | 4.8537 | 2.2779 | 28.5302 | 2.0725 | 1.5084 | 3.9699
0TimeDec | 4.8537 | 2.2779 | 28.5302 | 2.0725 | 1.5084 | 3.9699
SAGeSSD+NDP | 7.1782 | 10.3865 | 51.9319 | 2.0725 | 14.9719 | 10.3738
28.5
51.9
28.5
Speedup
15.0
3.9x
3.0x
12.3x
2.6x
SAGe provides significant speedup over both
general-purpose and genomics-specific baselines
SAGe achieves the same speedup as 0TimeDec
By efficiently integrating SAGeSSD with NDP SAGeSSD+NDP leads to large speedups
SAGeSSD+NDP
Notes: 15:30

## Slide 296: Reduction in Energy Consumption
  Normalized to (N)SprAcc (higher is better)
Chart: 
| RS1 | RS2 | RS3 | RS4 | RS5 | GMean
pigz | 0.25285 | 0.23041 | 0.38335 | 0.80657 | 0.45126 | 0.38195
(N)Spr | 0.67476 | 0.8028 | 0.57937 | 0.92535 | 0.92733 | 0.76922
SG | 9.3415 | 6.2919 | 45.2882 | 13.8158 | 10.0488 | 12.9878
Energy Reductuion
SAGe provides significant energy reduction over both
general-purpose and genomics-specific baselines
16.9x
34.0x

## Slide 297: Compression Ratio
Read Set | Uncompressed Size (MB) | Compression Ratio |  | 
Read Set | Uncompressed Size (MB) | pigz | (N)Spr | SAGe
RS1 | 5000 | 03.4 | 24.8 | 22.8
RS2 | 79000 | 12.5 | 40.2 | 36.8
RS3 | 4000 | 03.4 | 07.2 | 07.1
RS4 | 12000 | 03.9 | 04.8 | 04.5
RS5 | 88400 | 03.5 | 07.6 | 07.8
RS6 | 9600 | 3.27 | 18.5 | 18.9
2.9× better average compression ratio than general-purpose baseline
comparable compression ratio to genomics-specific baseline (with a modest 4.6% average reduction)

## Slide 298: Compression Ratio for Metagenomic Data
Read Set | pigz | (N)Spr | SAGe
CAMI-L | 3.53 | 21.54 | 32.53
CAMI-M | 3.59 | 17.65 | 26.20
CAMI-H | 3.54 | 7.35 | 9.53
Better average compression ratio than general-purpose baseline
Comparable compression ratio to genomics-specific baseline

## Slide 299: Area and Power
Based on Synthesis of SAGe’s hardware units using the Synopsys Design Compiler @ 22nm technology node
Logic unit | # of instances | Area [mm2] | Power [mW]
Comparator | 1 per channel | 0.000045 | 0.014
Read Construction Unit | 1 per channel | 0.000017 | 0.023
Double Registers | 1 per channel | 0.00020 | 0.035
Control Unit | 1 per channel | 0.000029 | 0.025
Total for an 8-channel SSD | - | 0.002 | 0.77
SAGe’s hardware units consume small area and power

## Slide 300: More in the Paper
Observations on different parts of mismatch information
  Matching positions
  Mismatch bases and types
  Mismatch counts
SAGe’s performance in software
Sensitivity analysis with varying the number of SSD
Impact of each of SAGe’s optimizations on compression ratio
SAGe’s performance for quality scores
SAGe’s resource requirements compared to other (de)compression accelerators
SAGe’s compression time
Notes: Let me briefly talk about other results that are included in the paper before concluding this talk. These include the following:

## Slide 301: More in the Paper
https://arxiv.org/abs/2504.03732
Notes: Let me briefly talk about other results that are included in the paper before concluding this talk. These include the following:

## Slide 302: Outline
Conclusion
Background
Motivation and Gaol
SAGe
Evaluation

## Slide 303: Conclusion
Data preparation bottleneck greatly limits end-to-end performance of genome analysis
SAGe
Improves performance
Improves the end-to-end performance of two state-of-the-art genome analysis accelerators
by 3.0×–32.1×
Low overhead
Area: 0.002 mm2
Power: 0.77 mW
Reduces energy consumption
Improves the end-to-end energy efficiency of two state-of-the-art genome analysis accelerators
by 13.0×–34.0×
High compression ratio 2.9× better than general-purpose baseline
and comparable to genomics-specific baseline (with a modest 4.6% average reduction)
An algorithm-architecture co-design for highly-compressed storage and high-performance access of large-scale genomic sequence data

## Slide 304
A Lightweight Algorithm-Architecture Co-Design for Mitigating the Data Preparation Bottleneck in Large-Scale Genome Sequence Analysis
Nika Mansouri Ghiasi
Mohammad Sadrosadati Jisung Park Onur Mutlu
Talu Güloglu Harun Mustafa Can Firtina Konstantina Koliogeorgi
Konstantinos Kanellopoulos Haiyu Mao Rakesh Nadig

## Slide 305: Backup Slides
Genomic Workflow
SAGe Compression
Properties of Mismatch Information
Tuning Arrays and Guide Arrays
Hardware Details
Data Preparation Performance
End-to-End Performance
Performance with Multiple SSDs
Compression Ratio Details
Effect of Different Optimizations
Resource Requirements
Compression Time
Summary
Background
Motivation and Goal
SAGe
Evaluation

## Slide 306: Genomic Workflow

## Slide 307: SAGe Compression High-Level Overview

## Slide 308: Properties of Mismatch Information (I)
Chart: 
| 0 | 1 | 2 | 3 | 4+
 | 78.4 | 14 | 3.3 | 1.3 | 0.9
% of Reads
#Mismatches per Read
Distribution of mismatch counts per short read

## Slide 309: Properties of Mismatch Information (II)
Cumulative distribution of (a) indel block lengths and (b) #bases in indel blocks of different lengths
Chart: 
 | 67.3471 | 85.8812 | 92.8234 | 96.1103 | 97.6941 | 98.4254 | 98.7746 | 99.0335 | 99.1639 | 99.3208
Chart: 
 | 38.199 | 59.224 | 71.0368 | 78.4941 | 82.9857 | 85.4744 | 86.8611 | 88.0355 | 88.7014 | 89.5915
Cumul. % of Indels
Cumul. % of Indel Bases
Indel Length
Indel Length
(a)
(b)

## Slide 310: Properties of Mismatch Information (III)
Distribution of #bits needed to store the delta-encoded matching position.
Chart: 
 | 34.3087 | 27.0759 | 24.6153 | 11.7102 | 2.0654 | 0.1676 | 0.040552 | 0.013403 | 0.00276 | 0.00022455 | 2.4686e-05 | 6.6079e-06 | 3.6157e-06 | 4.9871e-07 | 0
% of Matching Positions
Needed #Bits

## Slide 311: Example of a chimeric read
ACGTAGAAAAAGTAGT … CGCTTTCAGACCTAG
GTAAAAGTATGAGA
Matching Position#2
Matching Position#1
Chimeric reads: reads with sequences joined from different regions of the genome due to sequencing/library preparation errors, or structural variations
Chimeric Read

## Slide 312: Tuning Arrays and Guide Arrays

## Slide 313: Hardware for Data Preparation

## Slide 314: Data Preparation Performance
Only data preparation throughput, normalized to pigz

## Slide 315: End-to-End Performance
Speedup, with different SSDs

## Slide 316: Performance with Multiple SSDs
Chart: 
| 1× | 2× | 4× | 1× | 2× | 4× | 1× | 2× | 4× | 1× | 2× | 4× | 1× | 2× | 4× | RS1 | RS2 | RS3 | RS4 | RS5
SG | 4.835 | 4.8807 | 4.9038 | 2.2661 | 2.2795 | 2.2863 | 28.2644 | 32.5976 | 35.3038 | 2.0525 | 2.0732 | 2.0838 | 1.5078 | 1.5082 | 1.5085
SG+ISF | 7.1505 | 7.2508 | 7.3021 | 10.3328 | 10.6181 | 10.7667 | 58.6957 | 94.4623 | 121.4377 | 2.0525 | 2.0732 | 2.0838 | 15.0528 | 30.1057 | 60.2114
Speedup
#SSDs
Read Set

## Slide 317: Compression Ratio

## Slide 318: Effect of Different SAGe Optimizations
NO: no optimization on the raw mismatch information
O1: matching position optimization added to NO O2: mismatch positions and count optimizations added to O1
O3: mismatching base and type optimizations added to O2 O4: corner case optimizations added to O3

## Slide 319: Resource Requirements

## Slide 320: Compression Time
Chart: 
| pigz | (N)Spr | SAGe | pigz | (N)Spr | SAGe | pigz | (N)Spr | SAGe | pigz | (N)Spr | SAGe | pigz | (N)Spr | SAGe | RS1 | RS2 | RS3 | RS4 | RS5
Finding Mismatches | 0 | 0.92771 | 0.92771 | 0 | 0.94687 | 0.94687 | 0 | 0.93407 | 0.93407 | 0 | 0.93822 | 0.93822 | 0 | 0.97697 | 0.97697
Encoding | 0.051807 | 0.072289 | 0.012048 | 0.095825 | 0.053131 | 0.0018975 | 0.035714 | 0.065934 | 0.010989 | 0.036293 | 0.061776 | 0.011583 | 0.023659 | 0.023028 | 0.0018927
Norm. Comp. Time